## Slide 1
TAVAONE EDUCATION · PINELLAS STEM RADIO LAB
BSA Radio Merit Badge
Session 1 — Radio Foundations
Safety · Fundamentals · Propagation · Regulation · Amateur Radio (Reqs 1–6, 8-A(1–5))
TavaOne Education · Pinellas STEM Radio Lab · Gulf Coast Contest Club
Notes: Welcome Scouts. This session covers six of the nine merit badge requirements. By the end you will understand radio safety, the EM spectrum, how signals travel, FCC rules, and what amateur radio is. You will also make your first on-air voice contact today.

## Slide 2
Today's Agenda
Req 1 — Radio Safety (grounding, burns, Li-ion fires)
Req 2 — Radio Fundamentals (EM spectrum chart, definitions)
Req 3 — How Radio Waves Travel (propagation)
Req 6 — Radio Regulation (FCC/ITU, call signs, phonetic alphabet)
Req 8-A, Items 1–5 — Amateur Radio knowledge
Req 9 — Introduction to career/hobby research assignment
On-Air: Supervised voice contact at the club station
Notes: Run through the agenda so Scouts know what to expect. Let them know they will physically make an on-air contact today — this is usually the most exciting part. Session 2 covers Reqs 4, 5, 7, and the FT8 digital contact.

## Slide 3
Requirement 1
Radio Safety — Grounding, Burns & Battery Fires

## Slide 4
Req 1a — Grounding: Two Types of Circuits
DC Grounding
Batteries and solar panels produce DC
Negative terminal = ground reference
All negative leads connect to a common ground point
Prevents voltage differences and arcing between equipment
AC Grounding (Household Power)
Household outlets are 120 V AC in the US
The third (round) prong is the safety ground
Never remove the third prong or use an ungrounded adapter
Safety ground prevents the chassis from becoming energized
Notes: Grounding is one of the most important safety topics. Ask Scouts: "Why do appliances have three prongs?" Most already know the answer instinctively but may not know the technical reason.

## Slide 5
Req 1a — Antenna & Lightning Grounding
⚡ NEVER touch an antenna or feedline during a thunderstorm
Disconnect feedlines from radio BEFORE the storm arrives
Lightning arrestors divert strike energy to a ground rod — not through your radio
Antennas build up static charge even without lightning → a bleeder resistor or ground strap bleeds it off safely
Ground rod should be driven into moist earth, bonded to station ground bus
If outdoors near an antenna in a storm → move indoors immediately
Notes: This is not hypothetical — lightning injuries at antenna installations happen every year. Emphasize disconnecting and grounding before a storm, not when you hear thunder.

## Slide 6
Req 1b — Electrical Burns: Prevention & Treatment
Prevention
Always turn off and unplug before working inside equipment
Capacitors hold charge after power is off — discharge them first
One-hand rule: keep one hand in pocket when probing live circuits
Never work on electrical equipment alone
Treatment
FIRST: cut power before touching the victim
Call 911 — even if person "seems okay"
Cool running water on the burn — NOT ice
Cover loosely with sterile dressing, do not pop blisters
Internal damage is often far worse than external burns look
Notes: The one-hand rule prevents current from crossing the chest (the dangerous path near the heart). This is why electricians keep one hand behind their back.

## Slide 7
Req 1c — Lithium-Ion Battery Fire Prevention
Li-ion batteries power phones, handheld radios, tablets, laptops
THERMAL RUNAWAY: heat from one failing cell ignites adjacent cells — the fire spreads and re-ignites
Never use a charger not designed for your specific battery
Do not charge unattended overnight without a protected quality charger
Swollen (puffy) battery = failing → stop using, dispose properly
Never puncture, crush, or expose to temperatures above 140°F (60°C)
Li-ion fire: do NOT use water → use Class D extinguisher or sand, move device outdoors, call 911
Notes: Li-ion fires are dramatic and news-worthy. You can mention the hoverboard fires of 2015–16 and incidents with vape devices and e-scooters as examples Scouts likely know about. The key message: these batteries store a lot of energy and fail fast when abused.

## Slide 8
Quick Check
Your baofeng battery is puffy and the case feels warm. What do you do?
A) Charge it — the warmth means it needs more power
B) Continue using it, it's probably fine
C) Stop using it, do not charge it, dispose of it properly
D) Put it in the freezer to cool down
Answer: C — A swollen battery is failing. Stop using it immediately. Disposing properly means taking it to a battery recycling point, not the trash.
Notes: This is a real scenario Scouts may encounter. Baofengs are common in scout radio programs. Emphasize: swelling = danger, freezer = wrong.

## Slide 9
Requirement 2
Radio Fundamentals — Spectrum, Definitions & Discussion

## Slide 10
Req 2a — The Electromagnetic Spectrum (300 kHz – 3 GHz)
All radio waves are EM waves — same physics as light, just longer wavelength
Frequency ↑ = Wavelength ↓ (they're inversely proportional)
MF (300 kHz–3 MHz): AM broadcast, amateur 160m/80m, maritime
HF (3–30 MHz): Shortwave, all ham HF bands, CB radio (27 MHz), WWV
VHF (30–300 MHz): FM broadcast (88–108), TV, amateur 6m/2m, public safety
UHF (300 MHz–3 GHz): TV, amateur 70cm, cellular, Wi-Fi 2.4 GHz, GPS, Bluetooth
Microwave (3 GHz+): Wi-Fi 5 GHz/6 GHz, satellite TV, radar, 5G mmWave
ACTIVITY: Draw your own chart — label all five bands and mark 8 radio services
Notes: Hand out the blank spectrum chart worksheets now. Scouts fill in their chart during this slide and the next. Walk around and check their work. They must locate at least 8 radio services: AM broadcast, FM broadcast, CB, TV, amateur (4 bands), public safety, cellular, Wi-Fi.

## Slide 11
Req 2b — Three Discussion Topics
What is radio? · Broadcast vs. Two-Way
Radio: transmission of info using EM waves in the RF spectrum
TX converts audio/data → RF; antenna radiates it; RX captures and decodes
Broadcast: one-way, one-to-many (AM/FM, TV)
Two-way: both parties transmit and receive (ham, walkie-talkie, police)
Commercial Broadcast vs. Hobby Radio
Commercial: licensed for business, sells advertising, passive audience
Amateur (hobby): non-commercial, licensed for personal use and experimentation
Hams build equipment, experiment with antennas, provide emergency comms
No selling ads, no playing music for an audience
Notes: These three topics are a counselor discussion — Scouts need to explain them in their own words, not just read them back. Practice this with a volunteer Scout in the room.

## Slide 12
Requirement 3
How Radio Waves Travel — Propagation

## Slide 13
Req 3a — Three Propagation Modes
GROUND WAVE: Follows the earth's surface → MF/AM broadcast → range: a few hundred miles
SKY WAVE (Ionospheric): Signal goes up → hits the ionosphere → bends back down → HF can travel thousands of miles → explains why you hear faraway AM stations at night
LINE-OF-SIGHT (Direct wave): VHF and above travel in straight lines → limited by terrain and antenna height → FM radio, TV, 2m amateur, cellular
ACTIVITY: Sketch cross-section of earth, show all three paths with arrows
Label: transmitter, ionosphere layer, skip zone, receiver at distant skip distance
Notes: Have Scouts draw the propagation sketch in their student packs while you draw it on the whiteboard. The key teaching point is WHY AM stations are audible farther at night — the ionosphere absorbs MF during the day but not at night, allowing sky-wave propagation.

## Slide 14
Req 3b & 3c — WWV/WWVH and DX vs. Local
WWV and WWVH — Band Condition Indicators
NIST time-standard stations: WWV (Fort Collins CO), WWVH (Kauai HI)
Broadcast on 2.5, 5, 10, 15, 20 MHz — 24/7
If you can hear WWV on 20m → 20m is OPEN to Colorado
Weak signal → marginal conditions
Can't hear at all → band may be closed (absorbed)
Propagation forecast voiced at :18 each hour
DX vs. Local Stations
LOCAL: close enough for reliable ground wave or LOS reception → typically within 25–100 miles, strong and consistent
DX: "distance" — distant station reached by sky wave → signal fades in and out (QSB) → may be thousands of miles away
DX-ing is a major ham pursuit: rare countries, expeditions to remote islands, contests to work as many countries as possible
A "DX station" calling CQ on HF is usually someone YOU want to contact
Notes: WWV is something Scouts can listen to right now on the club station — pull it up on the receiver. Point out the voiced announcement at :18 past the hour. This makes the concept real and memorable.

## Slide 15
Requirement 6
Radio Regulation — FCC, ITU, Call Signs & Phonetic Alphabet

## Slide 16
Req 6a — FCC vs. ITU
FCC (Federal Communications Commission)
US government agency created by Communications Act of 1934
Regulates all radio, TV, wire, satellite, and cable in the US
Issues licenses, enforces rules, allocates US frequencies
Runs the amateur service via Volunteer Examiner Coordinators (VECs)
Investigates interference complaints
ITU (International Telecommunication Union)
UN agency — coordinates global use of radio spectrum and satellite orbits
Issues the Radio Regulations — an international treaty all nations agree to follow
Divides the world into 3 Regions; assigns frequency bands to services in each
FCC rules must comply with ITU at the international level
Simple: ITU sets global rules → FCC enforces them in the US
Notes: Ask Scouts: "Why would we need international rules for radio?" The answer: signals don't stop at borders. A US ham transmitting on HF can be heard in Europe — ITU coordinates so stations in different countries aren't using the same frequencies for conflicting purposes.

## Slide 17
Req 6b — Call Signs
AMATEUR: Prefix + Number + Suffix → e.g., W4GGJ
US prefixes: A, K, N, W — ITU-assigned
Number = call district (0–9 in continental US)
Must ID at end of every transmission and at least every 10 minutes
Your call sign identifies you — not your radio
BROADCAST: W_ _ _ _ for stations east of Mississippi, K_ _ _ _ west (with historic exceptions)
Must ID at top of each hour and at sign-on/sign-off
TV call signs use -TV suffix (WFLA-TV)
If there is a tie for "first use" — historical call signs may break the east/west rule (e.g., KDKA in Pittsburgh)
Notes: W4GGJ is Joe's personal callsign (the control op for TavaOne Education). You can use it as a real example. Walk through the structure: W = US station, 4 = 4th call district (southeastern US), GGJ = unique suffix.

## Slide 18
Req 6c — NATO Phonetic Alphabet
A–Alfa · B–Bravo · C–Charlie · D–Delta · E–Echo · F–Foxtrot · G–Golf
H–Hotel · I–India · J–Juliett · K–Kilo · L–Lima · M–Mike
N–November · O–Oscar · P–Papa · Q–Quebec · R–Romeo · S–Sierra · T–Tango
U–Uniform · V–Victor · W–Whiskey · X–X-ray · Y–Yankee · Z–Zulu
PRACTICE: Spell your first name using phonetic alphabet — say it out loud
PRACTICE: Spell your troop number phonetically
WHY: B/D/E/G/P/T/V all sound alike on a noisy radio channel — these words are chosen for maximum distinctiveness
Notes: Have the whole room say the alphabet in unison once, then each Scout spells their name. This is one of the most fun parts of the session. Note: "Alfa" is spelled without the "ph" intentionally — the NATO version is spelled phonetically to work in multiple languages.

## Slide 19
Quick Check
A ham must give their call sign: ___
A) Only at the beginning of each transmission
B) At the end of every transmission and at least every 10 minutes
C) Only when asked by another station
D) Only when transmitting on HF
Answer: B — End of every transmission AND at least every 10 minutes during a QSO (contact). This is FCC Part 97 rule.
Notes: This is a common exam question for Technician license too. If you have Scouts interested in getting licensed, point this out as double-useful knowledge.

## Slide 20
Requirement 8-A
Amateur Radio — Items 1 through 5

## Slide 21
8-A(1) — Why the FCC Has an Amateur Radio Service
Emergency communications: hams provide comms when cell/internet fails in disasters (ARES, RACES)
Advancement of the radio art: hams experiment and innovate — some innovations later go commercial
International goodwill: connecting people across borders without commercial or political purpose
Pool of trained operators: national asset in wartime or national emergency
What licensed hams can do: voice, digital, satellite (AMSAT), meteor scatter, moonbounce (EME), POTA/SOTA, APRS tracking, public service events, emergency communication
Notes: Ask Scouts if they have ever seen or heard about ham radio being used in a hurricane or tornado response. Florida examples: Hurricane Ian, Hurricane Michael. ARES operators staffed emergency management EOCs when 911 centers were flooded.

## Slide 22
8-A(2) — License Classes and VE Exams
TECHNICIAN (Element 2): 35 Qs from 423-Q pool, pass 26/35 (74%). All VHF/UHF; limited HF.
GENERAL (Elements 2+3): 35 Qs from 432-Q pool, pass 26/35. Technician privileges + most HF worldwide.
AMATEUR EXTRA (Elements 2+3+4): 50 Qs from 622-Q pool, pass 37/50. All amateur privileges; exclusive sub-bands; premium callsigns.
VE Exams: administered by Volunteer Examiners (VEs) — licensed hams accredited through Volunteer Examiner Coordinators (VECs) like ARRL-VEC, W5YI-VEC.
FCC does NOT administer the exams directly.
Exam fee: ~$15 (VEC session) + $35 FCC application fee after passing.
Notes: This is the path Scouts can take if they want to actually get on the air themselves. Point out that TavaOne Education runs Technician prep courses and holds VE exam sessions on-site. Having a license lets you operate independently without needing a control op.

## Slide 23
8-A(3) — Q Signals and Amateur Terms
QSO — A contact / "Can you communicate with ___?"
QTH — Location / "My location is ___."
QSL — Acknowledgment (also a confirmation card) / "I confirm the contact."
QRM — Interference from other stations / "I am being interfered with."
QRN — Static / "I am troubled by static."
QRZ — "Who is calling me?" / Used to ask who is there
QSB — Fading signals / "Your signals are fading."
CQ — General call: "Is anyone listening? I want to make a contact."
73 — Best regards (standard friendly sign-off)
RST — Signal report: Readability (1–5) / Strength (1–9) / Tone (1–9 for CW)
Notes: 5 Q signals is the minimum for Req 8-A(3). Go through them all so Scouts understand the system, not just memorize 5. RST is going to matter when they make their contact — they need to know how to give a signal report.

## Slide 24
8-A(4) — Emergency Calls on Voice and CW
Voice — MAYDAY
MAYDAY MAYDAY MAYDAY
[your call sign]
[your location]
[nature of emergency]
[number of people]
[any other critical info]
Repeat as needed on 146.520 MHz (2m simplex), 14.300 MHz (HF maritime mobile)
Morse Code — SOS
· · · — — — · · · (SOS)
SOS is NOT an abbreviation — it is one unbroken character: 3 dits, 3 dahs, 3 dits
Follow with DE [your callsign] — [location] — [situation]
Sent continuously until help responds or you must stop
Notes: You can have fun with this: demonstrate the MAYDAY call on a dummy mic. Ask a Scout to read it back. Point out that even if they aren't licensed, they can ALWAYS transmit to call for help in a life-or-death emergency — this is an FCC exception.

## Slide 25
8-A(5) — Transceivers and Repeaters
HANDHELD (HT — Handie-Talkie): battery-powered, portable, ~5 W, VHF/UHF, great for local use and public service events. Examples: Yaesu FT-60, Baofeng UV-5R.
MOBILE: vehicle-installed, 12 V power, 25–50 W on VHF/UHF, up to 100 W HF, larger antenna = more range. Examples: Icom IC-7100, Yaesu FT-891.
BASE STATION: fixed location, AC-powered, 100–1,500 W HF, large permanent antennas, maximum range. Examples: Icom IC-7300, Kenwood TS-890.
REPEATER: Listens on the INPUT frequency, retransmits on the OUTPUT frequency from a high location at higher power. Extends HT range from ~5 miles to 50+ miles.
Your radio needs: correct offset (e.g., −600 kHz on 2m) + CTCSS tone to open the repeater.
Many repeaters link via internet (IRLP, EchoLink, AllStar) for worldwide reach.
Notes: Point to the actual club station equipment in the room. Label which items are base station vs. HT. If you have a repeater linked, show how it works. Hands-on is better than slides here.

## Slide 26
Quick Check
What does a repeater's "offset" mean?
A) The time delay before the repeater responds
B) The difference between the repeater's input and output frequencies
C) The CTCSS tone code required to open the repeater
D) The maximum range of the repeater system
Answer: B — The offset is the frequency difference between where the repeater listens (input) and where it retransmits (output). On 2m this is typically −600 kHz.
Notes: Common source of confusion for new operators. Reinforce: your radio transmits on the INPUT; the repeater transmits on the OUTPUT. Your radio receives on the OUTPUT.

## Slide 27
Requirement 9
Career & Hobby Exploration — Homework Assignment

## Slide 28
Req 9 — Your Assignment (due before Session 2)
Option 9a — Radio Career
Research ONE career related to radio
Must cover: training, education needed, costs, job prospects, salary, duties, advancement
Good choices: broadcast engineer, RF engineer, antenna tech, air traffic controller, emergency manager, radio astronomer
Discuss findings with counselor in Session 2
Option 9b — Ham Radio Hobby or Volunteer
Research amateur radio hobby OR a volunteer role (ARES, RACES, public service)
Must cover: licensing and training, startup costs, supporting organizations
Discuss short-term AND long-term goals you might have
Interview a ham operator if possible
Notes: You only need to do ONE of these. Write your research notes in your student pack. Come to Session 2 ready to have a real conversation with the counselor — this is not a paper you turn in, it is a discussion.

## Slide 29
On-Air Time
Supervised Voice Contact — Req 8-A(6) Preparation

## Slide 30
Your First On-Air Contact — Voice Operating Procedure
1. LISTEN FIRST: Is the frequency already in use? "Is this frequency in use?" — wait 5 seconds.
2. CALL CQ: "CQ CQ CQ, this is [callsign], CQ and standing by."
3. ANSWER: "[Their callsign], this is [your callsign] — or — just [your callsign]"
4. EXCHANGE: Give name, QTH (location), and RST signal report
5. LOG IT: Date, UTC time, their call sign, band/frequency, mode, RST sent, RST received, their QTH
6. SIGN OFF: "73, this is [callsign] clear and listening."
RST reminder: "You are 5-9" = perfectly readable, extremely strong signal. "You are 5-5" = perfectly readable, middling strength. Most contacts get 5-9 if they're clear.
Notes: Walk through the procedure slowly. Have the licensed control op (W4GGJ or another GCCC operator) demonstrate a full CQ call and exchange first. Then have each Scout take a turn at the mic. They don't need to memorize the exact words — encourage natural conversation once the initial exchange is made.

## Slide 31
Session 1 Complete!
What to do before Session 2:
Complete your Req 9 research (career OR hobby/volunteer path)
Review the Q signals (QSO, QTH, QSL, QRM, QRN, QRZ, QSB)
Practice the phonetic alphabet until you can spell your name without looking
Bring this student pack, your blue card, and your Req 9 notes to Session 2
Session 2: Digital Modes · Hardware · Cell Phones · FT8 Contact · Blue Card Sign-Off
Notes: Thank Scouts for attending. Remind them to bring their signed blue card to Session 2 — the counselor cannot complete the sign-off without it. If any Scout wants to pursue a Technician license, let them know TavaOne Education runs prep courses and VE exam sessions on-site.