## Slide 1
Field Station Fundamentals
Session 2 — Radio, Antennas & Power
TavaOne Education · W4GGJ
Notes: Field Station Fundamentals

## Slide 2
Today's Session
Radio selection — which rig for portable HF
Antennas — EFHW, dipoles, verticals, deployment tools
Feedline and connectors — what to carry
Power — LiFePO4 batteries, capacity math, solar
Building your go-kit — checklist and weight targets
Hands-on: set up the club IC-705 + EFHW on the patio
Notes: Hands-on is the priority today. Keep the lecture moving — students need time outside with the station. The key concepts (battery math, EFHW basics) are in the student pack; don't get lost in detail. Aim to be outside by the 80-minute mark.

## Slide 3
Radio Selection
What to bring — and why it matters less than you think
Notes: Section: Radio Selection

## Slide 4
POTA Radio — What You Need
All-band HF transceiver (at minimum 40m + 20m)
Portable enough to carry to an operating position
Built-in or external antenna tuner
Reasonable battery draw for your expected activation length
Popular choices (ascending price):
  Xiegu G90 — 20W, 1.8 lb, built-in tuner and SDR, ~$450
  Xiegu G106 — 10W, 0.9 lb, touchscreen, ~$350
  Yaesu FT-891 — 100W, 2.2 lb, full power, needs external battery, ~$600
  Icom IC-705 — 10W, HF+VHF+UHF, built-in battery, GPS, ~$1,350
  Elecraft KX2 — 10W, 0.7 lb, AA batteries, keyer, ~$950
Notes: Show the radios on the table if available. Ask who already has a radio. If someone has a full-size HF radio at home, point out they can still do POTA with it — just bring a bigger battery. The most popular POTA radio at activations is probably the IC-705, but the Xiegu G90 is a fantastic starter.

## Slide 5
Power Considerations — TX Current
Higher power = easier contacts, shorter battery life
Typical TX current draw (at 12V):
  10W radio: 2–4A TX
  50W radio: ~10–12A TX
  100W radio: 15–22A TX
RX draw is usually 1–2A regardless of power level
SSB duty cycle: ~30% transmit / 70% receive
FT8 duty cycle: ~50% transmit
CW duty cycle: ~40% (depends on speed and spacing)
Balance: QRP (5–10W) gives longer battery life but harder contacts on bad days
Sweet spot for most activators: 25–50W with a 20Ah LiFePO4
Notes: Do the quick math live: 50W FT-891, 50W output at 12A TX. SSB duty 30%. Average draw = (12 × 0.3) + (1.5 × 0.7) = 4.65A. 20Ah battery ÷ 4.65A = 4.3 hours. Subtract 20% for LiFePO4 health = 3.4 hours. That's more than enough for any reasonable activation.

## Slide 6
Antennas for Portable Ops
The wire that does the work
Notes: Section: Antennas for Portable Ops

## Slide 7
End-Fed Half-Wave (EFHW) — Why It Won
The most popular POTA antenna — and for good reason
How it works:
  A half-wave wire fed at the high-impedance end
  49:1 transformer drops impedance to match 50-ohm coax
  40m wire: 66 feet — resonant on 40m, 20m, 15m, 10m (harmonics)
Why activators love it:
  Only needs support at ONE end (tree, squid pole)
  No ground plane required
  4 bands, no tuner adjustment between them
  Entire kit weighs under 1 lb and fits in a sandwich bag
Build cost: $15–20 in parts (FT140-43 toroid + wire)
Buy: SOTAbeams, MyAntennas EFHW-8010, Packtenna — $60–120
Notes: Hold up the club EFHW transformer — show how small it is. Then show 66 feet of wire coiled up. That's the antenna. The whole thing weighs maybe 4 oz. This is why it won. Walk through the theory briefly — the wire is a half-wave at 40m, so it's a full wave at 20m, 1.5 wave at 15m, etc. All are resonant multiples. The tuner may need a touch at some bands but usually not.

## Slide 8
Wire Dipole vs. Linked Dipole
📡 Center-Fed Wire Dipole
Half-wave per side (33 ft per leg on 40m)
50-ohm match — excellent SWR without a tuner
Needs 3 support points (center + 2 ends)
One band per build (need separate dipoles per band)
Works well as inverted-V with center up
Easy to build: center insulator + 2 wires + feedline
🔗 Linked Dipole
Quick-disconnect links (bullet connectors) in each leg
Remove links to shorten = change bands
No tuner needed for each resonant band
Common builds: 40/20/15/10m (3 links per side)
More deployment steps — clip links before TX
Popular with CW operators who hate tuner losses
Notes: Show the comparison physically if you have both antennas. The linked dipole looks more complex but becomes intuitive after a few deployments. For someone doing mostly SSB on one or two bands, a simple dipole is plenty. For someone wanting to bounce between 40m, 20m, and 10m without a tuner, linked dipole is the way.

## Slide 9
Verticals and Deployment Tools
Verticals — when trees aren't available:
  Chameleon MPAS Lite: versatile, needs radials, ~$200
  Wolf River Coil: loaded vertical, compact, ~$80
  Commercial hamsticks on a mag mount: vehicle-portable
  Key: always include a counterpoise or radials — skip it and efficiency tanks
Deployment tools:
  Throw bag + paracord: 3 oz bag + 100 ft line; toss over a branch
  Squid pole (fiberglass telescoping): 7–10m up to 60cm collapsed; best all-around
  Collapsed fishing rod: cheap substitute, works fine
  Painter pole: heavy but inexpensive and common
Practice throw-bag technique at home before your first activation
Notes: Walk outside and demo the throw bag if there's a suitable tree. Or demo with the squid pole. Students who haven't deployed an antenna outdoors often underestimate how much time it takes. The 15-minute station assembly activity will show them.

## Slide 10
Power Sources
LiFePO4, solar, and the capacity math
Notes: Section: Power Sources

## Slide 11
LiFePO4 — The Standard
Lithium Iron Phosphate: the POTA battery of choice
Why LiFePO4 beats lead-acid and standard lithium:
  Safe chemistry — won't catch fire if punctured or overcharged
  Flat discharge curve — stays at 13.2V until nearly empty
  1C discharge rate — 20Ah battery delivers 20A continuously
  2000+ charge cycles (lead-acid: ~500)
  Lighter: ~60% the weight of equivalent AGM
Popular brands: Bioenno, Dakota Lithium, Battleborn, Renogy
Do NOT discharge below 20% — protect cycle life
Charge with a LiFePO4-compatible charger — not a car charger
Notes: Pass around the 20Ah Bioenno battery. Let students feel the weight. For comparison, a 20Ah AGM battery weighs about 15 lbs. This weighs 4.4. That's the entire case for portable LiFePO4 operations. Mention the Anderson Powerpole connectors — ARRL standard for ham radio, worth putting on your go-kit cables for compatibility.

## Slide 12
Capacity Math — Size Your Battery
Formula: Average draw = (TX amps × TX duty%) + (RX amps × RX duty%)
Example — FT-891 at 50W, SSB:
  TX draw at 50W: 12A
  RX draw: 1.5A
  TX duty: 30%
  Average = (12 × 0.3) + (1.5 × 0.7) = 3.6 + 1.05 = 4.65A
  20Ah battery usable (80%) = 16Ah
  Runtime: 16 ÷ 4.65 = 3.4 hours
Example — IC-705 at 10W, FT8:
  TX draw: 3A | RX: 1A | TX duty: 50%
  Average = (3 × 0.5) + (1 × 0.5) = 2A
  10Ah battery (8Ah usable) ÷ 2A = 4 hours
Notes: Have students do the math with their own radio's specs. Most radio manuals list TX current draw. If they don't know their radio's draw, suggest checking the spec sheet or EHAM reviews. The math is quick once you know the numbers. Reinforce: always size for more capacity than you think you need — you can always bring the battery home full.

## Slide 13
Solar and USB Power
Solar — supplemental, not primary for most activations
  40W panel in full Florida sun: ~3A charge rate at 12V
  Pair with MPPT charge controller (Renogy 10A, ~$25)
  Weight penalty: ~2.5 lbs for 40W panel
  Best use: vehicle-portable multi-park day, long activations
  Not worth it for a single 90-minute activation — just bring a bigger battery
Generators — last resort
  Heavy, noisy, need fuel, many parks prohibit them
  If you think you need a generator, you've over-estimated power needs
  Solution: run lower power instead
USB power bank for logging devices
  Keep phone/tablet charged separately from the radio battery
  10,000–20,000mAh bank handles a full activation day
  Do not drain the radio battery through a USB adapter
Notes: Many students ask about solar. It's cool, it works, but for the typical 2-hour POTA activation you will never recoup the weight penalty. Where solar shines: long day trips to a park where you activate morning, have lunch, activate again in the afternoon. Or multi-day camping activations. For the capstone, we're just bringing batteries.

## Slide 14
Building Your Go-Kit
Ready to grab, ready to go
Notes: Section: Building Your Go-Kit

## Slide 15
The Go-Kit Philosophy
Should be ready to grab at any moment
Activation opportunity appears → you're on the road in 10 minutes
Everything lives in one bag, always stocked
Essentials:
  Radio + power cable + mic/headphones
  Antenna (EFHW or dipole) + feedline + adapters
  Battery (charged)
  Throw bag + line, or squid pole
  Logging device + paper backup + pens
  USB power bank
  FCC license (printed or phone)
Comfort:
  Portable chair or seat pad
  Water, snacks, sunscreen, bug spray
Notes: The go-kit discipline is underrated. How many times have you decided to activate somewhere on a whim but then spent 45 minutes finding gear? The bag that lives in your trunk is worth more than any radio upgrade. Share the "grabbed the bag and caught a P2P on the way to a soccer game" style story — it happens.

## Slide 16
Weight Targets by Setup Type
🚗 Vehicle-Portable
Park within walking distance of car
Under 40 lbs total — anything goes
Full station: 100W radio, big battery, real antenna
Comfort items: table, chair, umbrella
Best for first activations — minimize variables
🎒 Hike-Portable
Short hike (&lt;1 mile): under 25 lbs
Long hike / backpack: under 10 lbs
QRP radio (KX2, IC-705, G106)
66 ft EFHW on a squid pole
10Ah LiFePO4, phone logging
Everything fits in a daypack
Notes: For the capstone activation, we're doing vehicle-portable — park at the trailhead, walk 100 yards, set up. Perfect for learning. Once you've done 5 or 6 activations and know your kit cold, the hike-in activations become fun. But vehicle-portable first.

## Slide 17
HANDS-ON ACTIVITY
Station Setup — Bag to RF-Ready
Team roles (everyone rotates):
  Radio operator — unpack, connect power + feedline
  Antenna crew — unwind EFHW, connect to feedline, deploy
  Power crew — check battery voltage, connect to radio
  Logger — open HAMRS, start activation, enter park reference Done when: radio powered, antenna up, SWR checked, HAMRS loadedTarget: RF-ready in under 15 minutes
20 minutes · patio setup
Notes: Move everyone outside. Station bags are pre-packed on the counter. Don't let anyone read instructions — have them figure it out together, then correct. Key debrief point: what would you do differently? What needed more pre-staging? Usually answer is: pre-connect the feedline to the transformer before leaving home, pre-wind the throw bag, pre-charge the battery. None of this is hard but doing it under a time clock in a park for the first time is stressful.

## Slide 18
KNOWLEDGE CHECK
A 40m EFHW is built with 66 feet of wire. Without any changes, it also resonates on which bands?
A. 80m and 160m (longer harmonics)
B. 20m, 15m, and 10m (harmonic multiples)
C. Only 40m — EFHW is single-band
D. 60m and 30m (WARC bands)
Notes: ANSWER: B — 20m, 15m, and 10m 40m is the fundamental; 20m is the 2nd harmonic, 15m is the 3rd, 10m is the 4th. This is why the EFHW is so popular — four bands from one wire.

## Slide 19
KNOWLEDGE CHECK
Why is LiFePO4 preferred over lead-acid (AGM/SLA) for portable POTA operations?
A. LiFePO4 is cheaper per Ah
B. LiFePO4 is lighter, has more cycles, and holds voltage better through discharge
C. LiFePO4 doesn't need a BMS or charge controller
D. LiFePO4 works in hot climates; AGM doesn't
Notes: ANSWER: B — Lighter, more cycles, flatter discharge curve Price per Ah is actually higher for LiFePO4 initially but lower over the battery's lifetime due to 2000+ cycles vs ~500 for AGM. In Florida heat, both technologies need care — don't leave either in a hot car unnecessarily.

## Slide 20
KNOWLEDGE CHECK
You arrive at an open field with no trees. Your antenna kit contains an EFHW, a throw bag with paracord, and an 8m squid pole. What do you do?
A. Give up and drive to a park with trees
B. Deploy the EFHW vertically using the squid pole as a mast
C. The EFHW won't work without a tree — need a different antenna
D. Call CQ on VHF FM only
Notes: ANSWER: B — Deploy vertically on the squid pole The squid pole saves you in open areas. Run the EFHW wire up the pole and let it hang vertically, or run it as an inverted-L. The antenna works in any orientation — you just need to get the wire up somehow. Alternatively, an inverted-V dipole with the squid pole at center also works perfectly.

## Slide 21
Session 3 Preview
Operating, Logging & Uploading
CQ POTA calling procedure and exchange
Self-spotting on pota.app — getting hunters on your frequency
FT8 from the field — WSJT-X setup and the digital workflow
HAMRS logging — walkthrough from activation create to ADIF export
Log upload to pota.app — full workflow, common errors
Simulated activation: log 10 contacts start-to-finish
Bring: phone with HAMRS installed, pota.app login ready
Notes: Remind everyone: install HAMRS before Session 3 (free, iOS and Android). Make sure pota.app login works. Session 3 is heavily hands-on — the simulated activation is the core of the session. Also mention the capstone date if it's been scheduled.