## Slide 1
Operating, Logging &
Uploading
Session 3 — The On-Air Workflow
TavaOne Education · W4GGJ
Notes: Operating, Logging & Uploading

## Slide 2
Today's Session
Band and mode selection — when to be where
CQ POTA procedure and exchange
Self-spotting on pota.app
FT8 from the field — why it matters
HAMRS logging — walkthrough from create to ADIF
Log upload to pota.app — full workflow
Simulated activation — 10 QSOs start to upload
Notes: Heavy session — cover the material efficiently and save 15 minutes for the simulation. The simulation is where it clicks. Don't skip it.

## Slide 3
Band & Mode Selection
When to be where, and why
Notes: Section: Band & Mode Selection

## Slide 4
Band Strategy for Florida Activations
40m — the workhorse. Morning/afternoon: regional (0–500 mi). Night: 500–2500 mi.
20m — midday through mid-afternoon. Best for 1,000–4,000 mi hunters.
15m / 10m — when solar flux is high. Check before going. Often excellent in Solar Cycle 25.
80m — evenings, high noise, short range. Backup when 40m skips over your area.
VHF FM — 147.555 simplex. Any time. Local hunters, quick opener.
Pre-activation check:
  PSKReporter.info — see what bands are open in your area
  DX Maps app — real-time propagation map
  POTA Spots page — what bands active activators are using right now
Notes: Pull up PSKReporter live on screen and show what the current bands look like. Point to Florida on the map. Show where signals are being heard. This is more useful than any propagation theory — students learn to look at the map instead of memorizing rules.

## Slide 5
Mode Tradeoffs
🎙️ Phone (SSB)
20–60 contacts/hour in good conditions
No extra gear needed
Easy to manage a pileup verbally
Easiest way to explain you're in a park
Signal must be strong enough for voice
Most fun — you talk to real people
💻 FT8/FT4
30–80 contacts/hour, marginal conditions OK
Needs laptop/tablet + audio interface
15 dB better than SSB weak-signal
Excellent for days when SSB is tough
High TX duty cycle — watch power output
Works while you're sipping coffee
Notes: Make the point that these aren't in competition — they complement each other. Start with SSB for the enjoyment and human contact, switch to FT8 if you're struggling to get to 10. Many operators do both in the same activation. CW is a third option — not covering it deeply in this course but it's very effective for POTA. Point students to CWops and LCWO for practice resources.

## Slide 6
CQ POTA — The On-Air Workflow
From first call to last contact
Notes: Section: CQ POTA — The On-Air Workflow

## Slide 7
Finding a Clear Frequency
Before you transmit:
  Listen for 30–60 seconds on the frequency
  Ask "Is this frequency in use?" (CW: "QRL?")
  Wait 5 seconds — if no response, proceed
Common POTA frequency ranges (not exclusive):
  40m SSB: 7.200–7.290 MHz
  20m SSB: 14.150–14.300 MHz
  15m SSB: 21.200–21.400 MHz
  40m CW: 7.025–7.060 MHz
Avoid: known repeater inputs, other spotted activators, beacon frequencies
If the band is crowded: go up 5 kHz and try again
Notes: Stress the listen-first habit. Especially on 40m, the band can be crowded and jumping on an occupied frequency creates problems. Show the 40m segment on a bandscope if available. The good news: hunters know to listen for activators across a range of frequencies, so you have flexibility.

## Slide 8
The CQ POTA Exchange
CQ POTA, CQ POTA — this is Whiskey Four Golf Golf Juliet, W4GGJ
activating K-2119, Honeymoon Island State Park — W4GGJ listening
Exchange:
HUNTER: W4GGJ de K1ABC, 59 in Massachusetts
W4GGJ: K1ABC, you're 57, thanks for the Parks, 73
HUNTER: Thanks! 73
W4GGJ: QRZ? W4GGJ ← go immediately to next caller
Key: callsign + signal report only. No chat during a run.
Notes: Practice this exchange out loud with the class. Have a student call back, you respond. Then switch. The rhythm comes quickly. Emphasize QRZ immediately after — no dead air, no pleasantries during the run. You can chat with someone after you have 10 contacts. Before that, every second of dead air is a hunter giving up and tuning away.

## Slide 9
Managing a Pileup
When spotting works, multiple hunters call simultaneously
Rules for working a pileup:
  1. Pick ONE callsign you heard clearly
  2. Call them back: "W1ABC, you're 57, thanks for the Parks"
  3. QSL briefly, then: "QRZ? W4GGJ" — go immediately
  4. Never stop calling — dead air loses hunters
  5. Never chat during the run
If you can't pull a full callsign:
  "The station ending in Lima?"
  "Partial copy — last two characters?"
If QRM builds: move 5 kHz, re-spot new frequency
If pileup outruns you: stay calm, slow down, pick one at a time
Notes: A pileup is a good problem. Tell students that the chaos of 5 stations calling simultaneously is exciting — the trick is staying methodical. Pick one, work them, move on. If you can't separate two stations, don't guess. Ask for a partial. Most hunters are experienced and will adjust to your pace.

## Slide 10
Self-Spotting
Getting hunters on your frequency
Notes: Section: Self-Spotting

## Slide 11
Why Spotting Is Non-Negotiable
Without a spot on pota.app, hunters don't know you're active
A good spot can produce 5–10 callers within 60 seconds
How to self-spot:
  pota.app → Activator Tools → Spot Yourself
  Enter: callsign, park reference, frequency, mode
  Optional comment: "40m SSB running, come get it"
Spot accurately:
  Frequency must match what you're actually on (not 7.245 when you're on 7.247)
  If you QSY, re-spot immediately
Also visible to hunters via:
  DX cluster spots (DXsummit.fi)
  HamAlert push notifications
  POTA Watch website
Notes: Demo this live — open pota.app on the projected screen and walk through spotting. Show what the Spots page looks like from the hunter's side. If a real spot is happening nearby, point it out. The spot page is real-time and refreshes every minute.

## Slide 12
FT8 from the Field
The secret weapon for marginal conditions
Notes: Section: FT8 from the Field

## Slide 13
Why Learn FT8 for POTA
FT8 operates 15 dB below the noise floor — far beyond voice range
A band that sounds "dead" may have active FT8 contacts happening on it
Practical impact:
  SSB might get you 3 contacts on a bad band day
  FT8 gets you 10 contacts on that same day
Standard field setup:
  WSJT-X software (free, all platforms)
  Digirig ($50) + cable for most radios
  OR IC-705 built-in USB (no extra hardware)
POTA FT8 frequencies:
  40m: 7.074 MHz (dial USB)
  20m: 14.074 MHz
  15m: 21.074 MHz
Spot yourself on pota.app even on FT8 — hunters still check spots first
Notes: FT8 takes about 30 minutes to set up the first time, then it's plug and play. If students want to try FT8 at the capstone activation, offer a brief pre-capstone setup session (even 20 min helps). The Digirig is inexpensive enough to not be a barrier. For IC-705 users: just the USB cable and WSJT-X — almost zero friction.

## Slide 14
FT8 Duty Cycle Warning
FT8 is 100% duty cycle — full RF output for 13.5 of every 15 seconds
Implications:
  PA runs hot — reduce power for FT8 vs SSB
  Rule of thumb: 50% of max power rating for FT8
  FT-891: don't exceed 50W for FT8
  IC-705: 5W is already conservative — fine at 5W
Battery impact:
  FT8 at 50W ≈ constant 12A draw (no RX recovery)
  Plan shorter runtime or bigger battery for FT8 sessions
Contacts per minute:
  Once spotted and running: 3–6 contacts/minute is achievable
  10 contacts in under 5 minutes is common
  Do your math: the battery trade-off is worth it
Notes: Some students are surprised by the power warning. Make it concrete: at 100W SSB, the PA is transmitting 100W for 30% of the time on average. At 100W FT8, it's transmitting 100W for 95% of the time. The heat and battery math is completely different. 50W is the safe FT8 ceiling for most 100W radios.

## Slide 15
Field Logging
Paper, HAMRS, and WSJT-X
Notes: Section: Field Logging

## Slide 16
HAMRS — Full Walkthrough
1. Open HAMRS → tap + (new activation)
2. Select POTA template
3. Enter your callsign and park reference (K-2119)
4. Set default band and mode
5. Tap Start Activation
Logging a QSO:
  Type callsign in CALL field
  Date and time auto-populate in UTC
  Adjust band/mode if changed
  Enter RST sent (59 for SSB default)
  Tap Log QSO
Exporting ADIF:
  Activations → tap your activation → Export → ADIF
  Share to email, Drive, or AirDrop
Notes: Walk through this live on screen with HAMRS open on your phone projected. Do a real entry. Show students the QSO list building up. Then do the export — open the file in a text editor so they can see the raw ADIF. This demystifies the format completely.

## Slide 17
What ADIF Looks Like
<CALL:5>K1ABC <QSO_DATE:8>20260919 <TIME_ON:4>1532
<BAND:3>40M <MODE:3>SSB <RST_SENT:2>59
<SIG:4>POTA <SIG_INFO:6>K-2119 <EOR>
Critical fields:
CALL — their callsign
QSO_DATE — YYYYMMDD in UTC
TIME_ON — HHMM in UTC
BAND — 40M, 20M, 15M, etc.
SIG — must be exactly "POTA"
SIG_INFO — your park reference (K-2119)
Notes: HAMRS generates this automatically. The two red fields — SIG and SIG_INFO — are what POTA needs that a generic logger won't provide. Show the raw file and highlight those two fields. When students understand the format, they can fix export issues themselves instead of panicking.

## Slide 18
Uploading to pota.app
Log in to pota.app
My Activations → Upload Log
Select your ADIF file
Preview the upload — check park ref and contact count
Click Submit
Processing: usually instant
Common errors:
  "0 valid POTA contacts" → missing SIG/SIG_INFO fields
  "Invalid park reference" → typo; must include dash (K-2119)
  "Duplicate contact" → normal if re-uploading; duplicates silently rejected
After upload:
  Activation appears on your profile
  Hunters get credit automatically
  Activation visible in the global leaderboard
Always upload even if you didn't make 10
Notes: Demo the upload live if possible. If you have a test account, upload the log you just built in the HAMRS demo. If not, show screenshots of the upload flow. The confirmation screen where the activation shows on the profile is satisfying — screenshot it and show the class.

## Slide 19
Awards & Milestones
What you're chasing
Notes: Section: Awards & Milestones

## Slide 20
POTA Award Structure
Activator awards — based on valid activation count:
  1, 10, 25, 50, 100, 250, 500, 1000 activations
Park awards — unique parks activated:
  Separate from activation count
  Rare to repeat the same park a lot early on — explore
Hunter awards — unique parks worked as a hunter:
  1, 10, 25, 50, 100, 250, 500, 1000 parks
  Tracked automatically from uploaded hunter logs
P2P awards — park-to-park contacts:
  When you're activating and work another activator
  Both get P2P credit — separate award track
Leaderboards: worldwide, by entity, by state
Most-wanted list: unactivated or rarely activated parks
Notes: Show the badge icons on pota.app. Tell students their first activation gets them a badge — even just the 1-activation mark. It's motivating. Mention the "most-wanted" parks concept — some operators make a game of finding the rarest parks in their state and activating them. That's a great long-term goal to set early.

## Slide 21
SIMULATED ACTIVATION
From CQ to Upload
Instructor calls CQ POTA on club station (mock park)
Students call back — take turns at the mic
All students log simultaneously in HAMRS on phones
Paper log backup running simultaneously
Group reaches 10 QSOs together
Export ADIF from HAMRS — open in text editor
Upload to pota.app test account — watch it go live
15 minutes · phones out · HAMRS open
Notes: This is the session payoff. Move quickly and don't over-coach — let students figure out the rhythm. The student who freezes at the mic needs one try at it, then they'll be fine. Watch for students who aren't opening HAMRS and gently redirect. The upload confirmation at the end is the "this is real" moment for many students.

## Slide 22
KNOWLEDGE CHECK
The standard FT8 calling frequency on 20 meters is:
A. 14.000 MHz (CW calling frequency)
B. 14.074 MHz (FT8 calling frequency)
C. 14.225 MHz (SSB general)
D. 14.300 MHz (maritime emergency)
Notes: ANSWER: B — 14.074 MHz Same pattern: 40m is 7.074, 20m is 14.074, 15m is 21.074. Easy to remember — always .074 offset from the band edge pattern. Dial in USB mode for FT8.

## Slide 23
KNOWLEDGE CHECK
You upload your ADIF and pota.app says "0 valid POTA contacts found." The most likely cause is:
A. The contacts were on the wrong date
B. The SIG and SIG_INFO fields are missing from the ADIF
C. You didn't wait 24 hours before uploading
D. Your callsign doesn't match your pota.app username
Notes: ANSWER: B — Missing SIG/SIG_INFO fields pota.app needs to know these were POTA-specific contacts and which park they were from. HAMRS adds these automatically if you set the park reference at activation start. Generic loggers don't add them. Fix: open the ADIF in a text editor and add <SIG:4>POTA and <SIG_INFO:6>K-XXXX to each record.

## Slide 24
KNOWLEDGE CHECK
After calling CQ POTA for 10 minutes with no response, what should you try FIRST?
A. Give up and go home
B. Check if you self-spotted on pota.app with the correct frequency
C. Move to 80m immediately
D. Call only on CW instead of SSB
Notes: ANSWER: B — Check your pota.app spot No spot = no hunters know you're there. The most common reason for zero responses is a missing or incorrect spot. Check the spot page — is your callsign there? Is the frequency correct? If the spot looks fine and still no response after 5 more minutes, check propagation (PSKReporter) and consider changing bands.

## Slide 25
Session 4 — Field Activation Capstone
The Real Thing
Local POTA park — real activation, real contacts
Team setup: everyone assembles the station
Every student operates — at least 1 contact at the mic
Every student logs in HAMRS simultaneously
Group self-spots on pota.app
Upload log live — watch activation go live on pota.app
TavaOne Education POTA Activator Certificate issued
Notes: Announce the capstone date, time, meet location, and park reference here. If not yet scheduled, ask students for their available weekends. A Sunday morning activation is ideal for Florida — cooler temps, active bands, parks not yet crowded. Target a park within 20 miles that has a covered pavilion as weather backup. Honeymoon Island (K-2119) or Brooker Creek (K-2872) are great Pinellas-area options.