## Slide 1
Module 5: Practical Circuits
Digital Circuits · Amplifiers · Filters · SDR · Op-Amps · Oscillators
2024-2028 Amateur Extra Question Pool
TavaOne Education · Pinellas STEM Radio Lab
Notes: Module 5 opening slide.

## Slide 2
The Heaviest Module
8 exam questions — E7A through E7H — 16% of your Extra exam
Tied with E9 as the heaviest subelement in the pool
This is the hardest module — the content spans RF circuit design
Hour 1:
→ E7A: Digital circuits — flip-flops, counters, logic gates
→ E7B: Amplifier classes (A, AB, B, C, D)
→ E7C: Filter responses and matching networks
Hour 2:
→ E7D-E: Power supplies, modulation/demodulation
→ E7F: Software Defined Radio and DSP
→ E7G: Operational amplifiers and gain formulas
→ E7H: Oscillators — Colpitts, Hartley, PLL, DDS
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: Tell students this is the one to budget extra HamStudy time for. E7B (amplifier classes) and E7G (op-amp gain) have direct calculation questions. Get comfortable with the formulas.

## Slide 3
Part 1: Digital Circuits
Subelement E7A — 1 exam question
Notes: Flip-flops and logic gates — the building blocks of every digital circuit in your radio.

## Slide 4
Flip-Flops, Counters, Multivibrators
Flip-flop: bistable circuit — stays in state 0 or 1 until a clock edge triggers it
→ Each flip-flop divides frequency by 2
→ 4 flip-flops in series: divide by 2⁴ = 16
Decade counter: produces one output pulse per 10 input pulses (÷10)
Astable multivibrator:
→ Continuously oscillates — no stable state
→ Generates its own square wave — no external clock needed
Monostable multivibrator (one-shot):
→ Has ONE stable state
→ Trigger pulse sends it to the other state for a fixed time, then returns
Bistable (flip-flop): requires external trigger to change state
Positive logic: HIGH voltage = logic 1; LOW voltage = logic 0
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: Real-world: the frequency synthesizer in your radio uses flip-flop chains to divide down a reference oscillator. A 100 MHz crystal divided by 10 million gives 10 Hz steps.

## Slide 5
Logic Gate Truth Tables
Gate Behavior
NAND: output 0 ONLY when all inputs are 1
NOR: output 1 ONLY when all inputs are 0
OR: output 1 if ANY input is 1
AND: output 1 ONLY when all inputs are 1
XOR: output 1 when inputs DIFFER
XNOR: output 0 when inputs differ
NOT: output is opposite of input
NAND = universal gate (can make any function)
Truth Table: XOR
Input A | Input B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NAND truth table (2 inputs):
0,0 → 1 | 0,1 → 1
1,0 → 1 | 1,1 → 0
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: The exam tests NAND, XOR, and XNOR most often. NAND: only false when all true. XOR: true when different. XNOR: the inverse of XOR.

## Slide 6
Part 2: Amplifier Classes
Subelement E7B — 1 exam question
Notes: Amplifier class selection is one of the most practical decisions in RF circuit design. Every transmitter PA is designed around one of these classes.

## Slide 7
Amplifier Classes Comparison
Class A: device biased halfway between saturation and cutoff
→ Conducts for the full 360° of the input cycle
→ Lowest distortion; can amplify any waveform including SSB
→ Lowest efficiency (~25-30%); wastes power as heat
Class AB: each device in a push-pull pair conducts >180° but <360°
→ Good linearity; better efficiency than A (~50-70%)
→ Standard for SSB linear amplifiers
Class B: each device conducts exactly 180° (push-pull)
→ ~60-70% efficiency; crossover distortion without bias
Class C: conduction less than 180°
→ Highest distortion — NOT suitable for SSB
→ Works for CW and FM (constant envelope) with tuned output
→ Efficiency >80%
Class D: switching amplifier; device is at saturation or cutoff
→ Efficiency >90%; must filter output to remove harmonics
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: Ask: why is Class C fine for FM but not SSB? FM is constant amplitude — the tuned output restores the sine wave. SSB has amplitude modulation baked into it — Class C would clip the peaks and distort the content.

## Slide 8
Amplifier Configurations
Common emitter: most common; voltage gain with phase inversion
→ Figure E7-1: R1/R2 = voltage divider bias network; R3 = emitter self-bias
Common collector (emitter follower):
→ Input and output in PHASE (no phase inversion)
→ Voltage gain ~1; high input impedance, low output impedance
→ Used as impedance buffer
Grounded-grid amplifier (vacuum tube):
→ Low input impedance
→ Used in high-power HF amplifiers
Parasitic oscillation:
→ Unintended oscillation in an amplifier stage
→ Fix: install parasitic suppressors (ferrite beads on leads) and/or neutralize the stage
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: Emitter follower (common collector) is the transistor version of a cathode follower in tubes. It buffers impedance — high-Z in, low-Z out — without much voltage gain. Classic use: driving a coax cable from a high-impedance source.

## Slide 9
Part 3: Filters and Matching
Subelement E7C — 1 exam question
Notes: Filter response names are directly tested. Know the three filter types and what makes each different.

## Slide 10
Filter Response Types
Butterworth: maximally flat passband — no ripple anywhere
→ Smooth rolloff; moderate transition steepness
→ Best when passband flatness is most important
Chebyshev: ripple in the passband
→ Sharper cutoff than Butterworth for same number of poles
→ Trades passband ripple for steeper transition
→ Used when stopband attenuation is important and passband ripple is acceptable
Elliptical (Cauer): ripple in BOTH passband and stopband
→ Steepest transition of all for same number of poles
→ Has transmission zeros (notches) in the stopband
→ Used where sharp cutoff and stopband rejection are critical
Bessel: maximally flat group delay (linear phase)
→ Preserves waveform shape — best for digital/pulsed signals
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: Memory trick: Butter-worth = smooth (like butter). Cheby-shev = ripple in (starts with 'rip'). Elliptical = ripple everywhere. Ask: which filter would you use for a crystal bandpass filter in a receiver? Chebyshev or elliptical — sharp is good.

## Slide 11
Matching Networks and Stubs
Pi-network (low-pass):
→ Shunt C to ground → series L → shunt C to ground
→ Standard amplifier output matching; provides harmonic suppression
T-network (high-pass):
→ Series C → shunt L to ground → series C
Pi-L network: Pi-network + additional series inductor
→ Greater harmonic suppression than Pi alone
Band-pass filter: has two cutoff frequencies (upper and lower -3 dB points)
Stub filter: short section of transmission line (open or shorted)
→ Used at VHF/UHF/microwave for filtering
Impedance matching goal:
→ Cancel the reactive component (make it purely resistive)
→ Transform the resistive component to the desired value
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: Pi-network is the standard in any HF amplifier output because it simultaneously matches impedance AND provides low-pass filtering. The L-network only matches. The Pi-network does both in one step.

## Slide 12
Part 4: Power Supplies and Modulation
Subelements E7D-E — 1 exam question
Notes: Modulators and demodulators are at the heart of every radio. Know which circuit does what.

## Slide 13
Modulation and Demodulation Circuits
Modulator Circuits
Reactance modulator: varies oscillator frequency with audio → FM
Phase modulator: varies phase → PM (phase modulation)
Balanced modulator: multiplies carrier × audio
→ Output: DSB with SUPPRESSED CARRIER
→ Carrier is canceled; only sidebands remain
SSB filter method:
→ Balanced modulator + sideband filter = SSB
Switching regulator: high efficiency; switches to transfer energy
Linear regulator: simple but dissipates power as heat
Demodulator Circuits
Product detector: multiplies SSB signal with BFO
→ BFO reinserts the carrier; recovers audio
→ Used to demodulate SSB and CW
Mixer: multiplies two frequencies
→ Output: sum (f1+f2) and difference (f1-f2)
→ Used in superheterodyne receivers for frequency conversion
Envelope detector: follows AM carrier amplitude
→ Simple AM demodulator
Solar array charge controller: manages voltage/current from solar panels to batteries
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: Balanced modulator is the key stage in an SSB transmitter. It cancels the carrier while keeping the sidebands. Then the sideband filter removes one sideband, leaving just the upper or lower.

## Slide 14
Part 5: SDR and DSP
Subelement E7F — 1 exam question
Notes: SDR is how modern radios work. The concepts here explain why a Flex or IC-7300 works differently from a classic superheterodyne.

## Slide 15
Software Defined Radio Architecture
Traditional radio: analog filters and mixers do most of the work
SDR: convert to digital as early as possible; do everything in software
ADC (Analog-to-Digital Converter):
→ Samples the analog signal at high rate
→ Nyquist criterion: sample rate must be ≥ 2× highest signal frequency
→ Quantization: rounds each sample to nearest digital step
→ Dynamic range: ~6 dB per bit (16-bit = ~96 dB)
SDR overload: input signal exceeds ADC reference voltage
→ Fix: add attenuation before the ADC
DSP filtering: performed AFTER analog-to-digital conversion (in software)
→ FIR filter: finite impulse response; always stable; linear phase possible
→ IIR filter: infinite impulse response; recursive; more efficient; can oscillate
Advantages of DSP: flexible, reconfigurable, highly precise filter shapes
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: The IC-7300 digitizes the entire HF spectrum right after a low-noise amplifier. All filtering, AGC, and demodulation happens in an FPGA. The physical radio is essentially a high-quality ADC with an antenna port.

## Slide 16
Part 6: Operational Amplifiers
Subelement E7G — 1 exam question
Notes: Op-amp gain calculations appear directly on the exam. Know both formulas cold.

## Slide 17
Op-Amp Configurations and Gain
Ideal op-amp: infinite input impedance, zero output impedance, infinite open-loop gain
Inverting amplifier:
→ Gain = -(Rf/Rin) [negative = phase inversion]
→ Virtual ground at inverting input
→ Example: Rin=1kΩ, Rf=10kΩ → Gain = -10
Non-inverting amplifier:
→ Gain = 1 + (Rf/Rin) [positive = in phase]
→ Example: Rin=1kΩ, Rf=9kΩ → Gain = 1+9 = 10
Voltage follower (unity gain buffer):
→ Output connected directly to inverting input
→ Gain = 1; high input impedance, low output impedance
Summing amplifier: multiple inputs, each weighted by its Rf/Rin ratio
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: Work two examples right now. Inverting: Rin=2.2k, Rf=22k → -(22k/2.2k) = -10. Non-inverting: Rin=1k, Rf=4.7k → 1+(4.7k/1k) = 5.7. These exact numbers show up in the pool.

## Slide 18
Part 7: Oscillators
Subelement E7H — 1 exam question
Notes: Every transmitter has an oscillator. Know the topology names and what distinguishes each one.

## Slide 19
Oscillator Types
Colpitts: capacitive voltage divider provides the feedback
→ Two capacitors in the tank circuit; the junction between them feeds back
→ Common RF oscillator; stable; widely used
Hartley: inductive voltage divider (tapped coil) provides feedback
→ Tapped inductor in the tank; tap point feeds back
→ Simple; good for VFOs
Crystal oscillator: quartz crystal controls frequency via mechanical resonance
→ Very stable; used as reference oscillator
VCO (Voltage Controlled Oscillator): varactor tunes the tank circuit
→ Voltage changes capacitance; frequency follows
PLL (Phase-Locked Loop): VCO output compared to reference; error corrects VCO
→ Locks VCO to crystal-stable reference at any synthesized frequency
DDS (Direct Digital Synthesizer): digital lookup table + DAC
→ Generates frequency from math; very fine resolution; fast switching
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: Ask: what's in your radio's synthesizer? Probably a PLL with a DDS. The DDS generates a fine-step reference for the PLL, giving you the frequency resolution you see on the dial.

## Slide 20
Oscillator Quality and Stability
TCXO (Temperature-Compensated Crystal Oscillator):
→ Compensation circuit corrects for crystal frequency variation with temperature
→ Used in GPS receivers, precision instruments
OCXO (Oven-Controlled Crystal Oscillator):
→ Crystal kept at constant elevated temperature in a small oven
→ Highest practical frequency stability
Phase noise:
→ Close-in frequency instability — noise sidebands on either side of carrier
→ Affects receiver performance: LO phase noise mixes with nearby strong signals
→ Synthesizer phase noise degrades close-in signal quality
Microphonics:
→ Oscillator frequency varies with mechanical vibration
→ Classic problem in VFOs — physical shock changes the LC values slightly
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: OCXO vs TCXO: OCXO is better (orders of magnitude more stable) but draws more power and takes time to warm up. TCXO is a compromise — good stability without the warmup time.

## Slide 21
Key Numbers — Module 5
Class A conduction | 360° (full cycle); lowest distortion
Class C for SSB | NOT suitable — distorts the signal
Class D | Switching; >90% efficiency; needs output filter
Flip-flop divides by | 2 (each stage); 4 stages = ÷16
Astable multivibrator | Continuously oscillates; no external clock
NAND output = 0 when | ALL inputs are 1
XOR output = 1 when | Inputs DIFFER
Butterworth filter | Flat passband; no ripple
Chebyshev filter | Ripple in passband; sharper cutoff
Elliptical filter | Ripple in both bands; steepest transition
Balanced modulator output | DSB suppressed carrier (no carrier)
Product detector function | Demodulates SSB
Nyquist rate | Sample ≥ 2× highest signal frequency
ADC dynamic range | ~6 dB per bit
Inverting op-amp gain | -(Rf/Rin)
Non-inverting op-amp gain | 1 + (Rf/Rin)
Colpitts feedback | Capacitive voltage divider
PLL function | VCO locked to crystal reference
DDS | Digital lookup table + DAC; fine frequency resolution
TavaOne Education — Amateur Extra
E7 · Practical Circuits
Notes: Cover the right side. Say the answer. 2 minutes.

## Slide 22
Checkpoint Quiz 1 / 10
How many flip-flops are needed to divide a frequency by 16?
A. 2
B. 4
C. 8
D. 16
Answer: B — Each flip-flop divides by 2; 2⁴=16; need 4 stages
Notes: 2^4 = 16. Count the 2: 2, 4, 8, 16. That's 4 flip-flops.

## Slide 23
Checkpoint Quiz 2 / 10
Which amplifier class is NOT suitable for SSB?
A. Class A
B. Class AB
C. Class C
D. Class B
Answer: C — Class C conducts <180°; distorts SSB (signal distortion and excessive bandwidth)
Notes: Class C clips the waveform — fine for CW and FM (constant amplitude) but destroys SSB information.

## Slide 24
Checkpoint Quiz 3 / 10
What type of filter has ripple in both passband and stopband?
A. Butterworth
B. Bessel
C. Chebyshev
D. Elliptical
Answer: D — Elliptical (Cauer): ripple in BOTH passband and stopband; steepest transition
Notes: Butterworth = no ripple. Chebyshev = passband ripple only. Elliptical = both. Steepest transition = elliptical.

## Slide 25
Checkpoint Quiz 4 / 10
What does a balanced modulator produce?
A. AM with full carrier
B. FM signal
C. DSB with suppressed carrier
D. SSB with pilot carrier
Answer: C — Balanced modulator cancels the carrier; produces Double Sideband Suppressed Carrier
Notes: It multiplies audio times carrier. When they're equal and opposite, the carrier terms cancel. Only sidebands remain.

## Slide 26
Checkpoint Quiz 5 / 10
What is the dynamic range per bit in an ADC?
A. 3 dB
B. 6 dB
C. 12 dB
D. 20 dB
Answer: B — Approximately 6 dB per bit (more precisely 6.02 dB)
Notes: 16-bit ADC: 16 × 6 = 96 dB dynamic range. 12-bit: 72 dB. This is a direct exam question.

## Slide 27
Checkpoint Quiz 6 / 10
What is the gain of an inverting op-amp with Rin=2.2kΩ and Rf=22kΩ?
A. +10
B. -10
C. +11
D. -11
Answer: B — Gain = -(Rf/Rin) = -(22k/2.2k) = -10
Notes: Rf over Rin: 22k/2.2k = 10. Inverting, so negative: -10.

## Slide 28
Checkpoint Quiz 7 / 10
What is the gain of a non-inverting op-amp with Rin=1kΩ and Rf=4.7kΩ?
A. 4.7
B. -4.7
C. 5.7
D. -5.7
Answer: C — Gain = 1 + (Rf/Rin) = 1 + (4.7k/1k) = 5.7
Notes: Non-inverting: add 1. 4.7k/1k = 4.7, then +1 = 5.7. Positive because non-inverting.

## Slide 29
Checkpoint Quiz 8 / 10
A Colpitts oscillator uses which type of feedback network?
A. Tapped inductor
B. Capacitive voltage divider
C. Crystal
D. Phase-shift network
Answer: B — Colpitts: two capacitors form a voltage divider; the junction provides feedback
Notes: Colpitts = capacitive divider. Hartley = tapped (inductive) divider. Remember: C = Capacitors.

## Slide 30
Checkpoint Quiz 9 / 10
What is the main advantage of a PLL synthesizer over a free-running VFO?
A. Wider tuning range
B. Simpler circuit
C. Frequency stability referenced to a crystal
D. Lower phase noise
Answer: C — PLL locks the VCO to a crystal reference; gives crystal stability across the tuning range
Notes: The VCO can drift, but the PLL error correction keeps pulling it back to the exact frequency the crystal demands.

## Slide 31
Checkpoint Quiz 10 / 10
An astable multivibrator is best described as:
A. A circuit that toggles when triggered
B. A circuit that continuously alternates between two states without external triggering
C. A frequency divider
D. A bistable memory element
Answer: B — Astable: no stable state; generates its own square wave continuously
Notes: Mono = one stable state. Bi = two stable states (flip-flop). Astable = NO stable states; runs free.

## Slide 32
Before Module 6
Your assignment:
Drill HamStudy E7A-E7H to 80%+ confidence — this subelement takes the most time
Practice the two op-amp gain formulas until they're automatic
Know all three filter names and their passband/stopband ripple behavior
Coming up:
Module 6: Signals, Emissions & Safety — only 5 questions but includes formulas (Carson's rule, RMS voltage, modulation index). Good recovery module after this one.
Notes: Wrap up and send students to HamStudy.