## Slide 1
Module 6: Signals, Emissions & Safety
Fourier Analysis · Modulation · Digital Signals · Spread Spectrum · RF Safety
2024-2028 Amateur Extra Question Pool
TavaOne Education · Pinellas STEM Radio Lab
Notes: Module 6 opening slide.

## Slide 2
Module 6 Overview
5 exam questions — E8A-D (4 Qs) + E0A (1 Q) — only 10% of exam
Lighter module — good recovery after Module 5
But: E8 has real formula content
→ RMS voltage: Vrms = 0.707 × Vpeak
→ FM modulation index: peak deviation / modulating frequency
→ Carson's rule: BW = 2 × (deviation + max audio frequency)
→ Baud rate vs bit rate relationship
E0A safety: only 1 question but a guaranteed point
→ Know: MPE limits, duty cycle, BeO hazard, controlled vs uncontrolled
TavaOne Education — Amateur Extra
E8-E0 · Signals & Safety
Notes: This is the easier half of the course. We've done the hardest work. Module 6 consolidates signal theory you already know from operating FT8 and other digital modes — now you'll understand why they work.

## Slide 3
Part 1: Fourier Analysis and Power
Subelement E8A — 1 exam question
Notes: Fourier analysis is the mathematical tool that explains why every waveform can be treated as a collection of sine waves. Practical consequence: harmonics.

## Slide 4
Fourier Analysis and Harmonics
Fourier's theorem: any complex periodic waveform = fundamental + harmonics
Harmonics: integer multiples of the fundamental frequency
→ 2nd harmonic: 2× fundamental; 3rd: 3×; etc.
Square wave: fundamental + all ODD harmonics (3rd, 5th, 7th...)
→ This is why digital circuits radiate harmonics across the spectrum
→ And why switching amplifiers MUST have output low-pass filters
RMS Voltage (sine wave):
Vrms = 0.707 × Vpeak
→ Or: Vrms = Vpeak / √2
→ Example: 200V peak → 141.4V RMS
Peak Envelope Power (PEP):
PEP = (Vrms)² / Z measured at the highest amplitude point
→ For SSB: measure the peak of the modulation envelope
→ Average power < PEP for SSB
TavaOne Education — Amateur Extra
E8-E0 · Signals & Safety
Notes: Practical example: your 100W SSB transmitter puts out 100W PEP at voice peaks. The average power might be 30-40W. Legal limits are expressed in PEP. This is why an SSB transmitter rated at 100W PEP isn't running 100W continuously.

## Slide 5
Part 2: FM Modulation
Subelement E8B — 1 exam question
Notes: FM modulation is fundamentally different from AM — it encodes audio in frequency, not amplitude. The modulation index tells you how much the frequency varies.

## Slide 6
FM Modulation Index and Carson's Rule
Modulation index: peak frequency deviation / modulating frequency
→ Example: 5 kHz deviation, 1 kHz audio → index = 5
→ Higher index = more sidebands = more bandwidth
Deviation ratio: max frequency deviation / max modulating frequency
→ Design parameter (uses maximum values, not instantaneous)
Carson's Rule — FM bandwidth:
BW = 2 × (max deviation + max modulating frequency)
→ Example: 5 kHz deviation, 3 kHz audio → BW = 2×(5+3) = 16 kHz
→ This gives the bandwidth containing ~98% of the signal power
Frequency-Division Multiplexing (FDM): signals on different subcarriers
Time-Division Multiplexing (TDM): signals share the channel in time slots
OFDM: many narrow subcarriers, each using QAM or QPSK
TavaOne Education — Amateur Extra
E8-E0 · Signals & Safety
Notes: Practice the Carson's rule formula now. If deviation is 6 kHz and audio is 2.5 kHz: BW = 2×(6+2.5) = 2×8.5 = 17 kHz. Have students work one on paper.

## Slide 7
Part 3: Digital Signal Theory
Subelement E8C — 1 exam question
Notes: The math behind digital modes — error correction, modulation schemes, and constellation diagrams.

## Slide 8
Digital Modulation and Error Correction
Shannon's theorem: maximum data rate depends on bandwidth AND signal-to-noise ratio
Forward Error Correction (FEC):
→ Adds redundant bits at the transmitter
→ Receiver can DETECT and CORRECT errors without retransmission
→ Used when retransmission is impossible: EME, broadcast, satellites
Automatic Repeat Request (ARQ):
→ Receiver detects errors and REQUESTS retransmission
→ Used when two-way links exist: Winlink, PACTOR
Baud rate vs bit rate:
→ Baud rate = symbols per second (signal state changes per second)
→ Bit rate = baud rate × bits per symbol
→ QPSK: 2 bits per symbol → 1200 baud = 2400 bps
→ 16-QAM: 4 bits per symbol → 1200 baud = 4800 bps
TavaOne Education — Amateur Extra
E8-E0 · Signals & Safety
Notes: FEC vs ARQ: space probes use FEC because there's no way to ask for a retransmit from Voyager. Winlink email uses ARQ because you can wait for a retry. Moon bounce uses FEC because the round-trip delay makes ARQ impractical.

## Slide 9
Modulation Schemes and Constellation Diagrams
BPSK: 2 phase states (0°, 180°) — 1 bit per symbol; most robust
QPSK: 4 phase states (0°, 90°, 180°, 270°) — 2 bits per symbol
QAM: varies both amplitude AND phase
→ 16-QAM: 4 bits per symbol (16 unique states)
→ 64-QAM: 6 bits per symbol (64 unique states — more susceptible to noise)
OFDM: many narrow subcarriers simultaneously
→ Each subcarrier uses QAM or QPSK
→ Used in DVB-T (amateur ATV), Wi-Fi, LTE
Constellation diagram:
→ Plots I (in-phase) vs Q (quadrature) — shows all possible signal states
→ Each point = one symbol (specific amplitude + phase combination)
→ Noise causes points to spread — if adjacent points overlap, bit errors occur
TavaOne Education — Amateur Extra
E8-E0 · Signals & Safety
Notes: Show a QPSK constellation: 4 points on the compass. Each point is 1 unique state. 2 bits define which point. At higher SNR you can pack 16-QAM (16 points), 64-QAM (64 points). More points = more data rate = less noise margin.

## Slide 10
Part 4: Keying Defects and Spread Spectrum
Subelement E8D — 1 exam question
Notes: Keying defects are a practical operating issue. Spread spectrum is a technology question.

## Slide 11
Keying Defects and Spread Spectrum
Keying Defects
Key clicks: rise/fall time too fast → wide sidebands
→ Sounds like 'thwack' on nearby frequencies
→ Fix: slow rise/fall times with RC shaping
Chirp: oscillator frequency changes on keying
→ Power supply voltage pulling the VFO
→ Fix: better voltage regulation
Overmodulation (digital): excessive drive
→ Splatter on adjacent frequencies
ASCII: 7-bit code (128 characters)
Baudot (RTTY): 5-bit with shift characters
Spread Spectrum
DSSS (Direct Sequence):
→ Multiply signal by pseudo-random code
→ Spreads signal across wide bandwidth
→ Looks like noise to others
FHSS (Frequency Hopping):
→ Rapidly hop between frequencies
→ Using pseudo-random sequence
Both: resistant to interference and jamming
FCC: SS only above 222 MHz in Amateur Service
TavaOne Education — Amateur Extra
E8-E0 · Signals & Safety
Notes: Key clicks are the most common source of amateur complaints to the FCC. A properly shaped keying waveform has rise and fall times of about 5ms — fast enough for good CW sending but slow enough to contain sidebands.

## Slide 12
Part 5: RF and Electrical Safety
Subelement E0A — 1 exam question
Notes: One guaranteed point if you know the basics. RF safety is also practically important for any serious amateur operator.

## Slide 13
RF Safety Fundamentals
RF biological effect: thermal — RF energy heats body tissue like a microwave oven
MPE (Maximum Permissible Exposure): FCC RF field strength limits
→ Different limits for different frequency ranges
→ Lower frequency = higher MPE (body absorbs less)
Duty cycle reduces average exposure:
→ 50% duty cycle = half the average exposure
→ Pulsed modes (SSB, WSPR) have lower duty cycle than CW or FM
Controlled environment: amateur operators who know about RF and take precautions
Uncontrolled environment: general public, neighbors — STRICTER MPE limits
→ Your neighbors are in an uncontrolled environment
→ You must meet the stricter limit at their location
EIRP-based evaluation: use actual transmitter power + antenna gain - losses
TavaOne Education — Amateur Extra
E8-E0 · Signals & Safety
Notes: Practical consequence: a big beam antenna pointed at a neighbor's house is more of a concern than an omnidirectional vertical, even at the same transmitter power. The gain concentrates the energy in one direction.

## Slide 14
Hazardous Materials and Grounding
Lead solder:
→ Toxic if ingested — wash hands after soldering
→ Use fume extraction or solder outdoors — don't breathe solder fumes
Beryllium oxide (BeO):
→ Found in some old RF power transistors and magnetrons
→ Appears as white ceramic inside some transistors
→ EXTREMELY toxic as dust — DO NOT sand, grind, or break
→ If you find old transistors with white ceramic insulator — handle with extreme care
CRT high voltage:
→ Capacitors retain lethal charge even when unplugged — discharge before working
Single-point station ground:
→ All equipment grounds meet at one point — prevents ground loops
Lightning protection:
→ Surge protectors on all coax and control lines at the single-point ground panel
→ Disconnect antennas during lightning — no protector is perfect
TavaOne Education — Amateur Extra
E8-E0 · Signals & Safety
Notes: BeO story: in the 1970s-80s, power transistors commonly used BeO as a heat spreader. A technician who filed down a transistor case without knowing got very sick. It's on the exam and it's real.

## Slide 15
Key Numbers — Module 6
RMS voltage (sine wave) | Vrms = 0.707 × Vpeak
PEP measurement | At highest amplitude point; (Vrms)²/Z
FM modulation index | Peak deviation / modulating frequency
Deviation ratio | Max deviation / max modulating frequency
Carson's rule | BW = 2×(deviation + max audio freq)
OFDM | Many narrow subcarriers; each QAM or QPSK
FEC | Error correction without retransmission
ARQ | Requests retransmission on error
Baud rate | Symbols per second
QPSK bits per symbol | 2 bits per symbol (4 phase states)
QAM | Varies both amplitude and phase
Key clicks caused by | Rise/fall time too fast
Chirp caused by | Power supply pulling VFO on keying
DSSS | Pseudo-random code spreads signal
FHSS | Pseudo-random frequency hopping
SS authorized above | 222 MHz
Controlled environment MPE | Amateur operators (aware of RF)
Uncontrolled environment MPE | General public; stricter limits
BeO hazard | Extremely toxic dust; never grind or break
Single-point ground | All station grounds at one point; prevents loops
TavaOne Education — Amateur Extra
E8-E0 · Signals & Safety
Notes: Module 6 is lighter — review this grid and move into the quiz.

## Slide 16
Checkpoint Quiz 1 / 10
What is the RMS voltage of a 200V peak sine wave?
A. 200 V
B. 141.4 V
C. 100 V
D. 282.8 V
Answer: B — Vrms = 0.707 × 200 = 141.4V
Notes: 0.707 × 200. Just memorize the 0.707 multiplier (= 1/sqrt(2)).

## Slide 17
Checkpoint Quiz 2 / 10
What is the FM modulation index with 6 kHz deviation and 2 kHz audio?
A. 12
B. 3
C. 0.33
D. 8
Answer: B — Index = deviation/audio freq = 6000/2000 = 3
Notes: Simple division: 6k/2k = 3. Higher index = more sidebands = wider signal.

## Slide 18
Checkpoint Quiz 3 / 10
Using Carson's rule, what is the bandwidth with 5 kHz deviation and 3 kHz audio?
A. 8 kHz
B. 10 kHz
C. 16 kHz
D. 6 kHz
Answer: C — BW = 2×(5+3) = 16 kHz
Notes: Add deviation + audio, then multiply by 2. (5+3)=8, ×2=16 kHz.

## Slide 19
Checkpoint Quiz 4 / 10
What do constellation diagrams display?
A. Antenna radiation patterns
B. Phase and amplitude states of a digital signal
C. Frequency vs. time
D. Modulation index vs. audio frequency
Answer: B — I vs Q plot showing all possible signal states (amplitude + phase)
Notes: Each point on the constellation is one unique symbol. QPSK has 4 points. 16-QAM has 16 points.

## Slide 20
Checkpoint Quiz 5 / 10
What is the bit rate of a 1200-baud QPSK signal?
A. 1200 bps
B. 600 bps
C. 2400 bps
D. 4800 bps
Answer: C — QPSK: 2 bits/symbol; 1200 baud × 2 = 2400 bps
Notes: Baud = symbols per second. QPSK encodes 2 bits in each symbol. Multiply: 1200 × 2 = 2400 bps.

## Slide 21
Checkpoint Quiz 6 / 10
What causes key clicks in CW transmission?
A. Excessive power
B. Oscillator chirp
C. Rise/fall time too fast
D. Antenna mismatch
Answer: C — Key clicks: keying rise/fall time too fast → wide sidebands that splatter across the band
Notes: Fast switching = wide sidebands. 5ms rise time is a good target for 15-20 wpm CW.

## Slide 22
Checkpoint Quiz 7 / 10
What is a primary advantage of spread spectrum?
A. Narrower bandwidth
B. Lower power
C. Resistance to interference and jamming
D. Better audio quality
Answer: C — Spreading signal across wide bandwidth makes it resistant to narrowband interference
Notes: From a jammer's perspective: a jammer at one frequency kills only a tiny fraction of the spread signal's power.

## Slide 23
Checkpoint Quiz 8 / 10
FEC allows the receiver to do what that ARQ cannot?
A. Increase data rate
B. Detect and correct errors without requesting retransmission
C. Compress the signal
D. Synchronize clock automatically
Answer: B — FEC corrects errors without asking for a retransmit; ARQ must request retransmission
Notes: When the other station is 240,000 miles away on the Moon, waiting for an ARQ retransmit is not practical.

## Slide 24
Checkpoint Quiz 9 / 10
What material in some old RF transistors requires extreme caution to avoid creating dust?
A. Lead solder
B. Silicon dioxide
C. Beryllium oxide (BeO)
D. Tin plating
Answer: C — BeO dust is extremely toxic; never sand, grind, or break components containing it
Notes: BeO looks like white ceramic. Old high-power transistors often used it as a heat spreader. The 'do not grind' warning is on the exam.

## Slide 25
Checkpoint Quiz 10 / 10
Your neighbors live near your antenna. Which MPE environment applies at their location?
A. Controlled — they're near an amateur station
B. Uncontrolled — general public, stricter limits apply
C. No limits apply to neighboring properties
D. Controlled if they have been notified
Answer: B — Uncontrolled environment (general public) stricter MPE limits apply at all neighboring locations
Notes: Even if your neighbor knows about your station, they're still 'uncontrolled' by FCC definition — they're not the operator.

## Slide 26
Before Module 7
Your assignment:
Drill HamStudy E8A-E8D and E0A to 80%+ confidence
Practice Carson's rule and the RMS voltage formula — both appear directly on the exam
E0A safety: know BeO hazard, duty cycle effect on MPE, controlled vs uncontrolled
Coming up:
Module 7: Antennas and Transmission Lines — the final module. Real antenna math, Smith chart, transmission line theory. 8 questions tied with E7. Come with Module 3 math fresh.
Notes: Wrap up and send students to HamStudy.