## Slide 1
Module 7: Antennas & Transmission Lines
Gain · Patterns · Matching · Transmission Lines · Smith Chart · Receiving Antennas
2024-2028 Amateur Extra Question Pool — Final Module
TavaOne Education · Pinellas STEM Radio Lab
Notes: Module 7 opening slide.

## Slide 2
The Final Module
8 exam questions — all of E9 — 16% of your Extra exam
Tied with Module 5 as the heaviest module
This module has the most math — but all of it builds on Module 3
Hour 1:
→ E9A: Antenna parameters — gain, beamwidth, efficiency, ERP, EIRP
→ E9B: Radiation patterns and modeling software
→ E9C: Practical wire antennas — dipole, folded dipole, arrays, rhombic, Beverage
→ E9D: Yagi antennas and loading
Hour 2:
→ E9E: Impedance matching — quarter-wave section, stubs, matching networks
→ E9F: Transmission lines — coax vs. ladder line, velocity factor, line behavior
→ E9G: The Smith chart
→ E9H: Receiving antennas — loop, Beverage, active
TavaOne Education — Amateur Extra
E9 · Antennas & Transmission Lines
Notes: After this module: VE exam. You're on the final lap. The Smith chart intimidates most students but it's just a graph — work the practice problems and it clicks.

## Slide 3
Part 1: Antenna Parameters
Subelement E9A — 1 exam question
Notes: Gain, efficiency, ERP, EIRP — these are the quantities that define how well an antenna works.

## Slide 4
Antenna Gain and Related Quantities
Radiation resistance: equivalent resistance that would dissipate same power as antenna radiates
→ Half-wave dipole in free space: ~73 ohms
→ Quarter-wave vertical over perfect ground: ~35 ohms
Antenna gain references:
→ dBi: gain over a theoretical isotropic radiator (perfect omnidirectional)
→ dBd: gain over a half-wave dipole
→ Conversion: dBi = dBd + 2.15
ERP (Effective Radiated Power): TX power × antenna gain over a dipole
EIRP (Effective Isotropic Radiated Power): ERP + 2.15 dB (over isotropic)
Antenna efficiency = Rradiation / (Rradiation + Rloss)
Beamwidth: angle between -3 dB points on main lobe — narrower = higher gain
TavaOne Education — Amateur Extra
E9 · Antennas & Transmission Lines
Notes: The 2.15 dB difference between dBi and dBd is because a dipole has 2.15 dBi of gain over an isotropic. A Yagi rated '10 dBd' is '12.15 dBi.' The exam sometimes gives one and asks for the other.

## Slide 5
Part 2: Patterns and Practical Antennas
Subelements E9B-D — 1 exam question
Notes: Antenna patterns, practical wire antennas, and Yagi design — practical knowledge for the operating amateur.

## Slide 6
Radiation Patterns and Modeling
Azimuth pattern: antenna radiation in the horizontal plane (viewed from above)
Elevation pattern: antenna radiation in the vertical plane (side view)
Main lobe: direction of maximum radiation
Side lobes: unwanted radiation in other directions
Nulls: directions of minimum radiation — useful for null-steering
Front-to-back ratio: gain of main lobe vs. gain directly behind
Antenna modeling software:
→ NEC (Numerical Electromagnetics Code): industry-standard engine
→ EZNEC and 4NEC2: graphical NEC interfaces for amateurs
→ Models free-space patterns; real-world affected by ground and nearby structures
TavaOne Education — Amateur Extra
E9 · Antennas & Transmission Lines
Notes: Null steering is a practical DXing skill: if a station is interfering with your target DX and they're 90 degrees apart, a directional antenna can null the interferer while maintaining gain on the DX. The modeling software lets you predict this before building.

## Slide 7
Practical Wire Antennas (E9C)
Half-wave dipole: ~73-ohm feed impedance in free space; classic reference antenna
Folded dipole: ~300-ohm impedance (4× regular dipole)
→ More bandwidth; common as Yagi driven element fed through balun
Rhombic: diamond-shaped terminated long-wire; very high gain; wide bandwidth
→ Needs large lot; used for point-to-point HF links
Beverage: long wire (1+ wavelength) close to ground, terminated
→ RECEIVING ONLY; traveling-wave; directional; excellent low-noise on 160/80m
Ground effects on antennas:
→ Low dipole: high angle NVIS for regional communication
→ High dipole (>0.5λ): low-angle radiation; better for DX
Chordal hop (covered in Module 2) benefits from lower elevation angle = longer hops
TavaOne Education — Amateur Extra
E9 · Antennas & Transmission Lines
Notes: The Beverage antenna is a favorite of serious 160m DXers — a 500-foot wire stretched through the woods pointed at Europe, terminating in a 600-ohm resistor. It hears weak signals that a transmitting antenna misses due to high noise level.

## Slide 8
Yagi Antennas and Loading (E9D)
Yagi elements:
→ Driven element: connected to feed line (approximately half-wave)
→ Director: shorter than driven; placed IN FRONT → adds gain, narrows beam
→ Reflector: longer than driven; placed BEHIND → increases front-to-back ratio
More elements = more gain + narrower beamwidth
Feed point impedance reduced by nearby directors and reflectors
Common matching methods: gamma match, T-match, hairpin match
Parabolic dish: very high gain at microwave; feed at focal point
Electrically short antennas and loading:
→ Loading coil adds inductance to bring short antenna to resonance
→ High-Q coil: narrow bandwidth, high efficiency
→ Antenna Q: high Q = narrow bandwidth
→ Vertical ground system: radial wires improve radiation resistance
TavaOne Education — Amateur Extra
E9 · Antennas & Transmission Lines
Notes: Common exam question: which direction is the director? It's in front of the antenna, toward the desired direction. Remember: directors direct the signal. Reflectors reflect it back. The reflector is behind you, like a mirror.

## Slide 9
Part 3: Impedance Matching
Subelement E9E — 1 exam question
Notes: Impedance matching is how you transfer maximum power between the transmitter, feed line, and antenna. The quarter-wave formula is directly tested.

## Slide 10
Quarter-Wave Matching and Stubs
Quarter-wave matching section:
Z_match = sqrt(Z1 × Z2)
→ A quarter-wave section with this impedance transforms Z1 to Z2
→ Example: match 200Ω antenna to 50Ω coax:
Z = sqrt(200 × 50) = sqrt(10,000) = 100Ω
→ Use 100Ω coax (two 50Ω lines in series, or 75Ω for approximation)
Stub matching:
→ Open or shorted transmission line sections added in parallel at feed point
→ Used to cancel reactive component
→ Shorted quarter-wave stub: appears as open circuit (high impedance) at input
→ Open quarter-wave stub: appears as short circuit at input
Wilkinson power divider: equal-power split between two outputs at 50Ω
TavaOne Education — Amateur Extra
E9 · Antennas & Transmission Lines
Notes: Work the example on the board: sqrt(200 × 50). First: 200 × 50 = 10,000. Then: sqrt(10,000) = 100. The exam gives you numbers that work out cleanly — they pick the numbers to make the math convenient.

## Slide 11
Part 4: Transmission Lines
Subelement E9F — 1 exam question
Notes: Transmission line behavior is counterintuitive but follows exact mathematical rules. The quarter-wave inversion rule is a guaranteed exam topic.

## Slide 12
Transmission Line Properties
Velocity factor (VF): ratio of signal speed in line to speed of light
→ Always less than 1 — signal is slower in the dielectric
→ Typical values: coax 0.66-0.78; ladder line 0.91-0.95
Electrical length = physical length × velocity factor
→ Free-space quarter wave at 7 MHz = 10.7m
→ In RG-8 coax (VF=0.66): physical length = 10.7 × 0.66 = 7.1m
Quarter-wave line behavior (the inversion rule):
→ Open circuit at far end → appears as SHORT CIRCUIT at input
→ Short circuit at far end → appears as OPEN CIRCUIT at input
Open-wire (ladder line): lower loss than coax but balanced; needs balun
Microstrip: controlled-impedance PCB transmission line
Standing waves: result from impedance mismatch; high SWR = more feed line loss
TavaOne Education — Amateur Extra
E9 · Antennas & Transmission Lines
Notes: The quarter-wave inversion is the most exam-tested transmission line concept. Ask: what does a quarter-wave shorted stub look like at its input? Open circuit — very high impedance. This is used to build VHF/UHF traps.

## Slide 13
Part 5: The Smith Chart
Subelement E9G — 1 exam question
Notes: The Smith chart intimidates students but once you understand the layout it becomes intuitive. Focus on what each region and key point represents.

## Slide 14
Smith Chart Layout and Reading
The Smith chart is a graphical tool for transmission line and impedance matching problems
Key points:
→ CENTER: Z0 = perfect match (SWR 1:1) — normalized value 1.0 + j0
→ RIGHT SIDE: infinite impedance (open circuit)
→ LEFT SIDE: zero impedance (short circuit)
→ UPPER HALF: inductive reactance (positive imaginary)
→ LOWER HALF: capacitive reactance (negative imaginary)
Lines on the chart:
→ Constant resistance circles: pass through right side; center is their axis
→ Constant reactance arcs: curved lines from right side
→ SWR circles: concentric circles centered on Z0
All impedances normalized: divide by Z0 before plotting, multiply after
TavaOne Education — Amateur Extra
E9 · Antennas & Transmission Lines
Notes: Draw the Smith chart on the board with just the key points labeled: center (match), right (open), left (short), top (inductive), bottom (capacitive). That plus the SWR circles and resistance circles is what the exam tests.

## Slide 15
Using the Smith Chart
Moving along a transmission line:
→ Moving TOWARD GENERATOR: rotate CLOCKWISE
→ Moving TOWARD LOAD: rotate COUNTERCLOCKWISE
→ One complete revolution = one half wavelength along the line
SWR circles: all points on a circle have the same SWR
→ Center = SWR 1:1; larger circles = higher SWR
Converting impedance to admittance:
→ Move 180° around the chart (opposite side of same SWR circle)
Reading a point: find R and X from the constant circles/arcs,
then denormalize: Z = (R + jX) × Z0
Practical use: designing a stub matching network, finding SWR at any point on a line
TavaOne Education — Amateur Extra
E9 · Antennas & Transmission Lines
Notes: The clockwise-toward-generator rule makes sense physically: as you move toward the generator, you move away from the load. A clockwise rotation on the chart corresponds to moving one wavelength / 360 degrees of phase around one revolution.

## Slide 16
Part 6: Receiving Antennas
Subelement E9H — 1 exam question
Notes: Receiving-only antennas are optimized for low noise, not transmitting efficiency. They work on completely different principles.

## Slide 17
Receiving Antennas
Small loop antenna:
→ Figure-8 pattern with deep nulls at right angles to the loop plane
→ Used for Radio Direction Finding (RDF) — null points toward source
→ Excellent for noise reduction by steering nulls at interference
Beverage antenna:
→ Traveling-wave antenna — 1+ wavelengths long; close to ground; terminated
→ Pattern: cardioid (unidirectional) toward the terminated end
→ Very low noise floor — excellent for 160m and 80m DX receiving
→ Typical length: 500-1000 feet; terminated in 600-800 ohms
Active receiving antenna:
→ Small antenna element + low-noise preamplifier
→ Overcomes the impedance/size mismatch of a very small antenna
→ Useful where a full-size antenna is not practical
RDF (Radio Direction Finding):
→ Doppler systems: simulate antenna rotation for bearing
→ Useful for fox hunts and interference source location
TavaOne Education — Amateur Extra
E9 · Antennas & Transmission Lines
Notes: The Beverage and the small loop both work by being bad transmitting antennas — low radiation resistance, inefficient. But that's fine because efficiency doesn't matter for receive-only use. What matters is noise — and they're both quiet.

## Slide 18
Key Numbers — Module 7
dBi = dBd + | 2.15
Dipole feed impedance | ~73 ohms in free space
Folded dipole impedance | ~300 ohms (4× dipole)
Quarter-wave match formula | Z = sqrt(Z1 × Z2)
Match 200Ω to 50Ω | sqrt(200×50) = 100Ω section
Open end of 1/4-wave line | Short circuit at input
Shorted end of 1/4-wave line | Open circuit at input
Velocity factor | Always <1; signal slower in dielectric
Electrical length | Physical length × velocity factor
Ladder line VF typical | 0.91-0.95
Coax VF typical | 0.66-0.78
Smith chart center | Perfect match; SWR 1:1
Smith chart right side | Open circuit
Smith chart left side | Short circuit
Smith chart upper half | Inductive reactance
Smith chart toward generator | Clockwise rotation
Smith chart admittance | Move 180° around chart
Yagi director | Shorter; in front; increases gain
Yagi reflector | Longer; behind; increases F/B ratio
Beverage antenna | Receive-only; low noise; 160/80m DX
Small loop pattern | Figure-8; deep nulls perpendicular to loop
Antenna efficiency | Rrad / (Rrad + Rloss)
TavaOne Education — Amateur Extra
E9 · Antennas & Transmission Lines
Notes: Final review before the quiz. Cover the right column.

## Slide 19
Checkpoint Quiz 1 / 10
What is the impedance of a quarter-wave matching section to match 25Ω to 100Ω?
A. 62.5Ω
B. 75Ω
C. 50Ω
D. 125Ω
Answer: C — Z = sqrt(25 × 100) = sqrt(2500) = 50Ω
Notes: sqrt(25 × 100) = sqrt(2500) = 50. Classic 3-4-5 variant.

## Slide 20
Checkpoint Quiz 2 / 10
How does dBi relate to dBd?
A. dBd = dBi + 2.15
B. dBi = dBd + 2.15
C. dBi = dBd - 2.15
D. They are equal
Answer: B — dBi = dBd + 2.15
Notes: A dipole has 2.15 dBi of gain over isotropic. So any antenna's dBi is always 2.15 more than its dBd.

## Slide 21
Checkpoint Quiz 3 / 10
What is the input impedance of a quarter-wave line with an open circuit at the far end?
A. Open circuit
B. Z0
C. Short circuit
D. 2 × Z0
Answer: C — Quarter-wave open end appears as a SHORT CIRCUIT at the input
Notes: The quarter-wave line inverts. Open becomes short. Short becomes open. This is fundamental and always tested.

## Slide 22
Checkpoint Quiz 4 / 10
A Beverage antenna is best suited for:
A. High-gain transmitting on 10m
B. VHF direction finding
C. Low-noise receiving on 160m and 80m
D. Wide bandwidth transmitting
Answer: C — Beverage: receive-only, traveling-wave, low noise floor; ideal for 160/80m DX receiving
Notes: Beverage antennas are inefficient transmitters but excellent low-noise receivers. 160m DXers use them to hear signals they couldn't otherwise detect.

## Slide 23
Checkpoint Quiz 5 / 10
What does the center of a Smith chart represent?
A. Open circuit
B. Short circuit
C. Purely reactive impedance
D. Perfect match (SWR 1:1)
Answer: D — Center = Z0 normalized to 1+j0; perfect match; SWR 1:1
Notes: Dead center = matched. Right edge = open. Left edge = short. All other points are somewhere between.

## Slide 24
Checkpoint Quiz 6 / 10
What is the approximate feed impedance of a folded dipole?
A. 50Ω
B. 73Ω
C. 300Ω
D. 600Ω
Answer: C — Folded dipole: ~300Ω (4× the regular dipole's ~73Ω)
Notes: This impedance matches nicely to 300-ohm twin lead or through a 6:1 balun to 50-ohm coax.

## Slide 25
Checkpoint Quiz 7 / 10
A Yagi director is placed in front of the driven element and is:
A. Longer; reflects energy
B. Shorter; increases forward gain
C. The same length; provides matching
D. Variable length
Answer: B — Director: shorter than driven element; placed toward desired direction; increases forward gain
Notes: Directors direct. They're shorter and are out front. Reflectors are longer and behind. Both are parasitic (not connected to feed line).

## Slide 26
Checkpoint Quiz 8 / 10
What determines antenna efficiency?
A. SWR on the feed line
B. Ratio of radiation resistance to total resistance
C. Resonant frequency
D. Number of radials
Answer: B — Efficiency = Rrad / (Rrad + Rloss)
Notes: A loading coil with high resistance in a short antenna can waste most of the power as heat instead of radiation. That's low efficiency.

## Slide 27
Checkpoint Quiz 9 / 10
What pattern does a small loop receiving antenna produce?
A. Omnidirectional in loop plane
B. Figure-8 with nulls perpendicular to loop
C. Cardioid
D. Unidirectional toward loop opening
Answer: B — Small loop: figure-8 pattern; deep nulls perpendicular to the plane of the loop
Notes: The null is at right angles to the loop — if the loop faces north/south, the null points east/west. Rotate until signal disappears to find direction.

## Slide 28
Checkpoint Quiz 10 / 10
Moving clockwise on the Smith chart corresponds to movement in what direction on the transmission line?
A. Toward the load
B. Toward the generator
C. Increasing frequency
D. Decreasing SWR
Answer: B — Clockwise = toward generator; counterclockwise = toward load
Notes: One full revolution clockwise = moving half a wavelength toward the generator. Remember: toward Generator = clockwise (G clockwise).

## Slide 29
VE Exam — You're Ready
50 questions, 37 to pass (74%)
Bring: government-issued photo ID and your FRN number
After passing: $35 FCC fee via CORES online
License upgrades when the FCC ULS database reflects the new grant
Your call sign stays the same — you can apply for a 1×2 or 2×1 vanity later
TavaOne Education · Pinellas STEM Radio Lab · tavaoneeducation.org
Notes: Run the exam. Good luck to everyone. After the exam, collect results and file with the VEC. Walk students through checking ULS for their upgraded license.