## Slide 1
Module 3: Technical Core
Electrical Principles · Components · Schematics
2026–2030 Technician Question Pool
TavaOne Education · Pinellas STEM Radio Lab
Notes: The math module. 8 exam questions. The actual math is 4 formulas. Start by acknowledging the anxiety — then show them how simple it really is.

## Slide 2
Part 1: Electrical Principles
Subelements T5A & T5D · 2 exam questions
Notes: Ohm's Law and Power. This is the foundation.

## Slide 3
The Water Analogy
Voltage (V) = water pressure — what pushes the current
Current (I) = flow rate — how much is flowing (measured in amps)
Resistance (R) = pipe restriction — what opposes the flow (measured in ohms)
Power (P) = work being done (measured in watts)
This analogy works for every concept in this section
High pressure + wide pipe = lots of flow = lots of power
TavaOne Education — Module 3
Notes: Use the water analogy consistently. Students who get this analogy get Ohm's Law immediately.

## Slide 4
Ohm's Law: V = I × R
THE formula. Covers 3 of your 35 exam questions by itself.
Voltage = Current × Resistance
Current = Voltage ÷ Resistance (I = V/R)
Resistance = Voltage ÷ Current (R = V/I)
Example: 12V battery, 4Ω resistor → I = 12÷4 = 3 amps
Example: 2A through 50Ω → V = 2×50 = 100 volts
Cover the one you want — the other two multiply or divide
TavaOne Education — Module 3
Notes: Work 3-4 examples together. Use real numbers. Have students call out the answers. Make it a game, not a lecture.

## Slide 5
Power: P = V × I
Power in watts = Voltage × Current
Example: 13.8V × 10A = 138 watts
Also: P = I²×R (but V×I is the one on the exam)
A 100W radio at 13.8V draws about 7.2 amps
This tells you what size power supply and fuse you need
Real-world application: that's why your radio comes with a 15A power cord
TavaOne Education — Module 3
Notes: Connect to real equipment. Their 13.8V power supply × the current their radio draws = the watts they're running.

## Slide 6
AC vs. DC
DC = direct current — flows one direction (batteries, most radio circuits)
AC = alternating current — flows back and forth (wall outlet = 60 Hz)
Radio signals are AC — they alternate at the transmit frequency
Frequency = cycles per second (hertz)
Period = time for one complete cycle (1/frequency)
60 Hz AC = the current reverses direction 120 times per second
TavaOne Education — Module 3
Notes: AC vs DC is straightforward. The key exam concept: radio signals ARE alternating current at very high frequencies.

## Slide 7
Part 2: The Math
Subelement T5B · 1 exam question
Notes: Metric prefixes and decibels. Simpler than it sounds.

## Slide 8
Metric Prefixes
Giga (G) = 1 billion — 1 GHz = 1,000 MHz
Mega (M) = 1 million — 7.2 MHz = 7,200,000 Hz
Kilo (k) = 1 thousand — 1 kΩ = 1,000 Ω
Milli (m) = 1/1,000 — 500 mW = 0.5 W
Micro (μ) = 1/1,000,000 — 100 μF
Pico (p) = 1/1,000,000,000,000 — tiny capacitors
Just move the decimal point — multiply or divide by 1,000 each step
TavaOne Education — Module 3
Notes: Practice conversions as a group: 7200 kHz to MHz, 500 mW to W, 1.5 MHz to Hz. The exam tests this with real numbers.

## Slide 9
Decibels — Three Facts
Decibels (dB) measure power ratios, not absolute power
+3 dB = power DOUBLES
-3 dB = power HALVES
+10 dB = power × 10
That's it. That's all the dB math on the exam.
Example: 5W + 3 dB = 10W. 5W + 10 dB = 50W.
Example: 5W + 3 + 3 = 20W (doubled twice)
TavaOne Education — Module 3
Notes: Students expect dB to be complicated. Show them it's literally three facts. Work 2-3 examples. Their relief will be visible.

## Slide 10
Part 3: Capacitance & Impedance
Subelement T5C · 1 exam question
Notes: Energy storage components and impedance.

## Slide 11
Capacitors, Inductors, Impedance
Capacitor: stores energy in an electric field (water tank)
Inductor: stores energy in a magnetic field (flywheel)
Impedance: total opposition to AC current (resistance + reactance)
Impedance is measured in ohms — just like resistance
Standard amateur impedance: 50 ohms (everything matches to 50Ω)
Resonance: when L and C cancel each other → minimum impedance
Resonant circuits are how antennas and filters are tuned
TavaOne Education — Module 3
Notes: 50 ohms is the magic number. Radio = 50Ω, coax = 50Ω, antenna = ideally 50Ω. Mismatch = reflected power = bad SWR.

## Slide 12
Part 4: Components
Subelements T6A & T6B · 2 exam questions
Notes: The parts inside your radio.

## Slide 13
Passive Components
Resistors & Capacitors
Resistor: opposes current flow (zigzag symbol)
Fixed or variable (potentiometer = volume knob)
Capacitor: stores energy in electric field (|| symbol)
Fixed or variable (tuning circuits)
Fuse: melts to break circuit (overcurrent protection)
Battery: series = more voltage; parallel = more capacity
Inductors & Semiconductors
Inductor/choke: stores energy in magnetic field (coil symbol)
Blocks AC, passes DC — used as filters
Diode: one-way valve for current (triangle→line)
LED = diode that emits light
Transistor: electronic switch/amplifier
Gain = amplification factor
TavaOne Education — Module 3
Notes: Focus on what each component DOES, not the physics of how. Students need to match name→function→symbol.

## Slide 14
Part 5: Schematics
Subelements T6C & T6D · 2 exam questions
Notes: Reading circuit diagrams and component functions.

## Slide 15
Schematic Symbol Recognition
Resistor → zigzag line
Capacitor → two parallel lines
Inductor → coiled line
Diode → triangle pointing to a line
Transistor → three terminals with arrow
Battery → long/short parallel lines (long = positive)
Ground → downward triangle/lines
Antenna → vertical line with horizontal lines
Switch → gap in a line
Know these cold — symbol matching is guaranteed on the exam
TavaOne Education — Module 3
Notes: Flash through symbols rapidly. Do a drill: show the symbol, students shout the component name.

## Slide 16
Component Functions
Rectifier — converts AC to DC (made from diodes)
Voltage regulator — steady output voltage regardless of input
Relay — small signal controls a large current switch
Transformer — changes AC voltage (step up or step down)
Resonant circuit — tuned to specific frequencies (L+C)
Integrated circuit (IC) — thousands of components in one chip
These are 'what does X do' exam questions — pure definitions
TavaOne Education — Module 3
Notes: Each of these is a straightforward 'what does this do' question. Definitions, not math.

## Slide 17
Key Numbers for the Exam
Formulas & Math
V = I × R (Ohm's Law)
P = V × I (Power)
Wavelength = 300 ÷ MHz (from Module 2)
+3 dB = double power
+10 dB = 10× power
Standard impedance: 50 ohms
Metric: k=1000, M=1million, m=1/1000
Components
Capacitor: electric field storage
Inductor: magnetic field storage
Diode: one-way current valve
Transistor: switch/amplifier
Rectifier: AC → DC
Transformer: changes AC voltage
LED: diode that emits light
TavaOne Education — Module 3
Notes: These are free points if memorized.

## Slide 18
Checkpoint Quiz
10 questions from T5, T6
Notes: Quiz time.

## Slide 19
Checkpoint Quiz
Q1
What formula calculates voltage from current and resistance?
A. V = I ÷ R
B. V = R ÷ I
C. V = I × R
D. V = I² × R
Notes: C. V = I × R.

## Slide 20
Checkpoint Quiz
Q2
What is the current through a 100-ohm resistor connected across 200 volts?
A. 0.5 amps
B. 2 amps
C. 20 amps
D. 200 amps
Notes: B. I = 200÷100 = 2 amps.

## Slide 21
Checkpoint Quiz
Q3
How much power is delivered by 13.8 volts at 10 amperes?
A. 0.72 watts
B. 23.8 watts
C. 138 watts
D. 1380 watts
Notes: C. P = 13.8 × 10 = 138W.

## Slide 22
Checkpoint Quiz
Q4
What does +3 dB represent?
A. Power is tripled
B. Power is doubled
C. Power is halved
D. Power × 10
Notes: B. +3 dB = double power.

## Slide 23
Checkpoint Quiz
Q5
What component stores energy in an electric field?
A. Resistor
B. Capacitor
C. Inductor
D. Transformer
Notes: B. Capacitor.

## Slide 24
Checkpoint Quiz
Q6
What is the function of a transistor?
A. Store energy in magnetic field
B. Convert AC to DC
C. Switch or amplify signals
D. Block DC while passing AC
Notes: C.

## Slide 25
Checkpoint Quiz
Q7
What converts AC to DC?
A. Capacitor
B. Inductor
C. Rectifier
D. Transformer
Notes: C. Rectifier.

## Slide 26
Checkpoint Quiz
Q8
Standard impedance of amateur radio systems?
A. 8 ohms
B. 50 ohms
C. 75 ohms
D. 300 ohms
Notes: B. 50 ohms.

## Slide 27
Checkpoint Quiz
Q9
What is 1,500,000 hertz in megahertz?
A. 0.15
B. 1.5
C. 15
D. 150
Notes: B. 1.5 MHz.

## Slide 28
Checkpoint Quiz
Q10
What schematic symbol represents a diode?
A. Zigzag line
B. Two parallel lines
C. Triangle pointing to a line
D. Coiled line
Notes: C.

## Slide 29
Before Next Session
Assignment for Module 4

## Slide 30
Your Assignment
Drill HamStudy: T5A–T5D, T6A–T6D to 80%+
Practice the Ohm's Law calculations until they're automatic
Coming in Module 4: Signals, Antennas & Safety
→ Station equipment and SWR
→ Digital modes: FT8, APRS, Winlink, DMR
→ Antenna types: dipole, vertical, Yagi
→ Feed lines and connectors
→ Electrical and RF safety
The hard part is behind you — Module 4 is concrete and visual
TavaOne Education — Module 3
Notes: Reassure them: the math is done. Module 4 is hands-on and visual.