## Slide 1
TavaOne Education
General License Course · 2023–2027 Pool
Module 1
Rules & License Upgrade
General License Course · G1 · 5 Exam Questions
Notes: Welcome to Module 1. This module covers all five G1 subelement groups: HF frequency privileges, antenna/identification rules, international operations, the VE program, and control operator/remote rules. 5 of the 35 exam questions come from G1.

## Slide 2
Hour 1
Your Upgrade, Your New Privileges
Notes: First hour covers what changes when you upgrade from Technician to General, then dives into G1A (HF privileges) and G1B (antennas and ID rules).

## Slide 3
What Upgrading to General Unlocks
Technician → you had VHF/UHF + tiny HF slices (10m phone, small CW slivers)
General → major portions of EVERY HF band
80m: ragchews, traffic nets, NVIS regional comms
40m: the workhorse band — reliable day and night, domestic and DX
20m: the "gentleman's band" — DX most of the day, most of the solar cycle
17m, 15m, 12m, 10m: killer bands near solar maximum
6m: sporadic-E, linked repeaters, EME if you're ambitious
HF portable: POTA, SOTA, ARRL Field Day on real bands
Notes: Key talking point: the practical difference between Tech and General is massive. Tech is basically VHF/UHF. General opens the ionosphere. That's the whole deal with ham radio for most people.

## Slide 4
G1A — HF Band Privileges: The Big Picture
General gets large portions of each HF band — Extra gets small additional sub-bands at the low end
The Extra-exclusive segments are narrower than most people expect (25–50 kHz at the phone band bottom)
160m (1.8–2.0 MHz): General has full access — not tested heavily but know it exists
80m (3.5–4.0 MHz): General phone = 3.800–4.000 MHz; Extra extends down to 3.525 for CW
40m (7.0–7.3 MHz): General phone = 7.175–7.300 MHz; Extra CW down to 7.025
30m (10.1–10.15 MHz): CW and digital only — NO phone. 200W PEP max.
20m (14.0–14.35 MHz): General phone = 14.225–14.350 MHz
17m/15m/12m/10m: General gets substantial phone sub-bands on each
Notes: The exam will ask about 60m and 30m specifically. Know: 30m = no phone, 200W. 60m = channelized, USB only, 100W ERP. These are high-probability exam questions.

## Slide 5
G1A — 60-Meter Band Rules
60m is a secondary allocation — amateur is secondary to government users
Operation is CHANNELIZED — 5 specific channels only, you cannot pick a random 60m frequency
Channel center frequencies: 5330.5, 5346.5, 5357.0, 5371.5, 5403.5 kHz
You MUST set your dial to the channel center frequency
MODE: Upper sideband (USB) only for phone — this is the ONE HF band where USB is mandatory regardless of frequency (normally LSB below 10 MHz)
POWER: 100W PEP ERP maximum (not the 1500W general limit)
CW and digital modes are also permitted on 60m — also channelized
Why channelized? Sharing the band with federal agencies requires fixed coordination
Notes: High-probability exam question: What power limit applies on 60 meters? Answer: 100W PEP ERP. And: What mode must you use for voice on 60m? Answer: USB. These specific numbers are frequently tested.

## Slide 6
G1B — PRB-1 and Antenna Rules
PRB-1 is a federal preemption rule (47 CFR 97.15)
State and local governments MUST reasonably accommodate amateur radio antennas
HOAs and municipalities cannot simply ban antennas outright
"Reasonable accommodation" = consideration of aesthetic concerns is allowed, but must not effectively prohibit amateur operation
This has been interpreted broadly by courts — General operators can cite PRB-1 when fighting HOA restrictions
Practically: your city can say "paint it to match the house" — they cannot say "no antennas, period"
FCC does NOT pre-approve antenna designs — that's a homeowner association issue
Amateur antenna structures over 200 ft require FAA notification (Part 17)
Notes: PRB-1 comes up in the exam regularly. The key concept: local zoning must reasonably accommodate, but reasonable aesthetic restrictions are allowed. The phrase "reasonably accommodate" is the exam answer phrase.

## Slide 7
G1B — Identification Rules
When You MUST ID
Every 10 minutes during a contact
At the end of a contact
When using a club call as control op
When using a phone patch or autopatch
When operating a repeater as trustee
When You Do NOT Need to ID
Within a contact (you can talk without IDing every transmission)
Brief test transmissions (if no contact is made)
Tactical call signs in emergencies (but must still ID every 10 min + end of contact)
Notes: The identification rules are the same for General as for Technician. Nothing new here. The 10-minute rule and end-of-contact rule are what the exam tests.

## Slide 8
Hour 2
Control, VE Program, and Remote Rules
Notes: Second hour: G1C (international operations), G1D (VE program), G1E (remote/auto control, miscellaneous).

## Slide 9
G1C — International Operations: CEPT and IARP
CEPT Permit: allows General and Extra class to operate in member countries without a separate license
CEPT members include most of Europe plus some others — ~45 countries total
Technician class does NOT qualify for CEPT — General is the minimum
IARP (International Amateur Radio Permit): for operation in CITEL member countries (Western Hemisphere)
General and above may use IARP; Technician cannot
Third-party traffic: US has formal agreements with about 60+ countries
If no agreement exists: you can still say hi to a foreign ham, but formal third-party messages are prohibited
FCC Form 605: used for license upgrades, renewals, address changes, vanity callsigns — not for CEPT
Notes: Exam note: the key fact is General and above = CEPT/IARP eligible. Technician = no. The third-party traffic question is often about whether the country has an agreement — you don't need to memorize which countries, just that the agreement must exist.

## Slide 10
G1D — The VE Program
VEC (Volunteer Examiner Coordinator): organization that coordinates exam sessions (ARRL, W5YI, etc.)
VE (Volunteer Examiner): individual who is accredited by a VEC to administer exams
Minimum 3 VEs required per exam session — no exceptions
GENERAL CLASS VE: can only administer Element 2 (Technician exam)
EXTRA CLASS VE: can administer Elements 2, 3, and 4 (all three written exams)
VE may NOT examine immediate family members (spouse, parent, child, sibling)
VEs may receive reimbursement for out-of-pocket expenses only — not a salary
Fraudulent exam administration → VE faces revocation of station license AND suspension of operator license
Failed exam → VE team returns the NCVEC Form 605 paperwork to the applicant
Notes: High-value exam content: General VEs can only do Element 2 — this specific limit is frequently tested. Also: minimum 3 VEs, no family members, Extra does all three. These are the specific testable facts.

## Slide 11
G1E — Remote and Automatically Controlled Stations
Remote control: operator is physically separated from the transmitter
The control operator is still responsible for the station — same rules as local operation
Automatic control: no operator present; station operates autonomously
Automatically controlled digital stations CAN relay third-party traffic
Automatically controlled stations CANNOT relay phone or image communications (unless specifically authorized)
If the control link fails: automatically controlled station must cease transmitting within 3 minutes
General is the minimum class for remote control over HF (practical, not explicit — control op privileges determine the band)
Auxiliary stations: fixed digital stations that relay communications between amateur stations
Notes: The 3-minute rule for failed control links is testable. Also: automatically controlled digital stations can relay third-party — this is the workaround for Winlink gateways and similar systems.

## Slide 12
Checkpoint Quiz
What is the maximum power limit for amateur stations operating on the 60-meter band?
A. 100 watts PEP output
B. 1500 watts PEP output
C. 200 watts PEP output
D. 50 watts PEP output
Notes: Answer: A 100W PEP ERP on 60m. Note the question says "output" but the rule is ERP (Effective Radiated Power) — the exam pool question uses PEP output. The distinction between output and ERP rarely matters at 100W with a dipole, but know the number: 100W.

## Slide 13
Checkpoint Quiz
Which of the following privileges are available to General class control operators but NOT Technician class?
A. HF phone privileges on 40 and 20 meters
B. Full 2-meter band privileges
C. Repeater operation on 70 centimeters
D. Automatic control of digital stations
Notes: Answer: A The whole point of upgrading to General is HF phone. Technician gets 10m phone only (small slices). General gets major HF phone privileges on 40m, 20m, and more.

## Slide 14
Checkpoint Quiz
Which of these Volunteer Examiner actions is NOT permitted?
A. Administering an Element 3 exam as a General class VE
B. Reimbursement for expenses incurred preparing the exam
C. Administering an exam to an unrelated adult member of the public
D. Accreditation by a VEC
Notes: Answer: A General class VEs can only administer Element 2 (Technician). They cannot administer Element 3 (General) or Element 4 (Extra). Only Extra class VEs can do all three. This is a frequently tested fact.

## Slide 15
Checkpoint Quiz
What rule or regulation protects amateur radio operators from local zoning laws that would prohibit antenna installation?
A. PRB-1
B. CEPT Agreement
C. Part 15 of the FCC Rules
D. The Amateur Radio Parity Act
Notes: Answer: A PRB-1 (47 CFR 97.15) is the federal preemption that requires state and local governments to reasonably accommodate amateur antennas. "Reasonably accommodate" is the key phrase — they can impose reasonable aesthetic restrictions but cannot effectively prohibit amateur operation.

## Slide 16
Checkpoint Quiz
What is the minimum number of licensed amateurs required to supervise an amateur exam session?
A. Three Volunteer Examiners
B. Two Volunteer Examiners
C. One Volunteer Examiner and one VEC representative
D. One Volunteer Examiner
Notes: Answer: A Three VEs minimum. No exceptions. This is a fixed rule — the exam session cannot proceed with fewer than 3 accredited VEs present.

## Slide 17
HamStudy Assignment
Drill these sections before next module:
G1A — HF Frequency Privileges
G1B — Antenna Rules & ID
G1C — International Ops
G1D — VE Program
G1E — Remote/Auto Control
hamstudy.org
Scan the QR code to join our study group
Notes: Assign HamStudy sections G1A through G1E. Emphasize drilling the 60m rules (power, mode, channelized) and the VE program facts (General VEs = Element 2 only, minimum 3 VEs, no family). These have high exam hit rates.