## Slide 1
TavaOne Education
General License Course · 2023–2027 Pool
Module 2
Operating & Propagation
General License Course · G2 + G3 · 8 Exam Questions
Notes: Module 2 covers G2 (Operating Procedures, 5 questions) and G3 (Radio Wave Propagation, 3 questions). Total: 8 of 35 exam questions = 23%. This is where students learn how to actually get on the air and why signals go where they go.

## Slide 2
Hour 1
HF Operating Practices
Notes: First hour: G2A (phone/CW procedures), G2B (courtesy and courtesy), G2C (CW procedures), then intro to G2D/G2E (nets and digital).

## Slide 3
G2A — SSB Operating: The Basics
SSB is THE mode for HF phone — AM is rarely used (wastes power and bandwidth)
LSB (Lower Sideband) below 10 MHz: 80m, 40m use LSB by convention
USB (Upper Sideband) above 10 MHz: 20m, 17m, 15m, 12m, 10m use USB
Exception: 60m always uses USB regardless of frequency (channelized operation)
Before transmitting: listen first! Check if the frequency is in use
"QRL?" = "Is this frequency in use?" — the polite first check
If calling CQ: "CQ CQ CQ, this is W4GGJ, Whiskey Four Golf Golf Juliet, CQ and standing by"
DX station: send your call once or twice — don't monologue at the DX
Notes: The LSB/USB rule is the most-tested operating convention in G2. LSB below 10, USB above 10. 60m is always USB. Quiz them on this.

## Slide 4
G2A — Calling Frequencies by Band
80m CW calling: 3.585 MHz (approximate — varies by region)
80m/75m SSB calling: 3.940, 3.960, 3.975 MHz (regional nets vary)
40m SSB: 7.200, 7.250 MHz (General phone subband starts 7.175)
20m SSB calling: 14.225 MHz (also 14.230 SSTV, 14.300 maritime mobile)
15m: 21.300 MHz
10m SSB: 28.400 MHz; FM calling: 29.600 MHz
These are band plans (voluntary) not FCC allocations (mandatory)
Band plans tell you where people actually hang out — FCC only tells you which frequencies you're allowed to use
Notes: Distinction between band plans (voluntary conventions) and FCC allocations (legal requirements) is tested. The FCC only defines your privileges; ARRL and others create band plans to organize usage within those privileges.

## Slide 5
G2B — Operating Courtesy
Check if a frequency is in use BEFORE calling CQ — listen for a minute
"QRL?" before transmitting; wait 5–10 seconds for a response
Do NOT transmit on top of an ongoing contact — find another frequency
DX pileup operation: send your call once, wait and listen; don't repeat over and over
Working split: DX listens on one frequency, transmits on another — you transmit on the DX's listening frequency
Priority: distress (MAYDAY) > emergency traffic > other traffic
Band plans specify calling frequencies — don't rag-chew on a calling frequency (call CQ, then QSY)
Avoid operating near the band edge — dial drift and SSB sidebands extend beyond your carrier
Notes: Band edge operation is tested. In SSB, your carrier frequency is the dial reading, but the sideband extends up (USB) or down (LSB) by up to 3 kHz. So a USB dial of 14.350 would have sideband at 14.353 — outside the 14.350 edge.

## Slide 6
G2C — Q Signals You Need to Know
During a QSO
QRL — Is this frequency in use? / This frequency is in use
QRN — Static (natural noise)
QRM — Man-made interference
QSB — Fading (signal varies)
QRZ — Who is calling me?
QSL — I acknowledge / I confirm
QTH — My location is...
QSY — Change to another frequency
General Operating
QRP — Low power (5W or less)
QRX — Wait / I will call you again
QRN — Troublesome static
QRO — Increase power (or high power)
QRS — Send more slowly
QRQ — Send faster
73 — Best regards
SK — End of contact (end work)
Notes: The G2 pool tests specific Q signal meanings. QRL, QRM, QRN, QSB, QSY, QSL, QTH, QRP, QRZ are all high-probability. Students often confuse QRM (man-made) and QRN (natural static).

## Slide 7
G2D — ARES and RACES
ARES (Amateur Radio Emergency Service): ARRL-affiliated volunteer organization
ARES provides emergency communications during disasters — not government-controlled
Any licensed amateur can join ARES — no special FCC registration required
RACES (Radio Amateur Civil Emergency Service): government-affiliated, activated by civil defense
RACES requires FCC registration of the station AND enrollment in the civil defense organization
Only RACES personnel may operate RACES nets when activated — non-RACES amateurs may not participate
Key distinction: ARES = ARRL volunteer, activate on your own; RACES = government-activated, requires registration
In practice: many hams are dual-registered in both organizations
Notes: ARES vs. RACES is a consistently tested G2 topic. The key distinguisher: RACES requires official government activation and registration; ARES is more flexible. Only registered RACES members can operate RACES nets.

## Slide 8
G2E — Digital Modes on HF
RTTY: radioteletype — the oldest digital mode still in use; 170 Hz shift, 45.45 baud; uses AFSK on LSB
PSK31: phase-shift keying at 31 baud; ~80 Hz wide; keyboard-to-keyboard; dial + audio offset = RF frequency
FT8: 15-second transmit/receive cycles; requires clock sync within ±1 second; 50 Hz bandwidth; can decode −20 dB signals
Winlink: email over radio; uses HF gateways; PACTOR or Ardop modems
APRS: Automatic Packet Reporting System; 1200 baud on VHF; 300 baud on HF; digipeaters relay packets
Bandwidth matters: choose a mode whose bandwidth fits within your subband allocation
PSK31 note: your dial frequency is NOT your RF frequency — add the audio tone frequency to find actual RF
FT8: you exchange grid squares and signal reports; full QSO is automated; uses WSJT-X software
Notes: The PSK31 "dial vs. actual RF" distinction is tested. The dial shows the carrier; actual RF = dial + tone offset. For FT8, the exam tests the 15-second cycle and clock synchronization requirement.

## Slide 9
Hour 2
The Ionosphere and HF Propagation
Notes: G3 covers radio wave propagation: ionospheric layers, MUF/LUF, solar indices, and band-specific propagation. 3 exam questions.

## Slide 10
G3A — The Ionosphere: Your HF Backboard
The ionosphere: layers of ionized gas 60–600 km up; ionized by solar UV and X-ray radiation
D LAYER (60–90 km): lowest; absorbs signals, especially at LF/MF/low HF; exists only during daylight; disappears at night → why 80m/40m open up after dark
E LAYER (90–140 km): supports sporadic-E (Es); unpredictable; can open 10m/6m suddenly; seasonal (summer solstice peak)
F1 LAYER (140–200 km): daytime only; merges with F2 at night
F2 LAYER (200–600 km): the DX layer; reflects signals thousands of miles; higher during solar maximum
F1+F2 merge at night into single F layer → night brings better DX on 40m/20m due to D layer disappearing
Solar maximum: more ionization → F2 layer stronger → higher bands (15m, 10m, 12m) work reliably
Solar minimum: F2 weak → upper bands often dead; 20m and lower still work
Notes: The ionospheric layer structure is the foundation of all HF propagation. Key testable facts: D layer absorbs daytime, disappears at night; F layer reflects DX; E layer sporadic. Know which layer does what.

## Slide 11
G3B — MUF, LUF, and Skip
Skip: radio wave goes up at an angle, reflects off the ionosphere, and lands at a distance — the "skip distance"
Skip zone: the area between your ground wave range and where the skip lands — nobody there hears you
MUF (Maximum Usable Frequency): highest frequency that will reflect off the ionosphere for a given path
Stay below the MUF — frequencies above it pass through and go to space
LUF (Lowest Usable Frequency): lowest frequency usable before D-layer absorption kills the signal
Your working frequency must be between LUF and MUF to get through
As MUF decreases (toward night or solar minimum): switch to a lower-frequency band
Gray line: the terminator between day and night; enhanced propagation; D layer is thin → less absorption
Notes: MUF and LUF are tested concepts in G3. Remember: above MUF = goes to space; below LUF = absorbed. The operating window is between them. Gray line propagation is also tested — the terminator creates conditions where D-layer absorption is minimal.

## Slide 12
G3C — Propagation by Band
Lower HF (160m, 80m, 40m)
160m/80m: mostly nighttime; D layer absorbs during day; reliable regional
40m: workhorse band; nighttime DX, daytime regional
NVIS (Near Vertical Incidence Skywave): 80m/40m; antenna pointing nearly straight up; covers 100–500 miles; used by emergency nets
Key: these bands are worst during peak sunlight
Upper HF (20m, 17m, 15m, 12m, 10m)
20m: most reliable DX band; works most of solar cycle
15m/12m: excellent near solar maximum; often closes near minimum
10m: spectacular when open; long dead periods near solar minimum
6m: the "magic band" — sporadic E openings; EME; meteor scatter
Key: these bands need the F2 layer strong
Notes: Band-specific propagation is tested in G3C. The main facts: lower bands = nighttime focus, NVIS for regional; upper bands = solar cycle dependent, need strong F2. NVIS is important for emergency communications on 80m and 40m.

## Slide 13
Solar Indices: SFI, A-Index, K-Index
Solar Flux Index (SFI): measures solar radio emission at 10.7cm; higher = better F-layer ionization
SFI >150: excellent conditions on 10m, 15m, 20m; expect DX
SFI <80: 10m usually dead; 15m marginal; focus on 20m and lower
A-Index: daily average geomagnetic activity (0=calm, >50=major storm); lower is better for HF
K-Index: 3-hour geomagnetic activity (0–9 scale); lower is better; updated 8 times/day
High K-index = geomagnetic storm = poor HF propagation, especially on polar paths
Best HF conditions: high SFI, low A-index, low K-index
Real-time data: DX Maps (dxmaps.com), PSKreporter, solar.tavaoneeducation.org
Notes: The exam distinguishes what each index measures. Key: SFI = solar emission quality (higher better); A/K index = geomagnetic disturbance (lower better). A student who knows these indices can actually use them to pick the right band, which is more valuable than the exam question itself.

## Slide 14
Checkpoint Quiz
Which sideband is commonly used for HF phone operation above 10 MHz?
A. Upper sideband
B. Lower sideband
C. Double sideband
D. Vestigial sideband
Notes: Answer: A USB is used above 10 MHz (20m, 17m, 15m, 12m, 10m). LSB is used below 10 MHz (40m, 80m, 160m). 60m is the exception — always USB regardless of the sub-10 MHz frequency.

## Slide 15
Checkpoint Quiz
What is the Q signal for "Is this frequency in use?"
A. QRL
B. QRM
C. QRN
D. QRZ
Notes: Answer: A QRL = "Is this frequency in use?" or "This frequency is in use." It's the polite way to check before calling CQ. QRM = man-made interference. QRN = natural static. QRZ = "Who is calling me?"

## Slide 16
Checkpoint Quiz
Which ionospheric layer is responsible for long-distance HF communication?
A. F2 layer
B. D layer
C. E layer
D. Tropospheric layer
Notes: Answer: A The F2 layer (200–600 km) reflects HF signals for long-distance DX. The D layer absorbs signals (bad). The E layer creates sporadic propagation. The troposphere handles VHF/UHF ducting, not HF skip.

## Slide 17
Checkpoint Quiz
What does the term "Maximum Usable Frequency" (MUF) describe?
A. The highest frequency that will be refracted back to Earth by the ionosphere on a given path
B. The highest frequency the transceiver can generate
C. The maximum frequency permitted by FCC on a given band
D. The frequency at which D-layer absorption is maximum
Notes: Answer: A MUF is the highest frequency that will refract (bend back) off the ionosphere for a specific propagation path. Above the MUF, signals pass through the ionosphere and are lost to space. Operating near the MUF is desirable as higher frequencies = less noise and more efficient propagation.

## Slide 18
Checkpoint Quiz
What is the primary difference between ARES and RACES?
A. RACES is activated by a civil defense organization; ARES is ARRL-affiliated and can activate independently
B. ARES requires government registration; RACES does not
C. RACES operates on VHF only; ARES operates on all bands
D. ARES is only for Extra class operators; RACES is for all classes
Notes: Answer: A ARES = ARRL volunteer, activates independently during disasters. RACES = must be officially activated by civil defense authorities, requires registration with the government civil defense organization. This distinction is consistently tested.

## Slide 19
HamStudy Assignment
Drill these sections before next module:
G2A — Phone & CW Operating
G2B — Operating Courtesy
G2C — CW Procedures
G2D — ARES & RACES
G2E — Digital Modes
G3A — Ionosphere Layers
G3B — MUF/LUF/Skip
G3C — Band Propagation
hamstudy.org · scan to join our study group
Notes: G2 and G3 together are 23% of the exam. The highest-priority facts: LSB/USB convention, QRL/QRM/QRN/QSB/QSL, ARES vs. RACES distinction, ionospheric layers (what each does), MUF concept.