## Slide 1
TavaOne Education
General License Course · 2023–2027 Pool
Module 5
Antennas, Feed Lines
& Safety
General License Course · G9 + G0 · 6 Exam Questions
Notes: Module 5 covers G9 (Antennas and Feed Lines, 4 Qs) and G0 (Electrical and RF Safety, 2 Qs) = 6 of 35 exam questions = 17%. This is the last content module before the capstone.

## Slide 2
Hour 1
HF Antennas and Feed Lines
Notes: G9A covers feed lines and SWR. G9B covers basic HF antennas. G9C covers directional antennas.

## Slide 3
G9A — SWR and Feed Lines
SWR (Standing Wave Ratio): measure of impedance mismatch between the feed line and the antenna
1:1 SWR = perfect match; all power gets to the antenna. This is the ideal.
At 2:1 SWR: ~11% of power is reflected back; about 89% reaches the antenna — acceptable
At 3:1 SWR: ~25% reflected; most transceivers fold back power above 3:1 to protect their finals
High SWR causes: impedance mismatch, damaged/wet connector, antenna not resonant, wrong feed point
SWR at the transmitter ≠ SWR at the antenna: feed line loss absorbs some of the reflected power → makes SWR look better at the radio end (but you're still losing power to heat)
Dummy load (50 ohms): produces 1:1 SWR — use for testing without transmitting into the air
Antenna tuner (ATU): matches the radio output to the feed line; SWR at the radio becomes 1:1; SWR on the feed line between tuner and antenna is unchanged
Notes: SWR fundamentals are heavily tested in G9. Key misconceptions to address: antenna tuner does NOT fix the SWR on the feed line — it makes the radio happy while potentially sending high SWR signal down a lossy feed line. Also: feed line loss makes SWR APPEAR better at the radio end.

## Slide 4
G9A — Feed Line Comparison
RG-58: small diameter coax; high loss (~3 dB/100 ft at 30 MHz); fine for short portable runs, not base station HF
RG-213: standard 50-ohm coax; moderate loss (~1.5 dB/100 ft at 30 MHz); good for most base station use
LMR-400: low-loss coax; ~0.7 dB/100 ft at 30 MHz; use for long runs or high frequencies
LMR-600/LMR-1200: even lower loss; used for VHF/UHF long runs and contest stations
450-ohm open-wire (ladder line): very low loss (<0.1 dB/100 ft); balanced; needs balanced tuner input; can work with high SWR without excessive loss
Velocity factor: how fast the signal travels relative to speed of light in free space
RG-58 VF ≈ 0.66; RG-213 VF ≈ 0.66; LMR-400 VF ≈ 0.85; 450-ohm ladder line VF ≈ 0.91
Electrical length = physical length × velocity factor; matters for phased arrays and matching stubs
Notes: Feed line comparison is tested. Know which coax is which loss level. Ladder line is important to know: it has very low loss even at high SWR, which is why it's used with doublet antennas on multiple bands through an ATU. Velocity factor appears in matching section calculations.

## Slide 5
G9A — Quarter-Wave Matching Section
Quarter-wave transformer: a section of transmission line exactly ¼ wavelength long
It transforms impedance: Z_match = √(Z₁ × Z₂)
Example: to match 50Ω coax to a 200Ω antenna — use a ¼-wave section of 100Ω line
Because: Z = √(50 × 200) = √10000 = 100Ω
Physical length of ¼-wave section = (246/f in MHz) × velocity factor
For a 14 MHz signal in 50Ω coax (VF=0.66): 246/14 × 0.66 ≈ 11.6 feet
Half-wave section: transforms impedance exactly the same as if not there; useful for putting the match point at a convenient location
End-fed half-wave (EFHW) transformer: 49:1 or 64:1 unun; transforms ~2450Ω antenna impedance to ~50Ω; works on multiple bands
Notes: Quarter-wave matching is tested in G9. The formula Z = √(Z₁ × Z₂) must be memorized. Physical length = (246/f) × VF for quarter wave. EFHW antennas are very popular in portable/POTA operation and the 49:1 ratio is a specific testable fact.

## Slide 6
G9B — HF Antenna Fundamentals
Half-wave dipole: simplest antenna; resonant; fed at center; length = 468/f(MHz) feet total
Example: 20m dipole at 14.225 MHz = 468/14.225 = 32.9 ft total (16.45 ft per side)
Height matters: higher dipole → lower takeoff angle → better DX; lower → higher angle → regional
Flat-top dipole feeds at ~70Ω (varies with height); matched reasonably well with 50Ω coax + choke balun
Inverted-V: apex up, ends down at 45°; feedpoint impedance lowers (~50Ω often); omnidirectional horizontally
EFHW (End-Fed Half-Wave): very popular for portable; 49:1 unun at feedpoint; single conductor runs to tree
EFHW works on fundamental + harmonics: 40m half-wave also resonates on 20m and 10m (even harmonics)
Fan dipole: multiple dipoles fed at the same point; each resonates on its own band; no traps needed
Notes: The dipole formula 468/f is frequently tested. Know it. EFHW and why it works on multiple bands (fundamental + harmonics) is also tested. The direction of radiation from a dipole (broadside to the wire) is a physical concept worth mentioning.

## Slide 7
G9C — Directional Antennas
Yagi Antenna
Driven element: fed directly from the coax; ½-wave dipole
Directors: shorter than driven element; placed in front (toward desired direction); one or more
Reflector: longer than driven element; placed behind; only one
More elements = more gain and narrower beamwidth
Gain in dBd (over dipole): 3-el Yagi ≈ 5 dBd; 5-el ≈ 8 dBd
dBi = dBd + 2.15 (isotropic reference = 2.15 dB below dipole)
Baluns for Antennas
1:1 choke balun: blocks common-mode current on coax shield; used at dipole and Yagi feedpoints
Without a choke balun: RF flows on coax shield → comes into shack → causes RFI
4:1 voltage balun: transforms 200Ω balanced (folded dipole) to 50Ω
4:1 current balun: used with ladder line to coax transition at ATU output
Unun: unbalanced-to-unbalanced; 49:1 for EFHW; 9:1 for end-fed random wire
Notes: Yagi element roles are tested: directors shorter, in front; reflector longer, behind. The dBd vs. dBi distinction is also tested. dBi = dBd + 2.15.

## Slide 8
G9D — Antenna Tuners
Antenna tuner (ATU, transmatch): matches the transceiver output impedance to the feed line+antenna system
What it does: presents a 50Ω match to the transceiver so the radio sends maximum power
What it does NOT do: reduce SWR on the feed line between the tuner and antenna
What it does NOT do: make a bad antenna better; a lossy antenna or lossy feed line stays lossy
What it does NOT do: protect the antenna — it protects the transceiver final
L-network: simple 2-element network; efficient; works best in specific impedance ranges
T-network: most common in commercial tuners (MFJ, LDG, etc.); wide impedance range
Pi-network: used in tube amplifiers; provides some harmonic filtering
Mobile: loading coils on short HF verticals compensate for the antenna being electrically short; efficient is ~50% at best
Notes: The ATU misconception is a very common exam question: ATU does NOT improve the antenna, does NOT reduce feed line SWR, does NOT make a bad antenna better. It only makes the radio happy. Students frequently think the ATU is magic. Make sure they know it is not.

## Slide 9
Hour 2
RF and Electrical Safety
Notes: G0 covers RF exposure (MPE, duty cycle, evaluation requirements) and electrical safety. 2 exam questions.

## Slide 10
G0A — RF Safety and MPE
RF radiation: non-ionizing; does not break chemical bonds (unlike X-rays); can cause heating at high intensities
MPE (Maximum Permissible Exposure): FCC-established limits for how much RF field strength humans may be exposed to
Two environments: Controlled (operator and people who are aware of RF, like family) vs. Uncontrolled (neighbors, passersby) — different MPE limits
Duty cycle: fraction of time transmitting during a given period; matters because RF exposure is time-averaged
FM: 100% duty cycle (carrier is always present when transmitting)
CW: ~40% duty cycle (key down/up, not continuous)
SSB: ~20% duty cycle (carrier only present during voice peaks, approximately)
FT8 and digital modes: ~100% while transmitting (continuous carrier during each 15-second burst)
Notes: G0A is only 2 exam questions but they're well-defined. Duty cycle is the most commonly tested concept: FM = 100%, SSB ≈ 20%, CW ≈ 40%. The lower duty cycle of SSB means your time-averaged exposure is less than FM at the same power level. This is why SSB at 100W is often below MPE thresholds that FM would trigger.

## Slide 11
G0A — RF Exposure Evaluation
When required: any station that exceeds power levels in Part 97.13(c)(1) must perform an RF exposure evaluation
The thresholds vary by band: e.g., HF below 30 MHz: mobile stations need evaluation if >50W PEP
Evaluation methods: use FCC OET Bulletin 65 tables, online calculators (ARRL RF Safety Calculator), or math
Variables: transmitter power, antenna gain, feed line loss, operating frequency, duty cycle, distance
Reducing exposure: increase distance (power density drops as 1/r²), reduce power, reduce duty cycle, use directional antenna (point away from people)
Near-field vs. far-field: within about 1 wavelength = near field; calculations differ; near field can be complex
Practical: most 100W HF stations with base station antennas at reasonable height are fine; document the evaluation
The FCC requires the evaluation be done — NOT that you pass some test; you evaluate and document
Notes: The exam asks about when evaluation is required and how to reduce exposure. The key variables in the calculation are transmitter power, antenna gain, frequency, duty cycle, and distance. Distance is the most effective variable to change — power drops as the square of the distance.

## Slide 12
G0B — Electrical Safety
Power supply filter capacitors: can hold lethal charge after power is removed; discharge before touching
Bleeder resistor: connected across filter capacitors; drains charge when power is off; automatic safety device
Grounding: three types in a ham station — equipment chassis ground (safety), RF ground (antenna radials), lightning protection ground
Lightning protection: gas discharge arrestors in coax provide a path to ground for direct strikes
Most important lightning protection: disconnect antennas and feed lines during storms — nothing else works as well
Power wiring: fuse at the battery/power supply, as close to the source as practical; protects the wiring
Antenna installation: never install near power lines; if antenna falls, minimum clearance = 1 wire length
Tower climbing: never climb alone; use proper harness; know emergency rescue procedures
Notes: G0B electrical safety questions focus on specific facts: capacitor discharge hazard, bleeder resistors, grounding types, lightning protection. The most important safety rule for lightning: disconnect the antennas. This is tested and the correct answer is always disconnect, not "use a surge protector."

## Slide 13
Checkpoint Quiz
What is the impedance of a quarter-wave matching section needed to match 50 ohms to 200 ohms?
A. 100 ohms
B. 150 ohms
C. 50 ohms
D. 250 ohms
Notes: Answer: A √(50 × 200) = √10000 = 100 ohms. The quarter-wave matching section formula is Z = √(Z₁ × Z₂). This gives the characteristic impedance of the matching section needed. 100-ohm coax can be made by paralleling two 50-ohm lines or using specific commercial coax types.

## Slide 14
Checkpoint Quiz
Which of the following actions does an antenna tuner (transmatch) perform?
A. It matches the transmitter output impedance to the feed line and antenna system
B. It reduces SWR on the feed line between the tuner and antenna
C. It increases antenna efficiency by canceling reactive components
D. It protects the antenna from high RF voltages
Notes: Answer: A The ATU matches the radio's 50-ohm output to whatever the feed line+antenna presents. It does NOT fix SWR on the feed line past the tuner, does NOT improve antenna efficiency, and does NOT protect the antenna. It protects the TRANSCEIVER finals from an impedance mismatch.

## Slide 15
Checkpoint Quiz
In a Yagi antenna, where are the director elements located relative to the driven element?
A. In front of the driven element, toward the desired direction of transmission
B. Behind the driven element, away from the desired direction
C. On either side of the driven element for horizontal gain
D. At 90 degrees to the driven element for circular polarization
Notes: Answer: A Directors are SHORTER than the driven element and placed IN FRONT (toward the direction you want to transmit/receive). The reflector is LONGER and placed BEHIND. Memory aid: director "directs" the signal forward; reflector "reflects" it back into the driven element from behind.

## Slide 16
Checkpoint Quiz
What is the approximate duty cycle of single-sideband voice transmissions?
A. 20%
B. 100%
C. 50%
D. 40%
Notes: Answer: A SSB ≈ 20% duty cycle because the carrier is only present during voice peaks, not continuously. FM = 100% (always full carrier). CW ≈ 40% (key down about 40% of a typical transmission). This matters for RF exposure calculations: at the same average power, SSB's time-averaged exposure is much less than FM.

## Slide 17
Checkpoint Quiz
What is the purpose of a bleeder resistor in a power supply?
A. To discharge filter capacitors when power is removed
B. To regulate the output voltage
C. To limit current to protect the rectifier diodes
D. To reduce ripple in the filter capacitor
Notes: Answer: A Bleeder resistor: connected across the filter capacitors; provides a discharge path when power is removed. Without it, caps can hold lethal voltage for minutes or hours after shutdown. The bleeder slowly drains them to a safe level. Secondary benefit: improves voltage regulation under light loads.

## Slide 18
HamStudy Assignment
Drill these sections before capstone:
G9A — Feed Lines & SWR
G9B — HF Antennas
G9C — Directional Antennas
G9D — Tuners & Special Antennas
G0A — RF Safety & MPE
G0B — Electrical Safety
hamstudy.org · scan to join our study group
Next session: Capstone — bring everything, full practice exams
Notes: G9 has 4 exam questions (most in this module) and G0 has 2. Highest priority: SWR facts (2:1 = 11% reflected), antenna tuner limitations, dipole formula (468/f), Yagi elements (directors in front, shorter), duty cycle for exposure (SSB ≈ 20%), bleeder resistors. NEXT SESSION IS CAPSTONE — full practice exams.