## Slide 1
Module 2: Operating & Propagation
Repeaters · Propagation · Station Setup
2026–2030 Technician Question Pool
TavaOne Education · Pinellas STEM Radio Lab
Notes: Welcome back. Module 2 — this is where we stop talking about rules and start talking about actually getting on the air. 8 exam questions from this module.

## Slide 2
Part 1: Station Operation Basics
Subelement T2A · 1 exam question
Notes: Getting on the air — listening, calling, repeater offsets, band plans.

## Slide 3
Before You Transmit
LISTEN FIRST — always
Then ask: 'Is this frequency in use?'
Wait for a response before transmitting
This is the most basic operating courtesy
Applies every single time you go to transmit
Skipping this step = instant bad reputation
TavaOne Education — Module 2
Notes: This is the single most important operating habit. Drill it: listen, ask, wait, then talk.

## Slide 4
Making a Call
General call (CQ): 'CQ CQ CQ, this is [your call], standing by'
Calling a specific station: '[their call], this is [your call], over'
Responding to CQ: '[their call], this is [your call], over'
Ending: '[their call], this is [your call], 73, clear'
73 = 'best regards' — the universal ham goodbye
Always end with your call sign (it's your final ID)
TavaOne Education — Module 2
Notes: Practice a CQ call as a group. Have everyone say it out loud. It feels awkward the first time — that's normal.

## Slide 5
Repeater Offsets
A repeater listens on one frequency, transmits on another
The difference = the offset
2 meters: ± 600 kHz (0.6 MHz)
70 cm: ± 5 MHz
6 meters: ± 1 MHz
Your radio applies the offset automatically
You just need to know + or – for each repeater
TavaOne Education — Module 2
Notes: The 600 kHz offset for 2m is the exam answer. 5 MHz for 70cm. Radio handles the math.

## Slide 6
Part 2: VHF/UHF Practices
Subelement T2B · 1 exam question
Notes: Repeater operation, CTCSS, DMR, Q signals.

## Slide 7
CTCSS (PL Tones)
Sub-audible tone your radio sends to 'unlock' the repeater
Without the correct tone, the repeater ignores you
Each repeater publishes its required tone
Also called PL tone (Motorola trade name)
Set it in your radio BEFORE you try to talk
Common exam question: what is CTCSS used for?
TavaOne Education — Module 2
Notes: Students will encounter this immediately when they try a real repeater. Make sure they know where to find and set the tone on their radio.

## Slide 8
DMR Basics
Digital Mobile Radio — digital voice mode
Uses time slots (2 conversations per frequency)
Uses talk groups (virtual channels)
Requires a free DMR ID from radioid.net
Color code = DMR version of a CTCSS tone — must match repeater
Growing fast — many repeaters now support DMR
TavaOne Education — Module 2
Notes: DMR is increasingly common. Students don't need to master it now but should know the vocabulary for the exam: time slots, talk groups, color codes.

## Slide 9
Q Signals
QRM — man-made interference
QRN — natural noise/static
QSY — change frequency
QSL — confirmed/acknowledged
QRZ — who is calling me?
QTH — my location is...
These are used on both phone and CW
TavaOne Education — Module 2
Notes: Go through each one. QRM vs QRN is the exam trap — M for man-made, N for natural noise.

## Slide 10
Part 3: Emergency Comms
Subelement T2C · 1 exam question
Notes: ARES, RACES, nets, and when the rules bend.

## Slide 11
ARES vs. RACES
ARES (Amateur Radio Emergency Service)
Run by ARRL (volunteer)
FCC license required
Activates anytime by Emergency Coordinator
Broader scope — any emergency
Most active emergency comms organization
RACES (Radio Amateur Civil Emergency Service)
Run by local/state civil defense (government)
FCC license AND civil defense enrollment
Only during declared emergencies
More restricted scope
Often overlaps with ARES membership
TavaOne Education — Module 2
Notes: ARES vs RACES is a common exam question. Key difference: ARES = volunteer/ARRL, RACES = government/civil defense + requires additional enrollment.

## Slide 12
Emergency Communications
In a genuine emergency: use ANY frequency needed
Normal FCC rules bend to save lives
This is explicit in Part 97 — not a gray area
Net operations: net control directs all traffic
Tactical call signs OK during emergencies (still ID every 10 min)
ARES volunteers are the backbone of ham radio public service
TavaOne Education — Module 2
Notes: The 'any frequency' rule is absolute during a genuine emergency. That's the exam answer and it's also true in practice.

## Slide 13
Part 4: Radio Waves
Subelements T3A & T3B · 2 exam questions
Notes: How radio waves work — wavelength, frequency, polarization.

## Slide 14
The Wavelength Formula
Radio waves are electromagnetic waves — travel at the speed of light
Wavelength (meters) = 300 ÷ Frequency (MHz)
146 MHz → 300 ÷ 146 ≈ 2 meters (the '2-meter band')
440 MHz → 300 ÷ 440 ≈ 0.7 m = 70 cm (the '70-cm band')
28 MHz → 300 ÷ 28 ≈ 10.7 m (the '10-meter band')
This is the ONE formula you absolutely must know
TavaOne Education — Module 2
Notes: Work through 2-3 examples as a group. Have them calculate on their phones. Make sure they can do 300 ÷ freq = wavelength.

## Slide 15
Polarization & Propagation Basics
Vertical antenna → vertically polarized wave
Horizontal antenna → horizontally polarized wave
Mismatch = significant signal loss (cross-polarization)
VHF/UHF: mostly line of sight — blocked by terrain and earth's curve
HF: bounces off the ionosphere — can travel worldwide
Multipath: VHF signals reflecting off buildings → flutter/fading
TavaOne Education — Module 2
Notes: Polarization matters practically: FM is usually vertical, HF SSB is usually horizontal. Matching polarization improves your signal.

## Slide 16
Part 5: Propagation Modes
Subelement T3C · 1 exam question
Notes: How signals travel beyond line of sight.

## Slide 17
Propagation Modes
Line of sight — VHF/UHF normal; limited by terrain and earth's curve
Ground wave — follows earth's surface; low HF, AM broadcast
Sky wave (F-layer skip) — HF bounces off ionosphere → worldwide
Sporadic E — surprise VHF skip; 6m, sometimes 2m; 1000+ miles
Tropospheric ducting — weather bends VHF/UHF; extended range
Meteor scatter — brief bounces off meteor trails; 6m, 2m
Auroral — reflects off aurora; distorted signal
TavaOne Education — Module 2
Notes: Sky wave is HF magic. Sporadic E is VHF magic. These are the exciting modes — students should know all their names for the exam and understand why they happen.

## Slide 18
Part 6: Station Setup
Subelements T4A & T4B · 2 exam questions
Notes: Controls, setup, and operating your station.

## Slide 19
Essential Station Controls
Volume — audio level (doesn't affect transmitted signal)
Squelch — mutes receiver until signal exceeds threshold
Frequency/VFO — sets your operating frequency
Offset — sets repeater offset (+ or –)
CTCSS/Tone — sets the sub-audible tone
Power — adjusts transmit power level
PTT — push to talk; hold to transmit, release to listen
AGC — automatic gain control; keeps audio levels steady
TavaOne Education — Module 2
Notes: If you have a radio in the room, demonstrate each control live. Nothing replaces hands-on.

## Slide 20
Microphone Technique
Hold 2–3 inches from mouth, slightly to the side
Normal speaking voice — don't shout into the mic
Wait a beat after pressing PTT before speaking
Keep transmissions short — say it, then unkey
Don't 'double' — wait for the courtesy tone/tail
Listen more than you talk, especially when you're new
TavaOne Education — Module 2
Notes: Bad mic technique is the #1 complaint about new operators. Get this right from day one.

## Slide 21
Key Numbers for the Exam
Operating
2m offset: ± 600 kHz
70cm offset: ± 5 MHz
2m calling: 146.520 MHz
CTCSS: sub-audible tone for repeater access
DMR color code: like CTCSS for digital
Emergency: ANY frequency allowed
QRM = man-made, QRN = natural
Propagation & Waves
Wavelength = 300 ÷ MHz
VHF/UHF: line of sight
HF: sky wave (ionosphere)
Sporadic E: surprise VHF skip
Cross-polarization = signal loss
Squelch: mutes until signal present
AGC: keeps audio levels steady
TavaOne Education — Module 2
Notes: These are the free points from this module.

## Slide 22
Checkpoint Quiz
10 questions from T2, T3, T4
Notes: Quiz time. Show each question, discuss answers as a group.

## Slide 23
Checkpoint Quiz
Q1
What is a common repeater frequency offset in the 2-meter band?
A. ± 500 kHz
B. ± 600 kHz
C. ± 1 MHz
D. ± 5 MHz
Notes: Answer: B. ± 600 kHz.

## Slide 24
Checkpoint Quiz
Q2
What is the purpose of a CTCSS or PL tone?
A. To boost transmit power
B. To encrypt voice communications
C. To reduce interference by activating the repeater only with the correct tone
D. To identify your station automatically
Notes: Answer: C.

## Slide 25
Checkpoint Quiz
Q3
What is the national simplex calling frequency for FM in the 2-meter band?
A. 144.000 MHz
B. 146.520 MHz
C. 146.940 MHz
D. 148.000 MHz
Notes: Answer: B. 146.520 MHz.

## Slide 26
Checkpoint Quiz
Q4
What is the approximate wavelength of a 146 MHz signal?
A. 1 meter
B. 2 meters
C. 6 meters
D. 10 meters
Notes: Answer: B. 300 ÷ 146 ≈ 2 meters.

## Slide 27
Checkpoint Quiz
Q5
Which propagation mode allows HF signals to travel long distances?
A. Ground wave
B. Line of sight
C. Sky wave (ionospheric refraction)
D. Tropospheric ducting
Notes: Answer: C. Sky wave.

## Slide 28
Checkpoint Quiz
Q6
What can cause VHF signals to travel over 1,000 miles?
A. D-layer absorption
B. Sporadic E
C. Ground wave
D. Multipath
Notes: Answer: B. Sporadic E.

## Slide 29
Checkpoint Quiz
Q7
What organization manages ARES?
A. FCC
B. FEMA
C. ARRL
D. DHS
Notes: Answer: C. ARRL.

## Slide 30
Checkpoint Quiz
Q8
What does the squelch control do?
A. Increases transmit power
B. Adjusts the antenna tuner
C. Mutes the receiver until a signal exceeds a set level
D. Controls modulation percentage
Notes: Answer: C.

## Slide 31
Checkpoint Quiz
Q9
When may you use any amateur frequency to call for help?
A. During a net
B. When propagation is poor
C. At any time during a genuine emergency
D. Only during declared RACES emergencies
Notes: Answer: C.

## Slide 32
Checkpoint Quiz
Q10
What does a DMR color code do?
A. Changes frequency offset
B. Encrypts the signal
C. Functions like a CTCSS tone for digital
D. Sets the time slot
Notes: Answer: C.

## Slide 33
Before Next Session
Your assignment for Module 3
Notes: Give the HamStudy assignment. Warn them: Module 3 is the math module, but it's simpler than they think.

## Slide 34
Your Assignment
Drill HamStudy: T2A–T2C, T3A–T3C, T4A–T4B
Target: 80%+ confidence on each section
Coming in Module 3: Technical Core
→ Ohm's Law (V = I × R) and power (P = V × I)
→ Decibels (+3 dB = double power, that's basically it)
→ Resistors, capacitors, inductors, transistors
→ Reading schematics
Don't panic — the math is 4 formulas and that's it
See you next session!
TavaOne Education — Module 2
Notes: Module 3 anxiety is real. Preempt it: tell them the actual math is simpler than they think, and HamStudy drills the specific calculations.