## Slide 1
Module 4: Signals, Circuits,
Antennas & Safety
Equipment · Digital Modes · Antennas · Feed Lines · Safety
13 exam questions — 37% of the test
TavaOne Education · Pinellas STEM Radio Lab
Notes: Biggest module by weight but mostly concrete. Cover briskly, keep it visual.

## Slide 2
Part 1: Station Equipment
T7A & T7B · 2 exam questions

## Slide 3
Inside a Transceiver
Oscillator — generates the signal at your frequency
Mixer — combines signals to shift frequency (tuning)
RF Amplifier — boosts signal for transmission
Audio Amplifier — boosts received audio for the speaker
Filter — passes desired frequencies, blocks unwanted
Modulator — adds your voice to the signal
Demodulator — extracts voice from received signal
TavaOne Education — Module 4
Notes: Block diagram level — they don't need to build one, just know the stages.

## Slide 4
SWR — Standing Wave Ratio
Measures how well your antenna matches your radio
1:1 = perfect match (all power to antenna)
1.5:1 = excellent
2:1 = good, acceptable
3:1 = marginal — radio may reduce power
∞:1 = no antenna or dead short — all power reflected
SWR meter goes in the feed line between radio and antenna
TavaOne Education — Module 4
Notes: SWR is their first real diagnostic tool. 1:1 perfect, under 2:1 good, above 3:1 means something's wrong.

## Slide 5
Test Equipment & Troubleshooting
Dummy load — 50Ω non-radiating load; test without transmitting
Wattmeter — measures RF power output
Multimeter — measures V, I, R (the basic tool)
Solder: use ROSIN-CORE (never acid-core for electronics)
No power? Check supply, check fuse
High SWR? Check antenna connection, coax, wrong band
Distorted audio? Mic gain, compression, bad mic element
TavaOne Education — Module 4
Notes: If you have a dummy load in the room, pass it around. It's just a big resistor in a can.

## Slide 6
Part 2: Modulation Modes
T8A · 1 exam question

## Slide 7
Voice Modes
FM (Frequency Modulation)
Varies the frequency of the signal
~16 kHz bandwidth (widest)
Used on VHF/UHF repeaters and simplex
Clear audio, but uses the most spectrum
Most common mode for Technicians
SSB & CW
SSB: single sideband — efficient, ~3 kHz
USB above 10 MHz, LSB below (convention)
Used for HF phone and weak-signal VHF
CW: Morse code — on/off keying, ~150 Hz
Narrowest bandwidth = longest range
AM: ~6 kHz, old-style HF — rarely used
TavaOne Education — Module 4
Notes: FM vs SSB vs CW is guaranteed on the exam. Key: CW = narrowest, FM = widest.

## Slide 8
Part 3: Digital Modes
T8B, T8C, T8D · 3 exam questions

## Slide 9
FT8 — The Hottest Mode in Ham Radio
Uses WSJT-X software + radio + computer
Contacts take ~15 seconds (computer handles it)
Works with signals FAR below what you can hear
Perfect for Technicians on 10m and 6m
Can work the world with low power and a simple antenna
This is what gets new hams hooked on HF
TavaOne Education — Module 4
Notes: If you can demo FT8 live on your station during class, do it. Watching contacts pop up on the waterfall is magic.

## Slide 10
APRS, Winlink, and More
APRS — automatic position reporting with GPS + radio
Digipeaters relay APRS packets; see stations on aprs.fi
Winlink — email over radio; critical for emergency comms
PSK31 — keyboard-to-keyboard text; narrow bandwidth
Packet radio — data networking over radio
Mesh networking — IP broadband over amateur radio
DMR, D-STAR, System Fusion — digital voice modes
TavaOne Education — Module 4
Notes: APRS and Winlink are the two digital modes most relevant to emergency preparedness.

## Slide 11
Amateur Satellites
FM repeaters in space — talk through them with an HT
Doppler shift: freq shifts as satellite passes overhead
Moving toward you = higher frequency, away = lower
Track with apps or online satellite trackers
Technicians can use amateur satellites on VHF/UHF
No license upgrade needed — just point and talk
TavaOne Education — Module 4
Notes: Satellites are exciting for students. Show a pass prediction app during class.

## Slide 12
Part 4: Antennas
T9A · 1 exam question

## Slide 13
Antenna Types
Omnidirectional
Vertical — radiates in all directions
5/8-wave vertical — VHF favorite, low-angle gain
Rubber duck — HT convenience, poor efficiency
Mobile whip — mag-mount or permanent
Ground plane — vertical with radials
Directional
Dipole — bidirectional (figure-8 pattern)
Yagi (beam) — high gain, narrow beam
Director + driven element + reflector
Front-to-back ratio = rejection from behind
Great for DXing — point at the target
TavaOne Education — Module 4
Notes: Dipole formula: 468 ÷ freq (MHz) = length in feet. Vertical vs Yagi = omni vs directional.

## Slide 14
Antenna Concepts
Dipole length (ft) = 468 ÷ frequency (MHz)
146 MHz dipole = 468 ÷ 146 ≈ 3.2 feet total
Gain — directional antenna concentrates signal (dBi/dBd)
Polarization — match antenna to signal (vertical FM, horizontal SSB)
A rubber duck is convenient but terrible — external antenna is a huge upgrade
Antenna is the single most important part of your station
TavaOne Education — Module 4
Notes: 'The best radio with a bad antenna loses to a mediocre radio with a good antenna.' Drive this home.

## Slide 15
Part 5: Feed Lines & Connectors
T9B · 1 exam question

## Slide 16
Coaxial Cable & Connectors
Use 50-ohm coax (RG-58, RG-8X, RG-213, LMR-400)
NEVER use 75-ohm TV cable (RG-59/RG-6) — wrong impedance
Loss increases with frequency AND with length
LMR-400 = lowest loss; RG-58 = highest loss (but fine for short runs)
PL-259 / SO-239 = most common connector
BNC = HTs and test equipment; SMA = modern HTs; Type N = UHF/microwave
Balun: connects balanced antenna (dipole) to unbalanced feed (coax)
Weatherproof outdoor connections — water kills coax
TavaOne Education — Module 4
Notes: The connector question is common: PL-259 is the answer. And 50-ohm vs 75-ohm trips people up.

## Slide 17
Part 6: Safety
T0A, T0B, T0C · 3 exam questions

## Slide 18
Electrical Safety
As little as 30V can be lethal
Power supplies hold charge in capacitors — even after off
Always measure before touching a circuit
Replace fuses with SAME rating — never higher
GFCI outlets in the shack
Ground your station: single-point ground to ground rod
Disconnect antennas during lightning storms
TavaOne Education — Module 4
Notes: Safety is mostly common sense but the exam tests specific facts. '30 volts can kill' is the key number.

## Slide 19
Antenna & RF Safety
POWER LINES are the #1 killer in amateur radio
Never install antennas where they can contact power lines
Never climb a tower alone
MPE = Maximum Permissible Exposure (FCC RF safety limit)
Duty cycle: FM = ~100%, SSB = ~20%, CW = ~40%
Higher duty cycle = more exposure = stricter limits
Control exposure: less power, more distance, antennas high
FCC requires RF exposure evaluation for your station
TavaOne Education — Module 4
Notes: The power line rule is absolute. Every year hams die from antenna-power line contact. Make this stick.

## Slide 20
Key Numbers — Module 4
Equipment & Modes
SWR 1:1 = perfect match
Dummy load = 50Ω, non-radiating
CW = narrowest bandwidth (~150 Hz)
FM = widest common voice (~16 kHz)
USB above 10 MHz, LSB below
FT8 = WSJT-X, 15-sec contacts
APRS = position reporting
Antennas & Safety
Dipole: 468 ÷ MHz = feet
Standard coax: 50 ohms
PL-259 = most common connector
LMR-400 = least loss
Balun: balanced ↔ unbalanced
Power lines = #1 danger
Rosin-core solder only
TavaOne Education — Module 4
Notes: Free points.

## Slide 21
Checkpoint Quiz
10 questions from T7, T8, T9, T0

## Slide 22
Checkpoint Quiz
Q1
What does an SWR of 1:1 indicate?
A. Maximum power reflected
B. Antenna not connected
C. Perfect impedance match
D. Feed line is shorted
Notes: C.

## Slide 23
Checkpoint Quiz
Q2
What is a dummy load used for?
A. Increase range
B. Test without radiating
C. Match impedance
D. Filter signals
Notes: B.

## Slide 24
Checkpoint Quiz
Q3
Which emission has the narrowest bandwidth?
A. FM
B. SSB
C. AM
D. CW
Notes: D. CW at ~150 Hz.

## Slide 25
Checkpoint Quiz
Q4
What software is used for FT8?
A. Echolink
B. WSJT-X
C. Ham Radio Deluxe
D. Winlink
Notes: B.

## Slide 26
Checkpoint Quiz
Q5
What is APRS?
A. Encryption system
B. Automatic position reporting
C. Amplifier control
D. Antenna tuning
Notes: B.

## Slide 27
Checkpoint Quiz
Q6
Approximate total length of a 146 MHz half-wave dipole?
A. 10 feet
B. 6 feet
C. 3 feet
D. 1 foot
Notes: C. 468÷146≈3.2 ft.

## Slide 28
Checkpoint Quiz
Q7
Which coax has the least signal loss?
A. RG-58
B. RG-59
C. RG-8
D. LMR-400
Notes: D.

## Slide 29
Checkpoint Quiz
Q8
Most important antenna installation safety rule?
A. Always use a balun
B. Never near power lines
C. Use thickest coax
D. Mount as low as possible
Notes: B.

## Slide 30
Checkpoint Quiz
Q9
What solder for electronics?
A. Acid-core
B. Silver
C. Rosin-core
D. Plumber's
Notes: C.

## Slide 31
Checkpoint Quiz
Q10
What does MPE stand for?
A. Maximum Power Emission
B. Maximum Permissible Exposure
C. Minimum Power Efficiency
D. Modulated Power Evaluation
Notes: B.

## Slide 32
Before Module 5
Your final assignment

## Slide 33
Your Assignment
Drill HamStudy: T7A–T7D, T8A–T8D, T9A–T9B, T0A–T0C
This is the most sections — start NOW, don't wait
Target: 80%+ on every section
Module 5 = Capstone: full practice exam + review + VE exam
Bring your photo ID and your FRN if you have one
You're one session away from your license
The hard work is done — now you prove it
TavaOne Education — Module 4
Notes: Build excitement. They're almost there.