## Slide 1
TAVAONE EDUCATION · PINELLAS STEM RADIO LAB
BSA Radio Merit Badge
Session 2 — Digital, Devices & Badge Completion
Information · Hardware · Cell Phones · FT8 Contact · Blue Card Sign-Off (Reqs 4, 5, 7, 8-A(6), 9)
TavaOne Education · Pinellas STEM Radio Lab · Gulf Coast Contest Club
Notes: Welcome back. Session 2 finishes the merit badge. Scouts complete Requirements 4, 5, 7, the on-air FT8 contact, and their career/hobby report-out. The counselor signs all completed requirements on the blue card at the end of the session.

## Slide 2
Session 2 Agenda
Quick review of Session 1 material
Req 4 — Information by Radio (modulation, digital standards, range)
Req 5 — Radio Hardware and Services (block diagram, consumer devices, RFID)
Req 7 — Cell Phones (cellular, Airplane Mode, GPS, emergencies, wireless charging)
Req 8-A(6) — FT8 digital contact at the club station
Req 9 — Career/hobby discussion with counselor
Blue card review and counselor sign-off
Notes: Check that every Scout brought: (1) their blue card, (2) their Session 1 student pack with completed spectrum chart and propagation sketch, (3) Req 9 research notes. Flag anyone who is missing materials early so they can complete them during non-presentation time.

## Slide 3
Session 1 Quick Review — 60 Seconds
Req 1: Three safety topics: grounding, electrical burns, Li-ion battery fires
Req 2: EM spectrum from 300 kHz to 3 GHz — MF/HF/VHF/UHF/microwave
Req 3: Three propagation modes — ground wave, sky wave, line-of-sight
Req 6: FCC (US enforcement) vs. ITU (global rules); call signs; NATO phonetic alphabet
Req 8-A (1–5): FCC amateur service; license classes; Q signals; emergency calls; HT/mobile/base/repeaters
Any questions from Session 1 before we continue?
Notes: Spend 5 minutes on review. Ask a Scout to name the three propagation modes, another to name 5 Q signals, another to spell their troop number phonetically. This reinforces Session 1 without repeating the full content.

## Slide 4
Requirement 4
Information by Radio — Modulation, Digital Standards & Data Rates

## Slide 5
Req 4a — Five Ways Radio Carries Information
CW (Morse Code): carrier keyed on/off → extremely narrow bandwidth → cuts through noise → still used for DX and weak-signal work
AM (Amplitude Modulation): varies carrier strength → simple to receive → used for broadcast and aircraft voice → takes double the bandwidth of SSB
FM (Frequency Modulation): varies carrier frequency → excellent audio quality → rejects interference well → used for VHF/UHF voice and FM broadcast
SSB (Single Sideband): AM with carrier and one sideband removed → all power in useful signal → ~4× range of AM → standard HF voice mode
Frequency Hopping: carrier jumps rapidly between many frequencies → impossible to intercept or jam → used in Bluetooth, military comms, and spread-spectrum Wi-Fi
Notes: The key teaching point: all modulation is about varying something about the wave to encode information. Ask Scouts: "If you vary the rate at which a carrier turns on and off faster and faster, at what point does it stop being Morse code and start being something else?" This leads naturally into digital modes.

## Slide 6
Req 4b — Digital Radio Standards
Bluetooth & Wi-Fi
Bluetooth: frequency-hopping at 2.4 GHz, hops 1,600×/second across 79 channels, short range (10–30 m), designed for low-power personal devices
Wi-Fi 802.11: 2.4 GHz and 5 GHz, OFDM splits channel into hundreds of parallel subcarriers, 30–100 m indoor range, shared among all users
Both are digital: information encoded as ones and zeros BEFORE transmission → allows error correction and encryption
5G and Why Digital Wins
5G: three tiers — sub-6 GHz for coverage, mmWave (24–100 GHz) for extreme speed in dense areas
5G uses massive MIMO + beamforming: aimed beams instead of broadcast
Digital advantages over analog: error correction (FEC), encryption, more data per Hz, multiple channels multiplexed on one carrier (OFDM)
Real-world 5G: average speeds far below peak; mmWave barely penetrates walls
Notes: Point out the Wi-Fi router in the room or the Scouts' own phones as living examples. FT8 (which they'll use for the digital contact) is also a digital mode — each transmission is a carefully encoded 79-symbol sequence that decoders can extract 20 dB below the noise floor.

## Slide 7
Req 4c & 4d — Range vs. Encoding; Wi-Fi vs. Fiber
Range vs. Encoding Method
More data rate = more bandwidth = needs stronger signal = shorter range
CW/SSB/FT8: narrow bandwidth, most efficient → longest range per watt
FT8 can decode signals 20 dB below the noise floor — contacts possible with 5 W across oceans
High-speed Wi-Fi: wide bandwidth demands strong SNR → range shrinks rapidly with distance or walls
Wi-Fi vs. Wired/Fiber Data Rates
Wi-Fi 6 peak: ~9.6 Gbps theoretical; real-world: 500 Mbps to 2 Gbps (close, clear)
Fiber peak: 400+ terabits/sec on one strand using WDM; home service: 1–10 Gbps
Why fiber wins: dedicated glass tube, no shared spectrum, no atmospheric noise, deterministic latency
Wi-Fi latency varies under load; fiber latency is stable
Notes: FT8 is the perfect illustration of encoding efficiency. You can decode an FT8 signal that you literally cannot hear with your ears. Ask Scouts: "If a signal is below the noise floor, how does the software hear it?" Answer: correlation and pattern matching across many repetitions of the 15-second transmission sequence.

## Slide 8
Quick Check
SSB has roughly 4× the range of AM for the same power. Why?
A) SSB uses a higher frequency, which propagates better
B) SSB removes the carrier and one sideband, putting all power into the useful signal
C) SSB uses frequency hopping to avoid interference
D) SSB antennas are more efficient than AM antennas
Answer: B — SSB eliminates the carrier (which carries no information) and one of the two duplicate sidebands, concentrating all transmit power into a single usable sideband. Same information, less power wasted.
Notes: This is a fundamental concept that comes up in the amateur license exam too. If any Scouts are going for Technician, reinforce this.

## Slide 9
Requirement 5
Radio Hardware and Services

## Slide 10
Req 5a — Block Diagram vs. Schematic Diagram
Block Diagram
Shows major functional sections as labeled boxes
Arrows indicate signal flow between sections
No component-level detail (no resistors, capacitors)
Used to: understand system organization, troubleshoot at system level, explain to non-engineers
You can draw one without electronics knowledge
Schematic Diagram
Shows every component using standardized electrical symbols
Connections drawn as lines; you can trace every wire
Used to: build circuits, calculate voltages/currents, repair equipment
Requires training to read fluently
A modern transceiver may have hundreds of schematic pages
Notes: If you have a block diagram and a schematic of the same circuit in the room, show both side by side. The contrast makes the difference immediately obvious. The club radio's manual probably has both somewhere.

## Slide 11
Req 5b — Draw a Radio Station Block Diagram
ACTIVITY: Draw your block diagram in your student pack now
Microphone → Transmitter → [Power Amplifier] → Feedline → Antenna
Antenna → Feedline → Receiver → Speaker
(Transceiver = Transmitter + Receiver combined in one box)
Key component functions:
Microphone: sound → electrical audio signal
Transmitter: audio → RF carrier with modulation
Amplifier (PA): increases RF power before antenna
Feedline: carries RF between radio and antenna (coax)
Antenna: electrical energy ↔ electromagnetic waves
Receiver: captures incoming RF → audio signal
Speaker: electrical audio → sound waves
Notes: Have everyone draw this NOW. Walk the room and check their diagrams. The most common error is forgetting the feedline or putting the amplifier in the wrong place (it goes between TX output and feedline, not between feedline and antenna). Counselor checks this diagram as part of Req 5b sign-off.

## Slide 12
Req 5c, 5d, 5e — Consumer Devices, Weather Radio & RFID
Consumer devices using radio (5c): cell phone (4G/5G), car radio (AM/FM/satellite), Wi-Fi router (2.4/5 GHz), wireless earbuds (Bluetooth), GPS navigator (1.575 GHz), smart home devices (Zigbee/Wi-Fi), TV remote (IR or RF), contactless credit card (NFC at 13.56 MHz)
NOAA Weather Radio (5d): 162.400–162.550 MHz, 7 channels, continuous NWS broadcasts, SAME coding = your county only alerts YOUR radio, covers 97% of US population, no license needed to receive
RFID (5e): reader emits RF field → passive tag harvests energy from field → transmits its unique ID back. Active tags have their own battery. Uses: store anti-theft, library books, building access badges, pet microchips, passport chips, toll collection (E-ZPass/SunPass), supply chain tracking, tap-to-pay
Notes: For RFID, ask Scouts to take out their student ID, building access card, or credit card and look for the contactless symbol (the wave icon). That is an RFID/NFC chip. If you have a RFID reader and tag demo kit, now is the perfect time to show it.

## Slide 13
Quick Check
A weather radio with SAME can be programmed to alert only for ___
A) Any severe weather in the entire state
B) Only the weather station's primary broadcast area
C) Your specific county or FIPS region
D) Any National Weather Service office within 200 miles
Answer: C — SAME (Specific Area Message Encoding) lets you program the radio to respond only to alerts for your FIPS county code. This prevents middle-of-the-night alerts for counties far away from you.
Notes: SAME is underappreciated. Weather radios without SAME programmed correctly generate many false alarms that make people turn them off — then they're useless. Make sure Scouts know this feature exists and how to use it.

## Slide 14
Requirement 7
Cell Phones — Cellular, Airplane Mode, GPS, Emergencies & Wireless Charging

## Slide 15
Req 7a — Cellular vs. Broadcast vs. Amateur Radio
Cellular
Two-way, digital, private
User needs NO license (carrier is licensed)
Requires towers, backhaul, billing — fails without infrastructure
Coverage depends on tower proximity
Monthly subscription cost
Broadcast vs. Amateur
Broadcast: one-way only, licensed transmitters, free to receive, entertainment/news
Amateur: two-way, requires FCC license to transmit, non-commercial, self-funded
Amateur can operate with NO infrastructure — simplex, global HF
Amateur: experimentation, emergency comms, worldwide contacts
Notes: The key distinction for emergency communications: cellular needs infrastructure; amateur radio doesn't. A ham with a battery-powered HF radio on a mountain can still talk to the world. This is why emergency managers value licensed amateur radio operators.

## Slide 16
Req 7b & 7c — Airplane Mode and Time/Location
Airplane Mode — What It Does and Why
Disables ALL wireless transmitters: cellular, Wi-Fi, Bluetooth, NFC
Can selectively re-enable Wi-Fi or BT after enabling Airplane Mode
Why: avionics use sensitive RF receivers — cell phone TX bursts could cause interference, especially on older aircraft
Cell phone in weak signal → increases TX power → more RF emissions
FAA allows Wi-Fi at cruise altitude; cellular calling still restricted on US flights
Also useful: save battery, reduce distractions, avoid roaming charges abroad
Time and Location via GPS
Time sync: phone receives precise time from cellular network (NTP → GPS atomic clocks) — accurate to microseconds
GPS location: signals from 24+ satellites at 20,200 km altitude
Each satellite broadcasts its position and exact time; phone measures travel time from each
Need signals from 4+ satellites for 3D position (lat, lon, elevation)
Elevation accuracy: typically ±30 ft, less accurate than horizontal
Notes: Many Scouts will have heard "put your phone on Airplane Mode on the plane" without knowing why. This is a good moment to connect a familiar rule to the actual physics. Ask: "What does Airplane Mode have to do with what we learned in Session 1 about radio waves and interference?"

## Slide 17
Req 7d & 7e — Cell Phones in Emergencies & Wireless Charging
EMERGENCY BENEFITS: widespread coverage in populated areas · call 911 with any phone, even without a SIM · texts get through when voice calls fail · iPhone 14+ and some Android: satellite SOS with no cell coverage · WEA (Wireless Emergency Alerts) push to all phones in a cell area
EMERGENCY LIMITATIONS: towers need power → batteries last 8–24 hrs → towers overload in disasters → no coverage in rural/remote areas. This is why ARES/RACES amateur radio operators staff EOCs.
WIRELESS CHARGING (Req 7e): Inductive coupling — the charging pad coil carries AC → creates changing magnetic field → phone coil captures energy → converts back to DC. Standard: Qi (Wireless Power Consortium). MagSafe adds magnets for precise coil alignment at higher rates. Efficiency: ~80–85% vs. ~95% for wired.
Notes: The satellite SOS feature on iPhone 14+ is a great current-events hook. You can show a screenshot or video of it working in a simulated emergency. Connect wireless charging to the physics of electromagnetic induction they may have touched in school science — it's the same principle as an electric motor or generator.

## Slide 18
Quick Check
Why do cell phone towers often fail after a major hurricane?
A) Hurricanes only damage broadcast towers, not cellular towers
B) Cell towers are small and easy to knock over with wind
C) Towers need grid power; when the grid fails, backup batteries last only 8–24 hours
D) The FCC shuts down towers during hurricanes to prevent interference
Answer: C — Cell towers run on backup batteries or generators when grid power fails. Most batteries only last 8–24 hours. When fuel runs out or generators fail, the towers go dark — exactly when people need communications most.
Notes: This hits home in Florida. Ask Scouts if they or their families have experienced losing cell service after a hurricane. The follow-up question: "So what do emergency managers use instead?" → Amateur radio operators with battery-powered radios on elevated antenna systems.

## Slide 19
Requirement 8-A(6)
On-Air Digital Contact — FT8

## Slide 20
About FT8 — The Most Popular Digital Mode
Created by Joe Taylor (K1JT) and Steve Franke (K9AN) in 2017
Each transmission is EXACTLY 15 seconds — synchronized to GPS/internet time
Each message is 77 bits encoded as a 79-symbol sequence using Gaussian FSK
Software (WSJT-X) decodes signals 20 dB below the noise floor — below what human ears can hear
5 W of power can make contacts across oceans — impossible with voice at the same power level
Most popular HF digital mode; on 20m (14.074 MHz) there are hundreds of stations on at any given moment
The tradeoff: FT8 is automated and very brief — you can't have a conversation. It proves a contact was made, but it's not a conversation mode like voice or CW.
Notes: Joe Taylor (K1JT) is a Nobel Prize-winning physicist. He applied signal processing techniques from radio astronomy to amateur radio weak-signal communication. This is a great example of Req 1 for the Amateur Extra license — the "advancement of the radio art" that the FCC protects in Part 97. Point out that FT8 has been downloaded millions of times and completely changed HF operating.

## Slide 21
FT8 Contact Procedure at the Club Station
1. Open WSJT-X — confirm your callsign, grid square (EL87), and radio connection
2. Set to 20m FT8 frequency: 14.074 MHz USB
3. Watch the DECODE pane — you will see many stations decoded in each 15-second window
4. Find a station calling CQ — double-click their line to begin the exchange
5. WSJT-X sends your response automatically in the next TX slot
6. The exchange takes 4–6 transmissions (1–2 minutes) — watch each message appear
7. When you see "73" confirmed, the contact is complete — WSJT-X logs it automatically
8. Copy the log entry into your student pack contact log
Notes: Walk through this on the actual computer before Scouts take a turn. Show the WSJT-X interface with the waterfall and decode pane running. Let Scouts see live FT8 activity before they click anything. The most common mistake is double-clicking a station that is already in a QSO — teach them to look for stations where the sequence just started with a CQ.

## Slide 22
FT8 Message Sequence — What Each Line Means
CQ W4GGJ EL87 → "Anyone listening? I'm W4GGJ in grid EL87."
W4GGJ KD9XYZ EM72 → "W4GGJ, I hear you. I'm KD9XYZ in grid EM72."
KD9XYZ W4GGJ -12 → "KD9XYZ, you're −12 dB. Here's my signal report."
W4GGJ KD9XYZ R-08 → "Roger — your report is −8 dB. Contact confirmed."
KD9XYZ W4GGJ RR73 → "Roger-roger, 73 — contact complete, goodbye."
W4GGJ KD9XYZ 73 → "73 — confirmed, done."
The dB numbers are the SNR (signal-to-noise ratio): −12 means 12 dB below the noise floor. Perfectly normal for FT8. Voice would be impossible at this level.
Notes: Have Scouts follow along on a printed copy of this sequence in their student pack. Ask: "What does 'R' mean at the start of R-08?" It means 'roger' — I received your previous message. Ask: "What does RR73 mean?" Roger-roger plus 73. These abbreviations pack maximum information into FT8's tiny 77-bit message.

## Slide 23
Requirement 9
Career / Hobby Report-Out — Counselor Discussion

## Slide 24
Req 9 — Your Discussion with the Counselor
This is a CONVERSATION — not a paper, not a memorized report
Option 9a — Career Research:
Which career did you choose? What does the job involve day to day?
What training and education are required? What are the costs?
What are job prospects and salary ranges? Did this interest you?
Option 9b — Ham Radio Hobby / Volunteer Path:
What hobby or volunteer role did you research? (ARES? RACES? POTA? Contesting?)
What license and training would you need?
What are startup costs? What organizations support this?
What are your short-term and long-term goals if you pursued it?
Notes: Pull each Scout aside for a 3–5 minute one-on-one discussion. If a Scout did not complete the research, they can still discuss what they know and complete the research at home before the counselor signs that specific requirement. The blue card for Req 9 can be signed after the discussion even if it happens by phone or email.

## Slide 25
Blue Card Sign-Off
Final Review — All Nine Requirements

## Slide 26
Blue Card Checklist — Every Requirement
✓ Req 1: Grounding (DC/AC/antenna/lightning), electrical burns, Li-ion battery fires
✓ Req 2a: EM spectrum chart drawn; 5 bands labeled; 8 services located
✓ Req 2b: Definition of radio; broadcast vs. 2-way; commercial vs. hobby discussed
✓ Req 3a: Propagation sketch (ground wave, sky wave, line-of-sight)
✓ Req 3b: WWV/WWVH band condition use explained
✓ Req 3c: DX vs. local explained
✓ Req 4: CW/AM/FM/SSB/freq-hopping; digital standards; range; Wi-Fi vs. fiber
✓ Req 5a–e: Block vs. schematic; block diagram drawn; consumer devices; weather radio; RFID
✓ Req 6: FCC vs. ITU; call signs; phonetic alphabet
✓ Req 7a–e: Cellular; Airplane Mode; GPS time/location; emergencies; wireless charging
✓ Req 8-A(1–5): FCC amateur service; licenses & VEs; Q signals; emergency calls; equipment
✓ Req 8-A(6): On-air contact logged with RST report
✓ Req 9: Career or hobby research discussed with counselor
Notes: Work through each Scout's blue card systematically. The counselor initials each requirement as it is confirmed. If anything is missing, note it and arrange for completion by phone, email, or a brief follow-up meeting before the final signature. The blue card cannot be submitted to the council advancement chair without ALL requirements initialed.

## Slide 27
Badge Complete! 🎉
Congratulations — you earned your Radio Merit Badge
What's Next?
Interested in getting licensed? TavaOne Education runs Technician license courses on-site
VE exam sessions held at Pinellas STEM Radio Lab — pass to get your own callsign
Join the Gulf Coast Contest Club — club station access, mentorship, on-air events
ARES / RACES — serve your community as an emergency communicator
POTA (Parks on the Air) — take radio into the field and make contacts from national parks
tavaoneeducation.org · W4GGJ · EL87PT · TavaOne Education Inc., EIN 42-3444601
Notes: Congratulate every Scout who completes the badge. Hand out the blue cards. If any Scout is interested in getting licensed, point them to the TavaOne Education Technician course information. This is also a good moment to mention that the Gulf Coast Contest Club welcomes student members and can provide mentorship (Elmers) for new hams.