## Slide 1
Module 1: Rules & Operating
FCC Privileges · Operating Procedures · Digital Modes
2024–2028 Amateur Extra Question Pool
TavaOne Education · Pinellas STEM Radio Lab
Notes: Welcome to Extra class. This module is the biggest in the course at 22% of the exam. We cover E1 (rules) and E2 (operating) — 11 questions total. Remind students they need their General license to sit for Extra. HamStudy setup is next.

## Slide 2
What We're Building Toward
7 modules × 2 hours = 50-question Amateur Extra exam
Module 1 (today): Rules & Operating — FCC privileges, satellites, digital modes
Module 2: Propagation & Practices — EME, meteor scatter, test equipment
Module 3: Electrical Principles — resonance, Q, time constants, phasors
Module 4: Circuit Components — semiconductors, diodes, digital ICs
Module 5: Practical Circuits — amplifiers, filters, DSP, oscillators
Module 6: Signals, Emissions & Safety
Module 7: Antennas & Transmission Lines — heaviest math, Smith chart
50 questions on the exam, 37 to pass (74%) — you already know how to study
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Remind them the Extra pool has 602 questions. HamStudy will narrow that down for them. The prerequisite is already passing General, so they've been through the process before.

## Slide 3
The Extra Exam — What to Expect
50 multiple-choice questions, randomly drawn from the question pool
One question from each of 50 groups (E1A through E9H and E0A)
37 correct answers to pass = 74%
No trick questions — four choices, one is always correct
Exam sessions at the lab — same VE team as Technician and General
No FCC application fee for upgrade (it's already associated with your license)
Your call sign doesn't change when you upgrade
HamStudy is the primary study tool — use it between every session
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Unlike the $35 FCC application fee for a new license, upgrade exams typically don't require a new FCC payment if the VEC processes it as an upgrade. Verify current FCC fee rules at time of class.

## Slide 4
HamStudy Setup
Go to hamstudy.org — create or log into your account
Select the 2024–2028 Amateur Extra question pool
Share your progress link with your instructor (QR code on handout)
Between sessions: drill the assigned sections to 80%+ confidence
HamStudy tracks which questions you miss and drills those harder
Trust the system — it works the same way it worked for Tech and General
Target: 80%+ on E1A through E2E before Module 2
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Give students 3 minutes to pull up HamStudy on their phones. Confirm they can find the Extra pool. Share your instructor link so you can see their progress before Module 2.

## Slide 5
Part 1: Extra-Class Frequency Privileges
Subelement E1A — 1 exam question from this group
Notes: The E1A section is about where Extra-class operators can go that General cannot. These exclusive segments are small, mostly at the bottom of each HF band.

## Slide 6
Where Only Extras Can Transmit
80 meters: 3.500–3.525 MHz (CW) and 3.600–3.700 MHz (phone/CW/data)
40 meters: 7.000–7.025 MHz (CW)
20 meters: 14.000–14.025 MHz (CW) and 14.150–14.175 MHz (phone/CW)
15 meters: 21.000–21.025 MHz (CW)
10 meters: 28.000–28.025 MHz (CW)
These are small segments — Extra's reward for doing the harder exam
General already has most HF — Extra opens the competitive CW segments
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: The Extra-exclusive CW segments are where the serious CW contesters and DX operators live. On contest weekends, 14.000–14.025 is wall-to-wall CW that General operators can only listen to, not transmit in.

## Slide 7
Signal Bandwidth at Band Edges
Your signal extends beyond your carrier frequency — not just on the carrier itself
USB (upper sideband): signal extends upward from carrier — stay 3 kHz inside upper edge
LSB (lower sideband): signal extends downward from carrier — stay 3 kHz inside lower edge
CW: carrier IS the signal center — still has some bandwidth (filter shape)
FT8 and other digital modes also have real bandwidth — know where you sit
Transmitting outside the band is an FCC violation even if the carrier is inside
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Ask the class: if 20m phone extends to 14.350 MHz at the top, and you're using USB, what's the highest carrier frequency you'd use? Answer: roughly 14.347 MHz to keep the upper sideband edge at 14.350.

## Slide 8
60m, 630m, and 2200m Bands
60 meters (5 MHz): channelized operation on 5 specific channel center frequencies
→ 5332, 5348, 5358.5, 5373, and 5405 kHz
→ CW must be transmitted at the channel center (not USB-offset like phone)
→ Maximum power: 100 watts ERP
2200 meters (135.7–137.8 kHz): maximum 1 watt EIRP
630 meters (472–479 kHz): maximum 5 watts EIRP
Both LF bands require UTC (Utilities Technology Council) notification
Wait 30 days after notification before operating — unless UTC clears you earlier
EIRP = Effective Isotropic Radiated Power (referenced to a perfect isotropic)
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: EIRP vs. ERP: EIRP is referenced to an isotropic radiator, ERP is referenced to a dipole. EIRP = ERP + 2.15 dB. The LF bands share spectrum with power-line carrier systems — that's why UTC gets notified.

## Slide 9
Part 2: Station Restrictions
Subelement E1B — 1 exam question from this group
Notes: E1B covers spurious emissions, antenna structure rules, PRB-1, RACES, and the National Radio Quiet Zone.

## Slide 10
Spurious Emissions & Zoning (E1B)
Spurious Emissions
Any transmission not part of intended signal
HF standard: −43 dB below fundamental
Includes: harmonics, IMD, parasitic oscillations
Switching amplifiers need output filters
Your amp must meet this standard
PRB-1 Zoning Preemption
FCC preemption of local zoning rules
Local law must 'reasonably accommodate'
Cannot 'preclude' all amateur communications
Does NOT eliminate local authority
Does NOT cover HOA private covenants
Some states extended similar rules to HOAs
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: PRB-1 comes up in the exam and in real life. Know the language: 'reasonably accommodate' and 'not preclude all communications.' HOA restrictions are contractual and outside FCC jurisdiction unless your state has acted.

## Slide 11
RACES, Antenna Structures & Quiet Zone
RACES (Radio Amateur Civil Emergency Service):
→ Requires FCC amateur license AND civil defense certification — both required
→ May use any frequency authorized to your station during declared emergencies
→ Limited to 1 hour per week of RACES practice (no limit during actual emergency)
Antenna structure registration (Part 17 / FAA):
→ Structures over 200 feet above ground require FAA determination
→ Structures within certain airport proximity also require notification
→ FCC ASR database tracks registered structures
National Radio Quiet Zone: area around Green Bank, WV — restrictions on transmitted power near sensitive observatories
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: RACES is distinct from ARES (Amateur Radio Emergency Service, which is an ARRL program). RACES is FCC-defined and requires the civil defense certification. Ask: does your county have a RACES program? Most ARES operators function under both when activated.

## Slide 12
Part 3: Remote/Automatic Control
Subelement E1C — 1 exam question from this group
Notes: E1C covers remote control rules, the control link failure requirement, international permits, and LF band notification.

## Slide 13
Remote Control & Control Link Failure
Remote control: control operator is NOT at the transmitter site
Control link: the connection between operator and transmitter (internet, RF link, phone)
If the control link fails: station must automatically stop transmitting within 3 minutes
The control operator must be able to immediately terminate transmission at any time
HF FM: modulation index must not exceed 1.0 below 29.7 MHz
Automatic control: no operator present — station runs itself
Automatic control is allowed for: beacons, repeaters, RTTY/data gateways
Automatically controlled data stations may forward third-party traffic on RTTY/data modes
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: The 3-minute rule is a favorite exam question. Make sure students have it cold. Ask: why 3 minutes? Answer: to give the station time to detect the failure and shut down gracefully without requiring instant action.

## Slide 14
Operating Internationally (CEPT, IARP)
CEPT License: operate in CEPT member countries without a separate host-country license
→ CEPT = Conference of Postal and Telecommunications Administrations
→ Covers most of Europe plus some other countries
→ You operate under your US license — host country may impose equivalent class limits
IARP Permit: operate in IARP countries (mainly Americas)
→ IARP = International Amateur Radio Permit
→ Required by some Western Hemisphere countries
Canadian amateurs operating in the US: use Canadian license terms, up to Extra-equivalent
Check current country-specific rules before any international operation
STA (Special Temporary Authority): FCC authorization for experimental operations
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: A US amateur can get both CEPT and IARP documentation before an international trip. The ARRL has current information on which countries honor which permit. Always verify — rules change.

## Slide 15
Part 4: Space Stations & One-Way Comms
Subelement E1D — 1 exam question from this group
Notes: E1D is about amateur satellites, balloons, space telecommand, and one-way transmissions. Students who aren't into satellites often miss this section — emphasize the key definitions.

## Slide 16
Space Station Definitions
Space station: amateur station located above 50 km altitude
Telemetry: one-way data transmission FROM space station TO Earth (status, sensor data)
Telecommand: one-way control transmission FROM Earth TO space station (commanding it)
Space telecommand stations: only specifically designated amateur stations may transmit to control a space station
Model craft telecommand: ANY amateur may transmit up to 1 watt to control models — no ID required
HF bands with space allocations: 40m, 20m, 15m, and 10m
Balloon stations must transmit ID at regular intervals — standard amateur rules apply
One-way amateur transmissions are allowed for: beacons, space telemetry, and telecommand only
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Emphasize the distinction: you don't need a special designation to control a model aircraft — any amateur can do that with 1W, no ID. But you DO need a designated space telecommand station to control an orbiting satellite.

## Slide 17
Part 5: The Volunteer Examiner Program
Subelement E1E — 1 exam question from this group
Notes: Your students are probably sitting in front of the people who will administer their exam. Make this section personal and practical.

## Slide 18
VE Program Rules
VEC (Volunteer Examiner Coordinator): organization that coordinates VEs — ARRL, W5YI, Laurel, etc.
VE (Volunteer Examiner): individual licensed amateur who administers exams
VE must be accredited (confirmed) by a VEC — not just licensed
VEs can only be reimbursed for expenses directly related to exam preparation, processing, and administration
A VE may NOT examine immediate family members or household members
If an applicant fails an element: VE team RETURNS the application to the applicant — does not keep it
Fraudulent exam administration by a VE:
→ Revocation of station license AND suspension of operator license
→ This is the most severe consequence for VE misconduct
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Point out: the consequence for VE fraud is both a station license revocation AND an operator license suspension — not just one. The exam almost always asks about the consequence of fraudulent administration.

## Slide 19
Part 6: Miscellaneous Rules
Subelement E1F — 1 exam question from this group
Notes: E1F covers power amplifier certification, spread spectrum geography, Line A, Canadian amateurs, and mesh network rules.

## Slide 20
Miscellaneous Extra-Class Rules (E1F)
External RF power amplifiers: must meet FCC certification if capable of operating below 144 MHz
→ Prevents use on CB and other services
Spread spectrum: only authorized above 222 MHz (not on HF)
Line A: geographic boundary near Canadian border — 420–430 MHz operations restricted near Line A
Canadian amateurs in the US:
→ Operate under Canadian license terms
→ Privileges limited to US equivalent of their Canadian class (up to Extra)
Auxiliary stations: Technician class and above may serve as control operator
Mesh networks (AREDN): cannot transmit messages encoded to obscure meaning
→ Encryption to hide content is prohibited on mesh networks just as everywhere else
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: The spread-spectrum-above-222-MHz rule is a common exam question. Mesh networks are increasingly popular for emergency communications — make sure students understand the encryption restriction applies there too.

## Slide 21
Part 7: Amateur Satellites
Subelement E2A — 1 exam question from this group
Notes: Satellites are a favorite topic for Extra class. Even students who don't operate satellites find this section interesting once they understand how linear transponders work.

## Slide 22
Orbital Mechanics for Ham Radio
Ascending pass: satellite travels south to north across your location
Descending pass: satellite travels north to south
Perigee: closest point of orbit to Earth → least path loss → strongest signal
Apogee: farthest point → weakest signal, most Doppler shift
Geostationary: ~35,786 km altitude, satellite appears stationary from Earth
Keplerian elements: 6 parameters that fully define a satellite's orbit
→ Used by tracking software (like Gpredict) to predict passes
→ Updated regularly as orbits drift due to atmospheric drag
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Many students have used satellite tracking apps on their phones without knowing the math behind it. Keplerian elements are the underlying data. Ask: what happens to a satellite's orbit at very low altitudes? Atmospheric drag decays it faster.

## Slide 23
Linear Transponders — Key Concept
A linear transponder receives a range of frequencies on one band, retransmits on another
Linear transponders are INVERTING:
→ Upper Sideband uplink becomes Lower Sideband downlink
→ Signal at the top of the uplink passband appears at the BOTTOM of the downlink passband
Doppler correction: as satellite approaches, frequencies shift up; as it recedes, they shift down
Keep your ERP (power × antenna gain) at minimum needed:
→ High power crushes the transponder's automatic level control
→ Degrades the downlink signal for EVERYONE using the satellite
Spin modulation: rotating satellite causes rapid signal variations → use circular polarization
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Demo if possible: pull up a linear transponder satellite (like SO-50 or RS-44) on a tracking app and show students where it is. Explain that on a linear transponder, if you tune up 1 kHz on your uplink, you appear 1 kHz lower on the downlink.

## Slide 24
Satellite Mode Designators & Bands
Mode designators use letters for uplink/downlink bands:
→ Mode U/V: uplink on 70cm (UHF), downlink on 2m (VHF)
→ Mode V/U: uplink on 2m (VHF), downlink on 70cm (UHF)
→ Mode L/U: uplink on 23cm (L band), downlink on 70cm
L band = 23 cm = 1.2 GHz range
S band = 13 cm = 2.4 GHz range
Low-Earth orbit satellites: typical pass duration 8–12 minutes
Geostationary amateur satellites (like Phase 3 spacecraft): visible continuously
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Mode designators: the first letter is the uplink, the second is the downlink. A student asked once why they invert — it's because the repeater in space needs to receive on one band while transmitting on another, just like a terrestrial repeater.

## Slide 25
Part 8: Television, Contesting & DX
Subelements E2B–E2C — 1 exam question from this group
Notes: E2B covers SSTV and fast-scan ATV. E2C covers digital logging formats and DX operating. Quick section — mostly memorization.

## Slide 26
Slow-Scan Television (SSTV)
SSTV transmits still images via audio tones over standard SSB equipment
Colors are sent SEQUENTIALLY — one color scan per line (not simultaneously)
Tone frequency encodes pixel brightness: higher frequency = brighter pixel
VIS (Vertical Interval Signaling) code at the start of each frame:
→ Identifies the SSTV mode (color system + resolution)
→ Received automatically by SSTV software to decode correctly
DRM (Digital Radio Mondiale): uses SSB-capable receiver
Fast-scan ATV (amateur television): 525 lines NTSC, interlaced scanning
DVB-T (digital ATV): uses QAM and QPSK modulation
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: A quick demo of SSTV audio is very effective here if you have a recording. The students can literally hear the tones encoding image data — it makes the concept stick immediately.

## Slide 27
Contest Logging & DX Operating
Cabrillo format: the standard electronic log format for contest submission
→ Required by ARRL, CQ Magazine, and most major contest sponsors
ADIF (Amateur Data Interchange Format): exchange log data between programs
LoTW (Logbook of the World): ARRL's electronic QSL system
→ Confirms all contact types (phone, CW, digital) for DXCC, WAS, and other awards
DX pileup procedure:
→ Send your FULL call sign once or twice — not just suffix
→ Listen to how the DX is working: by suffix? by region? simplex or split?
Split operation: DX transmits one freq, listens on a range 5–10 kHz away
Remote operation in the US: no '/R' or additional indicator required
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: LoTW vs. paper QSLs: LoTW confirmations count for DXCC. The ARRL stopped accepting paper QSLs for most DXCC credit. Ask who has submitted a Cabrillo log before — they'll have strong opinions about contest logging software.

## Slide 28
Part 9: Digital Modes
Subelements E2D–E2E — 1 exam question from this group
Notes: This section covers the full spectrum of digital modes Extra operators need to know. Many students already use FT8 — build on what they know.

## Slide 29
Weak-Signal Digital Modes
FT8: 15-second TX/RX cycles; 4-tone CPFSK modulation; computer clock must be within ±1 second
→ Most popular digital mode in ham radio today
FT4: 7.5-second cycles; faster paced for contests; less sensitive than FT8
Q65: designed for EME (Earth-Moon-Earth / moon bounce)
→ Handles severe Doppler shifting and libration fading
MSK144: designed for meteor scatter
→ Uses sporadic E-layer ionization trails from meteors
→ Works on 28–148 MHz
FST4: four-tone Gaussian FSK; variable periods (15 seconds to 1800 seconds)
→ Used on VLF, LF, and MF bands where propagation is very slow
WSPR: propagation beacons ONLY — not two-way keyboard communication
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: FT8 is the gateway drug to understanding weak-signal modes. Ask: who's already used FT8? What happens if your computer clock is off? The answer (wrong decode cycles, missed contacts) makes the clock-sync requirement memorable.

## Slide 30
HF Data Modes & APRS
PACTOR IV: highest data throughput of any HF digital mode
→ Used extensively for Winlink email over HF
PSK31: variable-length (Varicode) character coding
→ Very narrow bandwidth — second narrowest after FT8
ALE (Automatic Link Establishment): scans a list of frequencies, selects best one automatically
APRS (Automatic Packet Reporting System):
→ Protocol: AX.25 packet radio
→ Frame type: unnumbered information (UI) frames — connectionless, broadcast
→ WIDE3-1 digipeater path: relayed by up to 3 digipeaters (counter decrements each hop)
→ Uses: position reporting, weather data, messages, object tracking
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Winlink + PACTOR IV is the combination most emergency communications operators use for HF email. APRS is live on 144.390 MHz — if anyone has a handheld, you can pull up aprs.fi on a projector and show live APRS traffic in the room.

## Slide 31
Quick Reference
The numbers and rules that matter
Notes: This slide is for review before the checkpoint quiz. Give students 2 minutes to quiz each other on the reference card from their student pack.

## Slide 32
Key Numbers for the Exam (Part 1)
Extra-only 80m CW segment | 3.500-3.525 MHz
Extra-only 20m phone segment | 14.150-14.175 MHz
60m max power | 100W ERP, channelized
2200m max power | 1 watt EIRP
630m max power | 5 watts EIRP
630m/2200m startup | UTC notification: 30-day wait
Control link failure | Auto-stop within 3 minutes
Spurious emissions (HF) | -43 dB below fundamental
Spread spectrum above | 222 MHz
FT8 cycle | 15 sec TX/RX; 4-tone CPFSK
MSK144 | Meteor scatter, 28-148 MHz
WSPR | One-way beacons only
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Part 1. Cover the right column, say the answer from the left. 90 seconds.

## Slide 33
Key Numbers for the Exam (Part 2)
PACTOR IV | Highest HF data throughput
Cabrillo format | Electronic contest log submission
LoTW | Confirms all contact types for awards
APRS protocol | AX.25, unnumbered information frames
VE cannot examine | Immediate family / household members
VE fraud consequence | Station license revoked + operator license suspended
RACES requirement | FCC license + civil defense certification
PRB-1 | Zoning must reasonably accommodate amateur radio
CEPT permit | Operate in CEPT countries on your US license
Satellite transponder | Inverting: USB in, LSB out
Perigee | Closest approach: least path loss
Model craft telecommand | Any amateur, 1W max, no ID required
TavaOne Education — Module 1
E1–E2 · Extra Class
Notes: Part 2. Then move into the checkpoint quiz.

## Slide 34
Checkpoint Quiz 1 / 10
What is the maximum power allowed on the 2200-meter amateur band?
A. 100 watts PEP
B. 5 watts EIRP
C. 1 watt EIRP
D. 50 watts PEP
Answer: C — 1 watt EIRP (2200m = 135.7–137.8 kHz)
Notes: Key distractor: B is 630m, not 2200m. Students mix these up constantly. 2200m = 1W, 630m = 5W.

## Slide 35
Checkpoint Quiz 2 / 10
Which of the following describes the operation of a linear transponder in an amateur satellite?
A. Amplifies signals and retransmits on the same frequency
B. Receives signals and retransmits them in an inverted passband
C. Converts digital signals to analog and retransmits them
D. Demodulates and remodulates signals to reduce noise
Answer: B — Inverting passband: USB in = LSB out; signal position reversed
Notes: This is a conceptual question. Make sure students can visualize the inversion before the exam.

## Slide 36
Checkpoint Quiz 3 / 10
What must happen before operating on the 630-meter band?
A. Notify the ARRL at least 30 days before operating
B. Notify the Utilities Technology Council and wait 30 days
C. File an STA request with the FCC
D. Register with a VEC
Answer: B — UTC (Utilities Technology Council) notification, then 30-day wait
Notes: Common wrong answer: A. The ARRL is not involved. UTC protects power-line carrier systems.

## Slide 37
Checkpoint Quiz 4 / 10
If the control link of a remotely controlled station fails, what must happen?
A. The station must automatically stop transmitting within 3 minutes
B. Switch to automatic control until the link is restored
C. The station may continue operating for up to 1 hour
D. The licensee must notify the FCC immediately
Answer: A — Auto-stop within 3 minutes
Notes: 3 minutes is the specific number. Not 5, not 10. Get that number solid.

## Slide 38
Checkpoint Quiz 5 / 10
What is the consequence of fraudulent exam administration by a Volunteer Examiner?
A. Revocation of VE accreditation only
B. Suspension of operator license only
C. Revocation of station license AND suspension of operator license
D. A written warning from the FCC
Answer: C — BOTH station license revoked AND operator license suspended
Notes: Both. Not one or the other. This is a two-part consequence.

## Slide 39
Checkpoint Quiz 6 / 10
What is the primary advantage of circular polarization on a ground station antenna when working satellites?
A. Greater signal bandwidth
B. Resistance to multipath propagation
C. Mitigation of spin modulation from tumbling satellites
D. Reduced path loss
Answer: C — Reduces spin modulation effects from tumbling satellites
Notes: Spin modulation = rapid amplitude variation as a rotating satellite's antenna sweeps past you. Circular polarization averages out the effect.

## Slide 40
Checkpoint Quiz 7 / 10
Which HF digital mode provides the highest data throughput?
A. PSK31
B. FT8
C. WSPR
D. PACTOR IV
Answer: D — PACTOR IV
Notes: PSK31 is narrow. FT8 is optimized for weak-signal, not throughput. WSPR is one-way only. PACTOR IV wins on throughput.

## Slide 41
Checkpoint Quiz 8 / 10
What does the VIS code at the beginning of an SSTV transmission identify?
A. The transmitting station's call sign
B. The SSTV mode being used
C. The receiving station's ID
D. The image resolution in pixels
Answer: B — The SSTV mode (color system and resolution)
Notes: VIS = Vertical Interval Signaling. Your software reads it and automatically selects the right decoder.

## Slide 42
Checkpoint Quiz 9 / 10
What is the Cabrillo format used for?
A. Exchanging QSO data between logging programs
B. Electronic submission of contest logs
C. Confirming contacts for DXCC awards
D. Automatic frequency control in digital modes
Answer: B — Electronic contest log submission
Notes: ADIF is for data exchange between programs. LoTW is for award confirmation. Cabrillo is specifically for submitting contest logs to sponsors.

## Slide 43
Checkpoint Quiz 10 / 10
What does PRB-1 require of state and local governments?
A. Exempt all amateur antennas from local zoning entirely
B. Allow unlimited antenna height in residential areas
C. Reasonably accommodate amateur radio and not preclude all antenna installations
D. Require permits for all antennas over 10 feet
Answer: C — Reasonably accommodate; cannot preclude all communications
Notes: PRB-1 does not eliminate local authority. It sets a floor: 'reasonably accommodate' and 'not preclude all.' HOA rules are not covered.

## Slide 44
Before Module 2
Your assignment:
Drill HamStudy sections E1A through E2E
Target 80%+ confidence on each section before Module 2
Focus extra time on E2A (satellites) — most students find it unfamiliar
HamStudy tracks your weak spots and drills those harder — trust the system
Coming in Module 2: Advanced Propagation & Practices
EME, meteor scatter, aurora, TEP, space weather, test equipment, receiver performance
Notes: Thank students. Remind them the VE exam is at the end of Module 7. At the pace of one module per week, they'll be licensed in 7 weeks.