## Slide 1
Module 2: Propagation & Practices
Advanced Propagation Modes · Test Equipment · Receiver Performance
2024-2028 Amateur Extra Question Pool
TavaOne Education · Pinellas STEM Radio Lab
Notes: Module 2 opening slide.

## Slide 2
What We're Covering Today
8 exam questions — E3 (3 Qs) + E4 (5 Qs) = 16% of your Extra exam
Hour 1: Advanced propagation — modes you won't see on General
→ EME, meteor scatter, auroral, tropospheric ducting
→ TEP, long-path, sporadic E, chordal hop
→ Space weather: solar flux, A/K index, Bz, VOACAP
Hour 2: Amateur practices
→ Test equipment: oscilloscope, spectrum analyzer, antenna analyzer, VNA
→ Measurement: S-parameters, directional wattmeter, Q measurement
→ Receiver performance: noise, dynamic range, blocking, SDR overload
→ Noise and interference sources
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: HamStudy check-in: who hit 80% on E1 and E2? Collect any straggler questions before moving on.

## Slide 3
Part 1: EME, Meteor Scatter & Auroral
Subelement E3A — 1 exam question
Notes: These are the exotic propagation modes. Most students have heard of them but never understood the physics. Spend time on libration fading — it's a memorable exam concept.

## Slide 4
Earth-Moon-Earth (EME / Moon Bounce)
The Moon reflects VHF/UHF signals — you can work stations on the other side of the world
Maximum one-way path: ~12,000 miles (Earth to Moon and back = ~480,000 miles round trip)
Perigee (Moon closest to Earth): minimum path loss, strongest signals
Libration fading: Moon wobbles slightly (libration) — antenna orientation constantly shifts
→ Causes rapid, irregular signal fluctuations — 'fluttery' audio
Mode: Q65 — designed for severe Doppler shifting and libration fading
Requires very high-gain antennas (big Yagi arrays) and usually maximum legal power
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: Ask: who has heard an EME recording? Play one if you have it — the libration fading is unmistakable and makes the concept stick. The Moon bounces signals but also moves, causing the wobble effect.

## Slide 5
Meteor Scatter
Meteors burn up in the E region of the ionosphere (~80-120 km altitude)
The ionized trail reflects VHF signals — for milliseconds to a few seconds
Frequency range: 28-148 MHz (10m through 2m)
Mode: MSK144 — designed for very short burst duration
MSK144 encodes data quickly enough to fit a full exchange in a single burst
Peak meteor scatter activity: major showers (Perseids in August, Leonids in November)
Random (sporadic) meteors: year-round low-level activity
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: MSK144 replaced WSJT-X modes like FSK441 for meteor scatter. Burst durations can be as short as 40ms — the entire QSO is compressed into those bursts and reassembled.

## Slide 6
Auroral and Tropospheric Ducting
Auroral propagation: severe geomagnetic storms excite the auroral oval
→ The aurora acts as a reflector for VHF signals
→ CW is the only practical mode — auroral reflection distorts audio badly
→ Signals have a characteristic 'buzz' or 'hiss' quality
→ Works best when you point your antenna toward the aurora (northward in N. hemisphere)
Microwave tropospheric ducting:
→ Temperature inversions over large bodies of water trap signals
→ Typical range: 100-300 miles; sometimes much farther
→ Most common on microwave bands (2.4 GHz and above)
→ Florida to Cuba; California to Hawaii (rare but happens)
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: Auroral prop is seasonal — peak around equinoxes when geomagnetic storm likelihood is higher. Students in northern states are more likely to experience this. CW is best because the aurora scatters and smears SSB audio.

## Slide 7
EM Wave Fundamentals
An EM wave has two fields at right angles to each other: E (electric) and H (magnetic)
The wave travels at right angles to BOTH E and H fields
Think of it as three perpendicular axes: travel direction, E field, H field
Circular polarization: both E and H fields rotate as the wave propagates
→ Reduces spin modulation on satellites (covered in Module 1)
Speed through a medium: determined by the index of refraction
→ Slower in denser media (glass, water, ionosphere) than in vacuum
MUF at night: as ionosphere thins at darkness, MUF drops — switch to a lower HF band
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: This is basic but tested. The key image: three perpendicular things — the direction of travel, the E field, and the H field. They're all at right angles. Circular polarization is just those fields continuously rotating.

## Slide 8
Part 2: TEP, Long-Path, Sporadic E
Subelement E3B — 1 exam question
Notes: These are the propagation modes that give long-distance VHF contacts. TEP in particular is fascinating — it enables 5,000-mile contacts on 2m without any ionospheric layer support.

## Slide 9
Transequatorial Propagation (TEP)
TEP enables 2,000-3,000 mile paths perpendicular to the geomagnetic equator
Maximum range: approximately 5,000 miles
Both stations must be roughly equidistant north and south of the geomagnetic equator
Timing: typically afternoon to early evening
This is a 2m DX mode — it enables contacts that are otherwise impossible
Not the same as standard F-layer propagation — TEP uses field-aligned irregularities
Example: Florida to southern South America on 144 MHz
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: TEP is one of those modes that sounds impossible — 5,000 miles on 2m with no Sporadic E? But it's real and documented. The key is both stations being equidistant from the geomagnetic equator.

## Slide 10
Long-Path, 160m, and Chordal Hop
Long-path propagation: signals travel the 'long way' around Earth (>180 degrees of arc)
→ Most frequent on 40m and 20m
→ Point antenna in the OPPOSITE direction from normal short-path
→ When short-path is blocked or noisy, long-path sometimes gives a better signal
160m (1.8 MHz) propagation:
→ Path must be ENTIRELY in darkness — even a short illuminated segment causes absorption
→ Best windows: around your local sunrise/sunset
Chordal hop: successive ionospheric refractions without ground touching between hops
→ Less loss than standard hops (no ground absorption)
→ Lower elevation angle = longer individual hop distance
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: The 160m darkness requirement is a real operating consideration for DXers. EU-NA contacts require careful timing around the gray line (sunrise/sunset terminator). The path has to be dark all the way across.

## Slide 11
Sporadic E and Ground Wave
Sporadic E (Es): random patches of intense ionization in the E layer
→ Peak occurrence: around solstices, especially summer (June-July N. hemisphere)
→ Occurs most often between sunrise and sunset
→ Can enable DX on 6m, 2m, 10m without F-layer support
→ Unpredictable — check DX clusters and spotting networks
Ordinary and extraordinary waves:
→ Two waves that propagate independently through the ionosphere
→ Both are elliptically polarized
Ground wave: travels along Earth's surface
→ Uses vertical polarization
→ Range decreases as frequency increases
→ Very reliable for short distances on 160m and 80m
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: Sporadic E is a favorite topic on 6m and 2m. When the band 'opens,' stations thousands of miles away suddenly appear out of nowhere, and then vanish. Encourage students to watch DX maps during summer for Es openings.

## Slide 12
Part 3: Space Weather
Subelement E3C — 1 exam question
Notes: Space weather drives HF propagation. Students who operate HF quickly learn to check the solar indices before calling CQ. This section is mostly memorization of what each index means.

## Slide 13
Space Weather Indices
Solar Flux Index (SFI) | UV/EUV from Sun; higher = better HF propagation
A-index | Daily geomagnetic average (0-400); rising = worse HF
K-index | 3-hour geomagnetic reading (0-9); K>4 = disrupted HF
Bz (north-south IMF) | Southward Bz = more geomagnetic disturbance
G-scale storms | G1 (minor) through G5 (extreme)
Solar flare class X | Most intense class; causes HF radio blackouts
304A parameter | UV emissions; correlated with solar flux index
VOACAP | HF propagation prediction software
Auroral oval when A/K high | High absorption on polar paths; auroral scatter on VHF
Sudden HF noise increase | CME impact or solar flare in progress
VHF radio horizon | ~15% farther than geographic horizon
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: The exam typically asks about what a rising A-index means (worsening conditions), what a southward Bz means, or what the strongest solar flare class is.

## Slide 14
Part 4: Test Equipment
Subelement E4A — 1 exam question
Notes: This section is more practical than theoretical. Most students have seen an oscilloscope or spectrum analyzer. Relate these to real amateur radio troubleshooting scenarios.

## Slide 15
Oscilloscope and Spectrum Analyzer
Digital oscilloscope:
→ Displays voltage vs. TIME
→ Sampling rate limits the highest frequency that can be accurately displayed
→ Aliasing: if signal frequency > half the sampling rate, it appears at a false lower frequency
→ Probe compensation: feed a square wave, adjust trimmer for flat top (no overshoot)
→ Line trigger (AC power line sync): best mode for measuring power supply ripple
Spectrum analyzer:
→ Displays AMPLITUDE vs. FREQUENCY
→ Vertical axis = amplitude (usually in dBm)
→ Horizontal axis = frequency
→ Best tool for viewing spurious emissions, harmonics, and IMD products
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: Oscilloscope = time domain. Spectrum analyzer = frequency domain. Both are critical test tools. An oscilloscope shows you the waveform shape; a spectrum analyzer shows you all the frequency components simultaneously.

## Slide 16
Antenna Analyzer and Frequency Counter
Antenna analyzer:
→ Computes SWR and feed point impedance
→ Can measure velocity factor of coax (from electrical length vs. physical length)
→ Can find cable length by measuring resonant frequency of a shorted stub
→ Can find resonant frequency of an antenna
Frequency counter:
→ Measures frequency by counting cycles over a precise time interval
→ Accuracy is determined by the time base (reference oscillator) accuracy
→ Better oscillator = more accurate counter
Prescaler:
→ Reduces a high-frequency signal to within the counter's operating range
→ Divides frequency by a known factor (e.g., divide by 10 or 100)
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: Students often confuse what an antenna analyzer measures vs. an SWR meter. An SWR meter only reads SWR; an antenna analyzer also gives impedance (R and X) and can do cable measurements.

## Slide 17
VNA and Measurement Techniques (E4B)
VNA (Vector Network Analyzer): measures S-parameters of RF circuits
→ Calibration: short circuit + open circuit + 50-ohm load — establishes reference planes
→ Two-port VNA: measures filter frequency response
S11 = input return loss / input VSWR (reflection at input port)
S21 = forward gain (signal from port 1 to port 2)
Directional wattmeter: measures forward and reflected power
→ Power absorbed = forward power - reflected power
→ Example: 100W forward, 25W reflected: 75W absorbed
Q measurement: Q = resonant frequency / 3-dB bandwidth
IMD measurement: inject two non-harmonically related tones; view IMD products on spectrum analyzer
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: VNA calibration removes errors from the test fixture and cables. Without calibration, you're measuring the cable, not the device under test. The short-open-50-ohm cal kit is fundamental — have students memorize these three steps.

## Slide 18
Part 5: Receiver Performance
Subelements E4C-D — 1 exam question
Notes: Receiver performance is the densest section in this module. Dynamic range, noise figure, blocking — these concepts explain why some radios work better than others. Relate to students' own radios where possible.

## Slide 19
Noise and Sensitivity
Thermal noise floor: -174 dBm in 1 Hz bandwidth at room temperature
Noise figure (NF): how much the receiver adds above the thermal minimum
MDS (Minimum Discernible Signal): weakest detectable signal in the receiver
Bandwidth increases noise floor:
→ 50 Hz to 1000 Hz: 10 x log10(1000/50) = +13 dB noise floor increase
→ Narrower filter = lower noise floor = weaker signals detectable
Phase noise in SDR master clock: LO phase noise mixes with nearby strong signals
→ Creates in-band interference that looks like receiver noise
Preselector/front-end filter: bandpass filter eliminating strong out-of-band signals before the LNA
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: Ask: why does switching from 500 Hz to 2700 Hz CW bandwidth on your radio increase noise? Because you're letting in more of the noise floor. Narrow filters are not just for selectivity — they reduce noise too.

## Slide 20
Dynamic Range and Blocking
Blocking dynamic range: range from noise floor to signal level causing 1 dB gain compression
→ A strong nearby signal compresses the front end — nearby signals get weaker
Third-order intercept point (IP3):
→ Theoretical signal level where IMD products equal the input signal
→ Higher IP3 = better receiver in crowded band conditions
Reciprocal mixing: LO phase noise mixes with adjacent strong signal → creates interference
Roofing filter: wide crystal filter at first IF — reduces reciprocal mixing effects
High IF frequency: image is farther away — easier to reject
SDR overload: input signal exceeds ADC reference voltage → add attenuation
Desensitization: strong nearby signal compresses front-end gain
→ Fix: insert attenuation before the first RF stage
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: The roofing filter is why expensive radios sound better on crowded contest bands. A wide roofing filter lets strong adjacent signals interact with LO phase noise; a tight one doesn't. This directly explains the price difference between radios.

## Slide 21
Noise and Interference Sources (E4E)
Noise Sources
Switch-mode power supplies: broadband noise at regular frequency intervals across HF
Power line noise: buzzing, worst on low HF
Corroded metal: rusty bolt effect — mixes and reradiates broadcast signals
Ignition noise: impulse noise from vehicles
Common-mode current: flows equally on all conductors
Mitigations
ANF (Auto Notch Filter): removes carriers and CW — but also removes a desired CW signal
Noise Blanker: impulse noise; can distort strong signals
Digital NR: broadband and power line noise
Ferrite choke on power cables: blocks common-mode
Single point ground panel: all protectors activate simultaneously
TavaOne Education — Amateur Extra
E3-E4 · Propagation & Practices
Notes: The rusty bolt effect has caught many operators off guard — a piece of corroded galvanized pipe or an old tower section can generate spurious signals. The fix is to find and clean or replace the corroded junction.

## Slide 22
Checkpoint Quiz 1 / 10
What type of fading is associated with EME propagation?
A. Multipath fading
B. Libration fading
C. Rayleigh fading
D. Selective fading
Answer: B — Libration fading: Moon's wobble causes rapid irregular signal variations
Notes: B is the answer. Libration = Moon wobble. The word 'fluttery' in the pool options is a giveaway.

## Slide 23
Checkpoint Quiz 2 / 10
Which mode is best suited for meteor scatter propagation?
A. FT8
B. Q65
C. MSK144
D. WSPR
Answer: C — MSK144 is designed for the very short burst duration of meteor scatter
Notes: Q65 is for EME. FT8 is too slow for meteor bursts. MSK144 is the meteor scatter mode.

## Slide 24
Checkpoint Quiz 3 / 10
Why is CW preferred for auroral propagation?
A. CW requires less power
B. Auroral reflection distorts audio — phone signals are unintelligible
C. The aurora only reflects CW frequencies
D. CW has a narrower beamwidth
Answer: B — Auroral reflection distorts audio; CW tone is still copyable through the distortion
Notes: SSB audio through the aurora sounds like white noise with a buzz. CW is just a tone, which survives.

## Slide 25
Checkpoint Quiz 4 / 10
What does a southward Bz indicate?
A. Improved HF propagation
B. Enhanced sporadic E
C. Increasing geomagnetic disturbance
D. Higher solar flux
Answer: C — Southward Bz couples energy into the magnetosphere, increasing disturbance
Notes: North = benign; South = trouble. Southward Bz is how solar wind energy gets into the magnetosphere.

## Slide 26
Checkpoint Quiz 5 / 10
What does aliasing on a digital oscilloscope look like?
A. Overshoot on square wave edges
B. A signal appearing at a false lower frequency
C. Loss of vertical resolution
D. Baseline drift
Answer: B — Aliasing: undersampled signal appears at a false (lower) frequency
Notes: Nyquist says sample at 2x the signal frequency. If you don't, the math wraps the frequency around and you see it at a phantom lower frequency.

## Slide 27
Checkpoint Quiz 6 / 10
What is the primary factor determining frequency counter accuracy?
A. Input impedance
B. Display resolution
C. Time base accuracy
D. Prescaler ratio
Answer: C — Counter accuracy is determined by the accuracy of its time base (reference oscillator)
Notes: The counter counts cycles over a time interval defined by its oscillator. If the oscillator drifts, every measurement drifts with it.

## Slide 28
Checkpoint Quiz 7 / 10
In a VNA two-port measurement, what does S21 represent?
A. Input return loss
B. Output return loss
C. Forward gain from port 1 to port 2
D. Reverse isolation
Answer: C — S21: signal into port 1, measured at port 2 — forward gain
Notes: S-parameter subscript convention: first digit = output port, second = input port. S21: out of port 2, in from port 1.

## Slide 29
Checkpoint Quiz 8 / 10
A receiver's noise floor increases by how many dB when bandwidth goes from 50 Hz to 1000 Hz?
A. 10 dB
B. 3 dB
C. 20 dB
D. 13 dB
Answer: D — 10 x log10(1000/50) = 10 x 1.301 = 13 dB
Notes: Calculate it: 1000/50 = 20. log10(20) = 1.30. Times 10 = 13 dB. This number appears directly on the exam.

## Slide 30
Checkpoint Quiz 9 / 10
What is the rusty bolt effect?
A. Coax connector corrosion increasing SWR
B. Corroded metal connections mixing and reradiating broadcast signals
C. Galvanic corrosion in antenna elements
D. Moisture in antenna insulators
Answer: B — Corroded metal junctions act as passive mixers, generating spurious signals from nearby broadcast stations
Notes: Any corroded metal joint near your antenna can be the source — old gutters, towers, fence posts. The fix is finding and cleaning it.

## Slide 31
Checkpoint Quiz 10 / 10
Which receiver filter improves blocking dynamic range?
A. Audio low-pass filter
B. ANF
C. Roofing filter
D. Noise blanker
Answer: C — Roofing filter (crystal filter at first IF) reduces reciprocal mixing and improves blocking dynamic range
Notes: The roofing filter is what separates a $500 radio from a $5000 radio in contest conditions. It limits which strong signals can interact with LO phase noise.

## Slide 32
Before Module 3
Your assignment:
Drill HamStudy E3A-E3C and E4A-E4E to 80%+ confidence
Focus extra time on E4C-D (receiver performance) — most students find it the hardest
E4B (S-parameters, directional wattmeter): get those formulas locked in
Coming up:
Module 3: Electrical Principles — resonance, Q, time constants, phasors. Only 4 exam questions but critical foundation for Modules 5 and 7. Come with a calculator.
Notes: Wrap up and send students to HamStudy.