## Slide 1
Module 3: Electrical Principles
Resonance · Q · Time Constants · Phasors · RF Effects
2024-2028 Amateur Extra Question Pool
TavaOne Education · Pinellas STEM Radio Lab
Notes: Module 3 opening slide.

## Slide 2
Why This Module Matters
Only 4 exam questions from E5 — but don't let that fool you
E5 is the math foundation for:
→ Module 5 (E7): amplifier biasing, filter design, op-amp calculations
→ Module 7 (E9): antenna impedance, transmission line matching, Smith chart
If you skip this math, you miss questions in those heavier modules
What we cover:
→ RLC resonance (series and parallel) and Q factor
→ RC and RL time constants
→ Phase angles in RLC circuits
→ Rectangular and polar impedance notation
→ Skin effect and reactive power
Bring a calculator — we will work practice problems
TavaOne Education — Amateur Extra
E5 · Electrical Principles
Notes: Set the expectation: this is the math session. It's not the most fun, but it's the one that unlocks everything else. Students who skip this and wonder why the Smith chart makes no sense later — it's because they didn't do this.

## Slide 3
Part 1: RLC Resonance and Q
Subelement E5A — 1 exam question
Notes: Resonance is the single concept that underlies filters, tank circuits, and antenna tuners. Get this solid before moving on.

## Slide 4
Series RLC Resonance
At resonance: XL = XC (inductive and capacitive reactances are equal)
Series circuit behavior at resonance:
→ Total impedance = resistance only (MINIMUM impedance — current is maximum)
→ Voltage across L or C can EXCEED the applied voltage
→ The Q ratio tells you how much: VL (or VC) = Q × Vapplied
Resonant frequency formula:
f = 1 / (2π × sqrt(L × C))
→ f in Hz, L in henrys, C in farads
→ Example: L = 10 uH, C = 100 pF → f = 1/(2π × sqrt(10e-6 × 100e-12)) = 5.03 MHz
TavaOne Education — Amateur Extra
E5 · Electrical Principles
Notes: Work the example on the board. Have students plug it in on their calculators. sqrt(10e-6 × 100e-12) = sqrt(1e-15) = 3.162e-8. Then 1/(2π × 3.162e-8) = 5.03 MHz. Make them get the same number.

## Slide 5
Parallel RLC Resonance and Q Factor
Parallel circuit at resonance:
→ Impedance is at MAXIMUM (approximately R × Q²)
→ Source current is at MINIMUM
→ Circulating current between L and C is at MAXIMUM
Q Factor:
→ Series circuit: Q = XL/R (reactance-to-resistance ratio)
→ Parallel circuit: Q = R/XL
→ Higher Q = narrower bandwidth, higher internal voltages/currents
Half-power bandwidth: BW = f_resonant / Q
→ Example: f = 7.2 MHz, Q = 80 → BW = 7,200,000/80 = 90 kHz
→ The -3 dB points of the resonance curve are at ±45 kHz from center
TavaOne Education — Amateur Extra
E5 · Electrical Principles
Notes: Sketch the resonance curve on the board: a peak at resonance with the bandwidth measured between the two -3 dB points. High Q = tall narrow peak. Low Q = short wide peak. Same area under the curve.

## Slide 6
Part 2: Time Constants and Phase
Subelement E5B — 1 exam question
Notes: Time constants are the key to understanding filters, amplifier coupling, and how fast circuits respond to changes.

## Slide 7
RC and RL Time Constants
RC time constant: τ = R × C
→ After 1τ: 63.2% of final voltage charged (36.8% remaining)
→ After 5τ: effectively fully charged
→ Example: R = 10kΩ, C = 1μF → τ = 10,000 × 0.000001 = 0.01 s = 10 ms
RL time constant: τ = L/R
→ Same 63.2% rule applies to current rise
→ Example: L = 10 mH, R = 100Ω → τ = 0.01/100 = 100 μs
Phase relationships — ELI the ICEman:
→ ELI: in an inductor (L), voltage (E) leads current (I)
→ ICE: in a capacitor (C), current (I) leads voltage (E)
→ Both by 90 degrees
TavaOne Education — Amateur Extra
E5 · Electrical Principles
Notes: Draw the charging curve: starts at 0, climbs steeply, then flattens asymptotically toward full voltage. Mark the 63.2% point at one time constant. Students find the 63.2% number strange — explain it comes from (1-1/e).

## Slide 8
Phase Angle in Series RLC
Phase angle formula:
tan(θ) = (XL - XC) / R
Examples:
→ XL = 100, XC = 60, R = 40: tan(θ) = 40/40 = 1.0 → θ = 45° (inductive)
→ XL = 30, XC = 80, R = 50: tan(θ) = -50/50 = -1.0 → θ = -45° (capacitive)
→ At resonance: XL = XC → tan(θ) = 0 → θ = 0° (purely resistive)
Admittance: Y = 1/Z (measured in siemens)
Susceptance: B = 1/X (imaginary part of admittance)
Conductance: G = 1/R (real part of admittance)
Polar to admittance: reciprocal of magnitude, negate the angle
TavaOne Education — Amateur Extra
E5 · Electrical Principles
Notes: Have students work the first example on paper: tan(theta)=(100-60)/40 = 1.0, theta = arctan(1.0) = 45 degrees. The positive result means inductive (XL > XC). This is a direct exam calculation.

## Slide 9
Part 3: Rectangular and Polar Notation
Subelement E5C — 1 exam question
Notes: Impedance notation shows up constantly in antenna and circuit work. Being fluent in rectangular and polar notation is essential for the Smith chart in Module 7.

## Slide 10
Rectangular Notation: R + jX
Rectangular form: R + jX
→ R = resistance (real part) — plotted on horizontal axis
→ jX = reactance (imaginary part) — plotted on vertical axis
→ Positive jX = INDUCTIVE (above horizontal)
→ Negative jX = CAPACITIVE (below horizontal)
Examples:
→ 50 + j0: purely resistive (50-ohm load, perfect match)
→ 0 + j100: pure inductance 100Ω
→ 0 - j100: pure capacitance 100Ω
→ 50 + j75: resistive + inductive
→ 50 - j25: resistive + capacitive
TavaOne Education — Amateur Extra
E5 · Electrical Principles
Notes: Draw the rectangular coordinate system: horizontal = R, vertical = jX. Inductive above the line, capacitive below. Every impedance is a point in this plane.

## Slide 11
Polar Notation and Conversion
Polar form: magnitude ∠ angle
→ Magnitude = sqrt(R² + X²)
→ Angle = arctan(X/R)
→ Pure inductance: +90° angle
→ Pure capacitance: -90° angle
→ Pure resistance: 0° angle
Converting Z = 30 + j40:
→ Magnitude = sqrt(30² + 40²) = sqrt(900+1600) = sqrt(2500) = 50Ω
→ Angle = arctan(40/30) = arctan(1.33) = 53.1°
→ Polar: 50∠53.1°
Frequency response graphs: logarithmic Y-axis shows amplitude in dB
TavaOne Education — Amateur Extra
E5 · Electrical Principles
Notes: Work the 3-4-5 triangle: 30² + 40² = 900 + 1600 = 2500, sqrt = 50. Students who remember Pythagorean theorem will find this comfortable.

## Slide 12
Part 4: RF Effects
Subelement E5D — 1 exam question
Notes: RF effects explain why components that work perfectly at 60 Hz cause problems at 100 MHz. These are practical concepts every Extra-class operator should understand.

## Slide 13
Skin Effect and RF Resistance
Skin effect: at RF, current flows near the surface of the conductor — not through the full cross-section
→ Effective resistance INCREASES with frequency
→ Skin depth decreases as frequency increases
→ At VHF/UHF: keep lead lengths short to minimize added inductive reactance
→ At microwave: keep connections short to reduce phase shift
→ Film capacitors at RF: skin effect in the foil causes loss
Electrical length:
→ Conductor diameter affects electrical length — larger diameter = slightly longer electrical length
Component pitfalls at RF:
→ Electrolytic capacitors: high parasitic inductance — don't use for RF bypass
→ Inductor self-resonance: inter-turn capacitance creates parallel resonance above some frequency
→ Long wire leads: significant inductive reactance at VHF/UHF
TavaOne Education — Amateur Extra
E5 · Electrical Principles
Notes: A simple demo: ask what's wrong with using a 100μF electrolytic as a bypass capacitor on a VHF transmitter. Answer: at 100 MHz its parasitic inductance makes it look like an inductor, not a capacitor.

## Slide 14
Real vs. Reactive Power
Real power (watts): converts electrical energy to heat (or work)
→ P = I² × R — only the resistive component dissipates power
Reactive power (VAR — volt-amperes reactive):
→ Energy stored in electric field (capacitor) or magnetic field (inductor)
→ Energy is returned to the circuit — not dissipated
→ Reactive power is 90° out of phase with real power
In a series R + jX circuit:
→ Current is the same through all components
→ Voltage across X is 90° out of phase with voltage across R
→ P = I² × R (NOT I² × Z)
→ The reactive component does not contribute to heat
Practical example: a tuner with a lossless inductor dissipates zero power in the coil
TavaOne Education — Amateur Extra
E5 · Electrical Principles
Notes: This explains why a loaded antenna with high SWR can still radiate effectively — the reactive power sloshes back and forth but the real power still goes out. A lossy tuner wastes real power in the coil resistance.

## Slide 15
Key Numbers — Module 3
Resonant frequency | f = 1/(2π·sqrt(LC))
Series resonance | Minimum Z; XL=XC; max current
Parallel resonance | Maximum Z; min source current
Q (series) | XL/R at resonance
Half-power BW | f_r / Q
RC time constant | τ = RC
RL time constant | τ = L/R
1 time constant | 63.2% of final value
ELI the ICEman | Inductor: V leads I; Capacitor: I leads V
Phase angle | tan(θ) = (XL - XC)/R
Rectangular +jX | Inductive
Rectangular -jX | Capacitive
Polar magnitude | sqrt(R² + X²)
Admittance | Y = 1/Z (siemens)
Skin effect | RF resistance increases with frequency
Real power formula | P = I²R (not I²Z)
TavaOne Education — Amateur Extra
E5 · Electrical Principles
Notes: Quick self-quiz: cover the right column, call out the left.

## Slide 16
Checkpoint Quiz 1 / 10
What is the resonant frequency of a circuit with L = 4 μH and C = 25 pF?
A. 31.8 MHz
B. 15.9 MHz
C. 7.96 MHz
D. 3.98 MHz
Answer: B — f = 1/(2π×sqrt(4e-6×25e-12)) = 1/(2π×1e-8) = 15.9 MHz
Notes: sqrt(4e-6 × 25e-12) = sqrt(1e-16) = 1e-8. Then 1/(2π×1e-8) = 15.92 MHz.

## Slide 17
Checkpoint Quiz 2 / 10
In a series RLC circuit at resonance, what is the impedance?
A. Zero
B. The inductive reactance
C. The resistance only
D. Sum of all reactances
Answer: C — At resonance, XL = XC and cancel; impedance = resistance only
Notes: This is the definition of resonance in a series circuit. Minimum impedance, maximum current.

## Slide 18
Checkpoint Quiz 3 / 10
What is the half-power bandwidth of a circuit where f = 3.5 MHz and Q = 70?
A. 245 kHz
B. 100 kHz
C. 50 kHz
D. 25 kHz
Answer: C — BW = f/Q = 3,500,000/70 = 50,000 Hz = 50 kHz
Notes: Simple division. 3.5M/70 = 50k. The half-power points are at ±25 kHz from the center.

## Slide 19
Checkpoint Quiz 4 / 10
What is the time constant of R = 47kΩ and C = 0.1 μF?
A. 4.7 ms
B. 47 ms
C. 0.47 ms
D. 470 μs
Answer: A — τ = R×C = 47,000 × 0.0000001 = 0.0047 s = 4.7 ms
Notes: Watch units: 47k × 0.1μ = 47,000 × 0.0000001 = 0.0047 seconds = 4.7 ms

## Slide 20
Checkpoint Quiz 5 / 10
In a capacitive circuit, current relates to voltage how?
A. Current lags voltage 90°
B. Current leads voltage 90°
C. In phase
D. Current leads by 45°
Answer: B — ICE: In a Capacitor, current (I) leads voltage (E) by 90°
Notes: ELI the ICEman: L → voltage leads current. C → current leads voltage.

## Slide 21
Checkpoint Quiz 6 / 10
What is the rectangular form of a pure 100Ω capacitive reactance?
A. 100 + j0
B. 0 + j100
C. 0 - j100
D. j100
Answer: C — Pure capacitive reactance: 0 - j100 (negative j indicates capacitive)
Notes: No resistance (0 on the real axis). Capacitive = negative imaginary. Inductive = positive.

## Slide 22
Checkpoint Quiz 7 / 10
Series circuit: XL=80, XC=30, R=50. Phase angle?
A. 22°
B. 45°
C. 90°
D. 63°
Answer: B — tan(θ)=(80-30)/50 = 50/50 = 1.0; arctan(1.0) = 45° inductive
Notes: tan(theta) = (XL-XC)/R = (80-30)/50 = 1.0. arctan(1.0) = 45 degrees. Positive = inductive.

## Slide 23
Checkpoint Quiz 8 / 10
Why are electrolytic capacitors unsuitable for RF bypass?
A. Too low capacitance
B. Excessive parasitic inductance
C. Too high voltage rating
D. Too low ESR
Answer: B — Electrolytic capacitors have high parasitic lead inductance; they act as inductors at RF
Notes: The aluminum foil windings create inductance. At RF frequencies this dominates and the capacitor is no longer capacitive.

## Slide 24
Checkpoint Quiz 9 / 10
What causes an inductor to self-resonate?
A. Skin effect
B. Inter-turn capacitance
C. Core saturation
D. Eddy currents
Answer: B — Inter-turn capacitance between adjacent windings creates a parallel LC; above self-resonant frequency it appears capacitive
Notes: Every winding is a tiny capacitor plate relative to the next winding. At high enough frequency this capacitance dominates.

## Slide 25
Checkpoint Quiz 10 / 10
Why is real power P = I²R rather than I²Z?
A. Reactance cancels at resonance
B. Only resistance dissipates power; reactive elements return energy
C. Z always equals R at RF
D. Different current flows through X and R
Answer: B — Reactive components store and return energy; only R converts energy to heat
Notes: P = V × I × cos(θ). The cosine factor accounts for the phase angle; only the in-phase component does real work.

## Slide 26
Before Module 4
Your assignment:
Drill HamStudy E5A-E5D to 80%+ confidence
Practice the resonance frequency calculation — it appears directly on the exam
Know the phase angle formula: tan(θ) = (XL-XC)/R
Coming up:
Module 4: Circuit Components — semiconductors, diode types, digital ICs, inductors, optical devices. Heavier on memorization than math, but schematic symbol recognition is tested.
Notes: Wrap up and send students to HamStudy.