## Slide 1
Module 4: Circuit Components
Semiconductors · Diodes · Digital ICs · Inductors · RF Packaging
2024-2028 Amateur Extra Question Pool
TavaOne Education · Pinellas STEM Radio Lab
Notes: Module 4 opening slide.

## Slide 2
Module 4 Overview
6 exam questions — E6A through E6F — 12% of your Extra exam
This module is heavier on identification than calculation
Hour 1:
→ E6A: Semiconductor materials and transistors
→ E6B: Diode types and their applications
Hour 2:
→ E6C: Digital ICs — CMOS, logic gates, FPGAs
→ E6D: Inductors, transformers, core materials, crystals
→ E6E-F: RF semiconductors, IC packaging, electro-optics
Focus areas: diode type identification is heavily tested. Know Zener vs. Schottky vs. PIN vs. varactor.
TavaOne Education — Amateur Extra
E6 · Circuit Components
Notes: Schematic symbol recognition is referenced in the pool (Figures E6-1, E6-2, E6-3) but tested conceptually in the written question. Focus on what each device does and when you'd use it.

## Slide 3
Part 1: Semiconductors and Transistors
Subelement E6A — 1 exam question
Notes: Start with the materials, then transistor types. GaAs vs Si vs GaN is a reliable exam topic.

## Slide 4
Semiconductor Materials
Materials
Silicon (Si): most common; moderate electron mobility
GaAs: higher electron mobility → microwave use
GaN: highest electron mobility + power density → UHF/SHF power amps, highest MMIC freq
N-type: excess free electrons (donor impurity)
P-type: excess holes (acceptor impurity)
PN junction reverse bias: depletion widens; no current
Transistor Types
BJT: current-controlled; beta = ΔIc/ΔIb
NPN turns on at Vbe ~0.6-0.7V
FET: voltage-controlled; higher input impedance than BJT
Depletion-mode FET: conducts with no gate voltage
Enhancement-mode MOSFET: OFF with no gate voltage
Dual-gate MOSFET: two gates for AGC or mixing
MOSFET gate protection: Zener diodes clamp against ESD
TavaOne Education — Amateur Extra
E6 · Circuit Components
Notes: GaAs vs Si: same physical size, 6x the electron speed. That's why microwave MMICs use GaAs — the transistors can switch faster. GaN adds high power density on top of the speed.

## Slide 5
BJT vs FET
BJT (Bipolar Junction Transistor):
→ Base current controls collector current
→ Beta (hFE) = collector current / base current
→ Consumes input current — lower input impedance
→ Good for high-frequency amplifiers; saturates easily
FET (Field Effect Transistor):
→ Gate VOLTAGE controls drain current
→ Almost zero gate current — very high input impedance
→ JFET: depletion type (reverse bias gate reduces current)
→ MOSFET: enhancement (common) or depletion type
→ Gate isolation: SiO2 layer or PN junction
Alpha cutoff frequency: frequency where grounded-base current gain falls to 0.707 (−3 dB) of low-frequency value
TavaOne Education — Amateur Extra
E6 · Circuit Components
Notes: The most important practical difference: BJT draws current at its input (base), FET draws almost none at its input (gate). This makes FETs ideal for high-impedance signal sources and mixers.

## Slide 6
Part 2: Diode Types
Subelement E6B — 1 exam question
Notes: Diode identification is heavily tested. Know all five types cold: Zener, Schottky, PIN, varactor, LED.

## Slide 7
Diode Types and Applications
Zener: conducts in reverse breakdown at a specific voltage — voltage regulation, clamping
Schottky: metal-semiconductor junction
→ Lower forward voltage drop (~0.2-0.4V vs 0.6-0.7V for silicon)
→ Fast switching; VHF/UHF mixer and detector
Varactor (varicap): PN junction used in reverse bias
→ Junction capacitance varies with voltage — voltage-controlled capacitor
→ Used in VCOs, AFC, phase modulators
PIN diode: P-Intrinsic-N structure
→ Low junction capacitance at RF
→ Controlled by forward DC bias current — acts as variable RF resistor
→ Used as RF switch or attenuator
LED: forward voltage set by semiconductor band gap
Point-contact diode: metal point on semiconductor — RF detector
Common failure mode: excessive junction temperature from overcurrent
TavaOne Education — Amateur Extra
E6 · Circuit Components
Notes: Mnemonic for the exam: 'ZVPL' — Zener (voltage reg), Varactor (variable C), PIN (RF switch), LED (light). Schottky is the fast low-drop one for VHF work.

## Slide 8
Part 3: Digital ICs
Subelement E6C — 1 exam question
Notes: Focus on CMOS characteristics and logic gate truth tables. FPGA programming language is also a reliable exam question.

## Slide 9
Logic Families and Gate Behavior
CMOS vs Others
CMOS: lowest power consumption (near-zero static current)
CMOS threshold: ~half supply voltage
CMOS noise immunity: high (wide margin between 0 and 1)
BiCMOS: CMOS input impedance + bipolar output drive
Tri-state: three states — 0, 1, high-impedance (disconnected)
Pull-up resistor: holds pin HIGH when open
Pull-down resistor: holds pin LOW when open
Comparator hysteresis: prevents chatter on noisy inputs
Gate Truth Tables
NAND: output=0 only when ALL inputs are 1
NOR: output=1 only when ALL inputs are 0
OR: output=1 if ANY input is 1
AND: output=1 only when ALL inputs are 1
XOR: output=1 when inputs DIFFER
XNOR: output=0 when inputs differ
NOT: inverts the input
FPGA: programmed with HDL (VHDL or Verilog)
TavaOne Education — Amateur Extra
E6 · Circuit Components
Notes: NAND is the 'universal gate' — you can build any other logic function from NANDs alone. This is why it shows up on the exam.

## Slide 10
Part 4: Inductors, Transformers, Crystals
Subelement E6D — 1 exam question
Notes: Core material selection is heavily tested. Ferrite vs powdered iron comes up regularly.

## Slide 11
Core Materials and Transformer Basics
Ferrite: high permeability → fewer turns needed for same inductance
→ More temperature-sensitive than powdered iron
→ Used for HF transformers, chokes, baluns
Powdered iron: lower permeability; better temperature stability
→ Used for HF inductors where frequency stability matters more
Brass core: DECREASES inductance (diamagnetic material)
Air core: no core loss, no saturation — VHF/UHF inductors
Laminated cores: thin insulated layers reduce eddy current losses (power transformers)
Toroidal core: confines magnetic field; low external radiation
Magnetizing current: flows in primary even with no secondary load
Inductor saturation: core flux exceeds capacity — inductance collapses
Ferrite beads: suppress VHF/UHF parasitic oscillations on leads
TavaOne Education — Amateur Extra
E6 · Circuit Components
Notes: Brass vs ferrite: brass decreases inductance (brass is non-magnetic — it actually slightly opposes the field). Ferrite dramatically increases inductance. This is a reliable test question.

## Slide 12
Quartz Crystals and Piezoelectric Devices
Quartz crystal equivalent circuit:
→ Series RLC (the mechanical resonance) in PARALLEL with a shunt capacitor
→ The shunt C is the electrode capacitance of the package
→ Series resonance: lower frequency, lower impedance
→ Parallel resonance: slightly higher frequency, very high impedance
Piezoelectric effect:
→ Mechanical stress → voltage
→ Applied voltage → mechanical deformation
→ Used in: quartz crystals, ceramic resonators, crystal filters, microphones, buzzers
Permeability: determines how well a core material supports magnetic flux
→ Higher permeability = more inductance per turn
TavaOne Education — Amateur Extra
E6 · Circuit Components
Notes: A crystal oscillator works because the mechanical resonance of the quartz is extremely stable. The crystal is physically vibrating at its resonant frequency. Temperature changes affect the resonant frequency — hence TCXOs and OCXOs.

## Slide 13
Part 5: RF Semiconductors and Packaging
Subelements E6E-F — 1 exam question
Notes: RF packaging choices directly affect circuit performance above VHF. Surface mount vs through-hole is a practical decision, not just an aesthetic one.

## Slide 14
RF and Microwave Semiconductors
GaAs FET: high electron mobility; low noise figure — microwave LNA and oscillators
GaN HEMT: highest electron mobility + power density
→ Used for UHF/SHF power amplifiers
→ GaN supports the HIGHEST frequencies in MMIC applications
MMIC (Monolithic Microwave Integrated Circuit):
→ Input and output impedance: 50 ohms
→ Controlled gain and low noise figure
→ DC power supplied through resistor or RF choke on the OUTPUT lead
→ Never feed DC through the input — sensitive to any impedance change
Microstrip: printed circuit board transmission line
→ Impedance determined by trace width and substrate thickness
→ Used to connect MMIC components with controlled impedance
TavaOne Education — Amateur Extra
E6 · Circuit Components
Notes: The 50-ohm standard is arbitrary but universal — everything designed around it, so all pieces interconnect. The MMIC output DC injection convention catches students off guard. It's on the output, not the input, so the input impedance isn't disturbed.

## Slide 15
IC Packaging and Electro-Optics
IC Packaging at RF
SMD (Surface Mount): shortest leads, least parasitic inductance — best above HF
DIP (Dual In-Line): through-hole; long leads = parasitic inductance; limited to HF
SOP/SOT/QFP: surface mount variants
Rule: smaller package = better at higher frequencies
DIP is unusable at UHF due to lead inductance
Electro-Optical Devices
Photovoltaic cell: light → electrical energy (photovoltaic effect); Si cell ~0.5V open circuit
Photoconductive material: more light = less resistance
Optoisolator (optocoupler):
→ LED + phototransistor in one package
→ Complete galvanic isolation between circuits
→ Used to interface logic to power circuits safely
TavaOne Education — Amateur Extra
E6 · Circuit Components
Notes: Optoisolators are everywhere in industrial electronics because they break ground loops and protect logic circuits from power transients. The LED side might be at ground; the phototransistor side at 120VAC potential.

## Slide 16
Key Facts — Module 4
GaAs advantage | Higher electron mobility than Si
GaN application | Highest MMIC frequencies; UHF power amps
FET vs BJT | FET = higher input impedance
NPN turn-on voltage | Vbe ~0.6-0.7V
Depletion-mode FET | Conducts with zero gate voltage
Zener diode | Constant voltage in reverse breakdown
Schottky diode | Low Vf; metal-semiconductor; fast; VHF mixer
Varactor | Voltage-controlled capacitor (reverse biased)
PIN diode | RF switch; DC forward bias controls RF resistance
CMOS power | Near-zero static power
CMOS threshold | ~Half supply voltage
FPGA programmed with | HDL (Hardware Description Language)
Ferrite vs powdered iron | Ferrite = fewer turns; pow. iron = better temp stability
Brass core effect | DECREASES inductance
Crystal eq circuit | Series RLC ¦¦ shunt capacitor
MMIC I/O impedance | 50 ohms; DC fed through OUTPUT lead
SMD advantage | Least parasitic inductance at RF
Optoisolator | LED + phototransistor; electrical isolation
TavaOne Education — Amateur Extra
E6 · Circuit Components
Notes: Cover the right column. Call the left. 2 minutes.

## Slide 17
Checkpoint Quiz 1 / 10
Which semiconductor material is used in microwave MMICs due to its higher electron mobility?
A. Silicon
B. Germanium
C. GaAs
D. Silicon carbide
Answer: C — GaAs has significantly higher electron mobility than silicon
Notes: GaN is even faster but GaAs came first for MMICs. Both are correct for microwave — GaAs is the traditional answer.

## Slide 18
Checkpoint Quiz 2 / 10
What is the primary advantage of a Schottky diode vs a silicon PN diode?
A. Higher reverse breakdown voltage
B. Lower forward voltage drop
C. Higher junction capacitance
D. Better temperature stability
Answer: B — Schottky: ~0.2-0.4V forward drop vs 0.6-0.7V for silicon PN
Notes: The metal-semiconductor junction is what makes Schottky faster and lower drop. No minority carrier storage.

## Slide 19
Checkpoint Quiz 3 / 10
What type of diode is used as a voltage-controlled capacitor?
A. PIN diode
B. Schottky
C. Zener
D. Varactor
Answer: D — Varactor: reverse-biased junction capacitance varies with voltage
Notes: Varactor = varicap = voltage-variable capacitor. PIN switches RF. Zener regulates voltage. Schottky rectifies at VHF.

## Slide 20
Checkpoint Quiz 4 / 10
A PIN diode in an RF switch circuit is controlled by:
A. RF signal amplitude
B. Reverse bias voltage only
C. Forward DC bias current
D. Gate voltage
Answer: C — PIN diode: RF resistance controlled by forward DC bias current
Notes: Forward bias current changes the width of the I (intrinsic) region, changing RF resistance. This is distinct from a regular diode switch.

## Slide 21
Checkpoint Quiz 5 / 10
What logic family has the lowest static power consumption?
A. TTL
B. ECL
C. CMOS
D. BiCMOS
Answer: C — CMOS draws near-zero static current (only during switching transitions)
Notes: That's why your smoke detector battery lasts for years — the CMOS logic is essentially off when idle.

## Slide 22
Checkpoint Quiz 6 / 10
Comparator hysteresis prevents what problem?
A. Output saturation
B. Oscillation of the oscillator stage
C. Chatter from noise near the switching threshold
D. Thermal runaway
Answer: C — Hysteresis creates two switching thresholds; prevents rapid toggling on noisy inputs
Notes: Without hysteresis: input at exactly the threshold + tiny noise = output flipping hundreds of times per second.

## Slide 23
Checkpoint Quiz 7 / 10
A brass slug inserted into an inductor coil will:
A. Increase inductance
B. Decrease inductance
C. Have no effect
D. Increase Q
Answer: B — Brass is diamagnetic; it slightly opposes the magnetic field and decreases inductance
Notes: Ferrite core → increases inductance. Brass slug → decreases inductance. Common use: fine-tuning coils by screwing a brass slug in or out.

## Slide 24
Checkpoint Quiz 8 / 10
What is the equivalent circuit of a quartz crystal?
A. Parallel LC tank
B. Series RLC only
C. Series RLC in parallel with a capacitor
D. RC low-pass filter
Answer: C — Series RLC (mechanical resonance) in parallel with shunt capacitor (electrode capacitance)
Notes: Two resonances: series (lower freq, low Z) and parallel (higher freq, high Z). Crystal oscillators typically use one or the other.

## Slide 25
Checkpoint Quiz 9 / 10
How is DC power supplied to an MMIC?
A. Through a coupling capacitor on the input
B. Through a separate DC pin
C. Through a resistor or RF choke on the output lead
D. Through the ground plane
Answer: C — DC supplied through output lead via RF choke or resistor; input is left unaffected
Notes: Standard practice: bias T on the output. The RF choke passes DC but blocks RF; the DC feeds the MMIC through the output port.

## Slide 26
Checkpoint Quiz 10 / 10
What does an optoisolator provide between its input and output circuits?
A. Impedance matching
B. Frequency translation
C. Complete galvanic (electrical) isolation
D. Voltage regulation
Answer: C — LED on one side, phototransistor on the other; no electrical connection between them
Notes: Galvanic isolation means no electron can physically cross from one side to the other. The information crosses as light.

## Slide 27
Before Module 5
Your assignment:
Drill HamStudy E6A-E6F to 80%+ confidence
Spend extra time on E6B (diode types) — Zener, Schottky, PIN, varactor are all tested
Core materials (E6D): ferrite vs powdered iron, brass core — these are reliable exam questions
Coming up:
Module 5: Practical Circuits — the hardest module. Amplifier classes, filter responses, SDR/DSP, op-amp gain formulas, oscillator types. 8 exam questions. Budget maximum HamStudy time.
Notes: Wrap up and send students to HamStudy.