## Slide 1
Module 1: License & Rules
FCC Framework · Licensing · Station Operation
2026–2030 Technician Question Pool
TavaOne Education · Pinellas STEM Radio Lab
Notes: Welcome everyone. This is Module 1 of the TavaOne Education Technician License Course. Today we cover the FCC rules — the legal framework for amateur radio. 6 of your 35 exam questions come from this module.

## Slide 2
What We're Building Toward
5 modules × 2 hours = your FCC Technician license
Module 1 (today): License & Rules — the FCC framework
Module 2: Operating & Propagation — how to get on the air
Module 3: Technical Core — the math and components
Module 4: Signals, Antennas & Safety — the hardware
Module 5: Capstone — practice exam + review → VE exam on-site
35 questions on the exam, 26 to pass (74%) — you WILL pass
TavaOne Education — Module 1
Notes: Walk through the 5-module structure. Emphasize: they will pass if they do the work. HamStudy between sessions is what makes the difference.

## Slide 3
The Exam — What to Expect
35 multiple-choice questions, randomly drawn from the question pool
One question from each of 35 groups (T1A through T0C)
26 correct answers to pass = 74%
No trick questions — the answer is always one of the four choices
Most people finish in 15–20 minutes
VE exam right here at the lab — bring photo ID and your FRN
$35 FCC fee is paid online through CORES after VEs submit your application
TavaOne Education — Module 1
Notes: Demystify the exam. Many students are nervous. Point out: 74% means you can miss 9 and still pass. The VEs come to us — no need to go somewhere else.

## Slide 4
Let's Set Up HamStudy
Your #1 study tool between sessions
Notes: Guide everyone through creating their HamStudy account NOW. Don't move on until everyone is set up.

## Slide 5
HamStudy Setup — Do This Now
Go to hamstudy.org on your phone or computer
Create a free account
Select the 2026–2030 Technician question pool
Scan the QR code on your handout (or visit the link) to share progress
Share link: hamstudy.org/share?shareTo=qslujd
This lets your instructor see which sections you're strong and weak on
Between sessions: drill T1A–T1F to 80%+ confidence
TavaOne Education — Module 1
Notes: Walk the room and make sure everyone gets signed up. This is the single most important thing for their success. The progress sharing lets you see who's studying and who's not.

## Slide 6
Part 1: What Is Amateur Radio?
Subelement T1A · 1 exam question from this group
Notes: Transition to the first content section. T1A covers the basis and purpose of the service.

## Slide 7
The Amateur Radio Service
A radiocommunication service — not a product, not a toy, not CB
Regulated by the FCC (Federal Communications Commission)
Purposes defined in FCC Part 97:
→ Advancing skills in technical and communication phases of radio
→ Self-training and technical investigation
→ Emergency communications and public service
→ Building international goodwill
TavaOne Education — Module 1
Notes: Emphasize: amateur radio is a SERVICE defined by law, with specific purposes. It's not commercial, not for entertainment, not for business.

## Slide 8
Key Terms You Need to Know
Harmful interference — seriously degrades or repeatedly interrupts another service
Beacon — a station transmitting for propagation observation (28.200–28.300 MHz on 10m)
RACES — Radio Amateur Civil Emergency Service (requires FCC license AND civil defense certification)
Frequency coordinator — recommended by local amateurs, coordinates repeater frequencies
Willful or malicious interference — the single most explicitly prohibited act in amateur radio
TavaOne Education — Module 1
Notes: These terms come up on the exam as definitions. 'Harmful interference' and 'willful interference' are the ones students mix up — harmful is the standard, willful/malicious is the prohibition.

## Slide 9
The Phonetic Alphabet
Alpha Bravo Charlie Delta Echo Foxtrot Golf
Hotel India Juliet Kilo Lima Mike November
Oscar Papa Quebec Romeo Sierra Tango Uniform
Victor Whiskey X-ray Yankee Zulu
Practice: spell your call sign (or your name) phonetically
You'll use this CONSTANTLY on the air
The FCC encourages (not requires) phonetics on phone
TavaOne Education — Module 1
Notes: Have everyone practice spelling their name. Make it interactive — go around the room. This is a skill they'll use every single time they key the mic.

## Slide 10
Part 2: Frequency Allocations
Subelement T1B · 1 exam question from this group
Notes: Transition to T1B. This is the 'where can I operate' section.

## Slide 11
Technician Band Privileges
VHF / UHF (full privileges)
6 meters: 50.0–54.0 MHz
2 meters: 144.0–148.0 MHz
1.25 meters: 222.0–225.0 MHz
70 cm: 420.0–450.0 MHz
Plus 902 MHz and up
Max power: 1500W PEP
HF (limited privileges)
10 meters only: 28.000–28.500 MHz
CW/digital: 28.000–28.300
Phone/SSB: 28.300–28.500
Max power on 10m: 200W PEP
Can use FT8, CW, SSB, FM
Can contact the ISS on VHF!
TavaOne Education — Module 1
Notes: The band chart is the most-referenced page in the handout. Point to it. Key exam numbers: 146.520 (2m calling), 200W on 10m HF, 1500W above 30 MHz.

## Slide 12
Important Frequency Rules
Don't transmit on the exact edge of a band — sidebands extend beyond
CW-only segments: 50.0–50.1 MHz and 144.0–144.1 MHz
2-meter FM simplex calling frequency: 146.520 MHz — memorize this
Secondary allocations: you must not interfere with the primary user
Technicians CAN use digital modes (FT8) on 10m, 6m, and 2m
Any Technician can contact the International Space Station on VHF
TavaOne Education — Module 1
Notes: 146.520 is the number they need to memorize for the exam AND for real life. It's the national calling frequency. CW-only segments trip people up — below 50.1 and below 144.1.

## Slide 13
Part 3: Licensing
Subelement T1C · 1 exam question from this group
Notes: Transition to the licensing system. This is straightforward but has specific numbers they need to know.

## Slide 14
Three License Classes
Technician — your entry point. Full VHF/UHF + limited 10m HF
General — adds most HF bands. Requires Element 2 + Element 3
Amateur Extra — all frequencies. Requires Elements 2 + 3 + 4
Each upgrade opens more bands — you keep all previous privileges
No Morse code requirement for ANY license class
Vanity call signs available to ANY licensed amateur (not just Extra)
TavaOne Education — Module 1
Notes: Emphasize: no Morse code. This is still the #1 misconception about ham radio. Also: vanity calls are open to everyone — common exam question.

## Slide 15
License Numbers to Know
License term: 10 years
Renewal window: up to 90 days before expiration
Grace period after expiration: 2 years — but you CANNOT transmit
After passing: transmit as soon as your call appears in the FCC ULS database
How you're notified: email from the FCC with a link to download your license
If the FCC can't reach you by email: they can revoke your station license
Keep your email address current in the FCC system!
TavaOne Education — Module 1
Notes: The grace period is a trap question — yes there's a 2-year grace, but NO you can't transmit during it. That catches a lot of students.

## Slide 16
Part 4: What You CAN and CAN'T Do
Subelement T1D · 1 exam question from this group
Notes: This section is about the rules of the road. What's allowed, what's not.

## Slide 17
Transmissions: Allowed vs. Prohibited
PROHIBITED
Broadcasting (transmitting to the general public)
Obscene or indecent language
Music (with narrow exception)
Encryption to hide meaning (mostly)
Business communications for profit
Willful or malicious interference
ALLOWED
Selling amateur equipment (occasionally, not regularly)
One-way: beacons, telecommand, emergencies
Compensation when part of classroom instruction
International comms (unless country objects via ITU)
Test transmissions (but you must still identify)
Emergency communications override most rules
TavaOne Education — Module 1
Notes: The 'broadcasting' definition is an exam favorite: 'transmissions intended for reception by the general public.' Two-way communication between hams is NOT broadcasting.

## Slide 18
The Broadcasting Definition
Broadcasting = transmissions intended for reception by the general public
This is NOT what amateur radio does — we communicate station to station
One-way transmissions that ARE allowed:
→ Beacons (propagation observation)
→ Telecommand of model craft (no ID required for this one!)
→ Emergency communications
→ Brief test transmissions (must still identify)
When in doubt: if it's two-way between licensed operators, it's probably fine
TavaOne Education — Module 1
Notes: The broadcasting question is almost guaranteed on the exam. Make sure they understand the FCC definition — it's about the INTENT to reach the general public, not about one-way vs two-way.

## Slide 19
Part 5: Control Operators
Subelement T1E · 1 exam question from this group
Notes: This is one of the most important concepts. Control operator rules show up frequently on the exam.

## Slide 20
What Is a Control Operator?
The licensed amateur designated by the station licensee
Responsible for all transmissions and FCC compliance
An amateur station may NEVER transmit without a control operator
The station licensee designates who the control operator is
Both the control operator AND the licensee share responsibility
Transmitting privileges = the control operator's license class
A Technician can NEVER be control op in an Extra-only segment
TavaOne Education — Module 1
Notes: The 'never transmit without a control operator' rule is absolute — even repeaters have a control operator (automatic control). Drive this home.

## Slide 21
Control Types
Local control — you're physically at the transmitter
→ Example: sitting at your radio desk
Remote control — you're somewhere else, controlling via a link
→ Example: operating your station over the internet
Automatic control — no operator present, station runs on its own
→ Example: a repeater
The control point = where the control operator function is performed
Any station may be remotely controlled
TavaOne Education — Module 1
Notes: Students confuse remote and automatic. Remote = a human is controlling it from afar. Automatic = no human in the loop (repeater). Both still have a control operator — the repeater trustee.

## Slide 22
Part 6: Station Identification
Subelement T1F · 1 exam question from this group
Notes: Last content section. Station ID rules, repeaters, third-party, club stations, FCC inspection.

## Slide 23
How to Identify Your Station
Identify at least every 10 minutes AND at the end of the communication
Use your FCC-assigned call sign
On phone: identify in English (CW or phone emission)
Tactical call signs are fine — but still give your FCC call every 10 min
Self-assigned indicators: 'stroke,' 'slant,' or 'slash' — all acceptable
You must ID even during test transmissions
Exception: transmitting to control model craft (no ID required)
TavaOne Education — Module 1
Notes: 10 minutes + end. That's the rule. Tactical calls like 'Race Headquarters' or 'Net Control' are supplemental — they don't replace your FCC call.

## Slide 24
Repeaters, Third-Party & Club Stations
Repeater = simultaneously retransmits on a different channel
If a repeater retransmits a violation: the originating station is responsible
Third-party communication = a message on behalf of another person
You can let an unlicensed person talk — but YOU are responsible
With foreign stations: only with third-party agreement countries
Club station license requires at least 4 members
FCC can inspect your station at ANY time — no advance notice
TavaOne Education — Module 1
Notes: The repeater accountability question is common: it's the ORIGINATING station, not the repeater owner. And FCC inspection: at any time upon request, no warrant needed.

## Slide 25
Quick Reference
The numbers that matter
Notes: Quick recap of the key facts before the quiz.

## Slide 26
Key Numbers for the Exam
Rules & Licensing
Regulating agency: FCC
License term: 10 years
Grace period: 2 years (no TX!)
Renewal window: 90 days before
Station ID: every 10 min + end
ID language on phone: English
Club station: minimum 4 members
Frequencies & Power
2m calling freq: 146.520 MHz
Tech max power (VHF+): 1500W PEP
Tech max power (10m HF): 200W PEP
CW-only: below 50.1, below 144.1
Beacons on 10m: 28.200–28.300
Control operator: ALWAYS required
Vanity calls: ANY licensed amateur
TavaOne Education — Module 1
Notes: Run through these quickly. These are the 'free points' — pure memorization, no concepts to understand. If they know these cold, that's 6 easy questions on the exam.

## Slide 27
Checkpoint Quiz
10 questions from the T1 question pool
Notes: Time for the quiz. Do it as a group — show each question, let them think, then discuss the answer.

## Slide 28
Checkpoint Quiz
Q1
Which of the following is part of the Basis and Purpose of the Amateur Radio Service?
A. Providing personal radio communications for as many citizens as possible
B. Providing communications for international contesting
C. Advancing skills in the technical and communication phases of the radio art
D. All these choices are correct
Notes: Answer: C. The key phrase is 'advancing skills in the technical and communication phases.' This comes directly from Part 97.1.

## Slide 29
Checkpoint Quiz
Q2
Which agency regulates and enforces the rules for the Amateur Radio Service?
A. ARRL
B. Homeland Security
C. The FCC
D. All these choices are correct
Notes: Answer: C. The FCC. ARRL is a membership organization, not a regulatory body.

## Slide 30
Checkpoint Quiz
Q3
Which frequency ranges are available for phone operation by Technician licensees?
A. 28.050 MHz to 28.150 MHz
B. 28.100 MHz to 28.300 MHz
C. 28.300 MHz to 28.500 MHz
D. 28.500 MHz to 28.600 MHz
Notes: Answer: C. Phone starts at 28.300. Below that is CW and digital. Above 28.500 is out of the Tech allocation.

## Slide 31
Checkpoint Quiz
Q4
What is the normal term for an FCC-issued amateur radio license?
A. Five years
B. Eight years
C. Ten years
D. Life
Notes: Answer: C. Ten years. Renewable up to 90 days before expiration.

## Slide 32
Checkpoint Quiz
Q5
Which of the following is prohibited?
A. International communications on VHF
B. Willful or malicious interference
C. Third-party traffic using digital modes
D. All these choices are correct
Notes: Answer: B. Willful or malicious interference is the most explicitly prohibited act. The others are allowed.

## Slide 33
Checkpoint Quiz
Q6
When may an amateur station transmit without a control operator?
A. When using automatic control
B. When the licensee is away and another amateur is using the station
C. When the station is an auxiliary station
D. Never
Notes: Answer: D. NEVER. Even automatic control (repeaters) has a designated control operator.

## Slide 34
Checkpoint Quiz
Q7
How often must you identify with your FCC-assigned call sign?
A. At the beginning of each contact and every 10 minutes
B. At least once during each transmission
C. Every 15 minutes and at the end
D. Every 10 minutes during and at the end of a communication
Notes: Answer: D. Every 10 minutes during AND at the end. Not the beginning — that's a common trap.

## Slide 35
Checkpoint Quiz
Q8
What determines the transmitting frequency privileges of an amateur station?
A. The frequency coordinator
B. The frequencies printed on the license
C. The highest class on the premises
D. The class of the control operator
Notes: Answer: D. The control operator's license class. Not the station licensee's, not whoever else is in the room.

## Slide 36
Checkpoint Quiz
Q9
What is the grace period for renewal if an amateur license expires?
A. Two years
B. Three years
C. Five years
D. Ten years
Notes: Answer: A. Two years. But remember — you CANNOT transmit during the grace period.

## Slide 37
Checkpoint Quiz
Q10
How does the FCC define broadcasting for the Amateur Radio Service?
A. Two-way transmissions by amateur stations
B. Any transmission made by the licensed station
C. Transmissions directed only to amateur operators
D. Transmissions intended for reception by the general public
Notes: Answer: D. Broadcasting = intended for the general public. Normal amateur radio is station-to-station, not broadcasting.

## Slide 38
Before Next Session
Your assignment for Module 2
Notes: Wrap up. Give the HamStudy assignment and preview what's coming.

## Slide 39
Your Assignment
Drill HamStudy sections T1A through T1F
Target: 80%+ confidence on each section
HamStudy tracks what you're getting wrong and drills those harder
Trust the system — it works
Coming in Module 2: Operating & Propagation
→ How to actually use a repeater
→ CTCSS tones, DMR, Q signals
→ How radio waves travel and propagation modes
→ Station setup and controls
See you next session!
TavaOne Education — Module 1
Notes: Remind them: the exam pass rate correlates directly with HamStudy drilling. Students who do the homework pass. Students who don't, struggle.