## Slide 1
TavaOne Education
General License Course · 2023–2027 Pool
Module 3
Equipment, Practices
& Electronics
General License Course · G4 + G5 + G6 · 10 Exam Questions
Notes: Module 3 is the heaviest content module: G4 (Amateur Radio Practices, 5 Qs), G5 (Electrical Principles, 3 Qs), G6 (Circuit Components, 2 Qs) = 10 of 35 exam questions = 29%. Also the most practically useful for operating.

## Slide 2
Hour 1
Station Equipment and Practices
Notes: G4A covers transceiver controls, TR sequencing, VOX, speech processing. G4B covers test equipment. G4C covers RFI.

## Slide 3
G4A — Transceiver Controls You Need to Know
RF Gain: controls the sensitivity of the receiver front end — turn it down to reduce overload from strong signals or high noise
AF Gain: volume control — adjusts audio output level only
Squelch: mutes audio when no signal present — rarely used on HF (too much noise), standard on VHF FM
Noise Blanker (NB): removes impulse noise (ignition noise, power line hash) by detecting brief high-amplitude pulses and blanking the receiver
Notch Filter: eliminates a specific interfering carrier — tune the notch to the exact frequency of the interferer
Passband Tuning (PBT): shifts the IF passband to move interference out of the audio; different from notch
VOX: voice-operated transmit; microphone audio triggers PTT automatically; set the threshold carefully
Speech Processor: increases average power by compressing audio peaks — sounds louder to the other station
Notes: G4A has 5 exam questions. All of these controls appear in exam questions. Key confusions: RF Gain (front end sensitivity) vs. AF Gain (volume). Noise blanker (impulse noise) vs. notch filter (single carrier). Know what each does.

## Slide 4
G4A — TR Sequencing and External Amplifiers
External linear amplifier: amplifies the transceiver's output, typically 100W → 500W–1500W
Problem: if you key the amplifier before the transceiver switches from receive to transmit, you hot-switch the PA
TR Sequencing: the order in which the system switches from receive to transmit
Correct sequence: 1) PTT pressed → 2) transceiver goes to transmit mode → 3) relay switches → 4) amplifier is keyed
Built-in delay circuits (or separate sequencers) handle this; most modern transceivers have a key delay setting
Hot-switching the PA can destroy expensive amplifier tubes or transistors
CW: semi-breakin (QSK semi) vs. full breakin (QSK) — full breakin hears between dit spaces, slow CW only
VOX delay: prevents the radio from dropping out between words; too short = choppy, too long = can't receive replies promptly
Notes: TR sequencing is an exam topic in G4A. The concept: key the transceiver first, then the amplifier — never the reverse. Real-world context: any ham running a linear amp needs to understand this to avoid expensive failures.

## Slide 5
G4B — Test Equipment
Oscilloscope: displays voltage waveforms vs. time; use to check modulation, look for key clicks, check power supply ripple
Directional Wattmeter (SWR meter): measures forward and reflected power; placed in the feed line between transceiver and antenna
Dummy Load: 50-ohm resistive load (no radiation); use when testing or tuning to avoid transmitting on the air unnecessarily
Antenna Analyzer: measures feed-point impedance, SWR, resonant frequency; invaluable for antenna work
Frequency Counter: measures transmitted frequency precisely; useful for VFO calibration
Signal Generator: creates a test signal at a known frequency and level; use to test receiver sensitivity
Multimeter (DMM): measures DC voltage, current, resistance, continuity; essential for troubleshooting
Spectrum Analyzer: displays power vs. frequency; shows harmonics, spurious emissions (expensive)
Notes: G4B test equipment questions are often about which instrument measures which thing. Key: oscilloscope = waveform/time; wattmeter = power; dummy load = no radiation during testing; antenna analyzer = impedance and SWR. Spectrum analyzer would show harmonics.

## Slide 6
G4C — RF Interference and Remedies
Common-mode current on coax shield: RF flows back along the outside of the coax into the shack, gets into audio equipment
Solution: choke balun (ferrite core) at the antenna feedpoint; snap-on ferrites on cables
TVI (television interference): usually harmonics from the transmitter; most TVs have improved rejection but still possible
Audio equipment interference: RF gets rectified by op-amp input diodes and appears as audio distortion
Fix for audio interference: ferrite choke on the microphone cable at the radio; snap-on cores work well
Telephone interference: RF on phone lines; ferrite chokes at the phone handset
BCI (broadcast interference to your receiver): a strong AM station mixing in your receiver front end
Your responsibility: you must not cause harmful interference to other services; neighbors' interference is often also your issue to resolve
Notes: G4C RFI questions focus on identifying the cause and the remedy. Ferrite chokes are the answer to most common-mode and audio interference problems. The exam may ask: what should you do if your transmission causes interference to a neighbor's stereo? Answer: investigate and correct it.

## Slide 7
G4D — SSB Microphone Technique and Dynamic Range
SSB mic technique: speak across the mic, not into it; keep distance consistent; avoid breathing directly at the mic
Audio compression: speech processor compresses dynamic range → higher average power → louder on the other end (but sounds more compressed)
Receiver dynamic range: ability to receive a weak signal in the presence of a strong one on a nearby frequency
Intermodulation distortion (IMD): two strong signals mixing in the receiver front-end create a third (unwanted) signal
IMD products: f = n×f1 ± m×f2; third-order products (2f1−f2) fall close to the original signals and are the most problematic
Desensitization: very strong signal overloads the front end, reducing sensitivity to weaker signals
Solution to IMD/desens: reduce RF gain, add attenuation, use a bandpass filter before the receiver
Mobile HF noise: alternator whine (RPM-correlated), ignition noise (pops); fix with ferrite chokes, ground straps, noise filter on power leads
Notes: IMD and dynamic range questions appear in G4. The practical understanding: a strong signal nearby can cause problems in your receiver that make it seem like there are extra signals present. The solution is always to reduce the received signal level somehow — ferrite chokes, attenuation, or good shielding.

## Slide 8
Hour 2
Electronics: Reactance, Components, and Circuits
Notes: G5 (Electrical Principles) and G6 (Circuit Components) — the math and the parts. 5 exam questions total.

## Slide 9
G5A — Impedance and Reactance
Impedance (Z): total opposition to AC current flow = combination of resistance (R) and reactance (X)
Reactance: opposition to current caused by capacitors or inductors; changes with frequency
Capacitive reactance: Xc = 1/(2πfC) — as frequency INCREASES, Xc DECREASES; capacitor acts like a short at high frequency
Inductive reactance: XL = 2πfL — as frequency INCREASES, XL INCREASES; inductor acts like an open at high frequency
At resonance: XL = Xc; net reactance = 0; impedance = purely resistive
Series resonance: impedance is MINIMUM at resonance (Z = R only)
Parallel resonance: impedance is MAXIMUM at resonance (very high Z at resonant frequency)
50 ohms: why all amateur radio gear is 50 ohms — it's a compromise between minimum loss and maximum power transfer in coax
Notes: G5A reactance formulas are tested. Students need to know the direction of change: capacitive reactance goes DOWN with frequency; inductive reactance goes UP. These can be confused under pressure. Quick memory aid: capacitors block DC, pass AC (high freq) → Xc decreases with frequency.

## Slide 10
G5B and G5C — Circuit Calculations
Power factor: ratio of real power (watts) to apparent power (VA); PF = cos(phase angle); unity PF = purely resistive
Series resistors: R_total = R1 + R2 + ... (just add them)
Parallel resistors: 1/R_total = 1/R1 + 1/R2 + ...; two equal resistors: half the value
Series capacitors: 1/C_total = 1/C1 + 1/C2 (like parallel resistors — they get smaller)
Parallel capacitors: C_total = C1 + C2 (just add them)
Series inductors: L_total = L1 + L2 (just add them)
Parallel inductors: 1/L_total = 1/L1 + 1/L2 (like parallel resistors)
Transformer turns ratio: Vs/Vp = Ns/Np; impedance ratio = (turns ratio)²; 2:1 turns = 4:1 impedance
Notes: The circuit calculation rules can be confusing because capacitors and resistors behave oppositely in series vs. parallel. Quick memory: for capacitors, series = small (like parallel resistors), parallel = large. For inductors, series = large, parallel = small. Transformer impedance ratio is the square of the turns ratio — this appears on the exam.

## Slide 11
G6A & G6B — Semiconductor Components
Diodes
Rectifier diode: allows current in one direction only; converts AC to pulsating DC
Zener diode: operates in reverse breakdown at a specific voltage; used for voltage regulation
Varactor diode: capacitance varies with reverse voltage; used in VFOs and PLLs for electronic tuning
LED: light-emitting diode; emits photons when forward biased
Transistors and ICs
NPN bipolar: base current controls collector-emitter current; current flows collector to emitter when base is +
PNP bipolar: opposite polarity; less common in RF work
MOSFET: voltage at gate controls drain-source current; very high input impedance; common in RF amplifiers
Op-amp: differential input, very high gain; use feedback to set closed-loop gain
Crystal: piezoelectric resonator; extremely stable frequency; used in oscillators and filters
Notes: G6 is only 2 exam questions. The most likely: varactor diode (what it does), Zener diode (what it does), MOSFET advantage (high input impedance). Crystals are tested for their stability property.

## Slide 12
G6B — The Phase-Locked Loop (PLL)
PLL: Phase-Locked Loop — the heart of every modern synthesized transceiver
Purpose: generate a precise, stable frequency by comparing a divided VCO output to a crystal reference
How it works: VCO → frequency divider → phase detector → low-pass filter → back to VCO control voltage
The VCO (voltage-controlled oscillator) changes frequency until its divided-down output matches the reference crystal
Change the division ratio → change the output frequency → this is how digital tuning works
PLLs are fast (frequency changes in microseconds) and stable (locked to the crystal)
Phase noise: a PLL's limitation — the output isn't perfectly clean; sidebands appear near the carrier
Practical: every time you tune your Icom or Yaesu, the PLL is setting the new frequency
Notes: The PLL is tested in G6 and shows up in G7 (receivers). The exam-level understanding: PLL generates stable frequencies by locking a VCO to a crystal reference. Students don't need to design one, just understand the purpose and basic operation.

## Slide 13
Checkpoint Quiz
What is the purpose of a noise blanker in a receiver?
A. To reduce or eliminate pulse-type interference such as ignition noise
B. To reduce random static from atmospheric noise
C. To eliminate a specific interfering carrier signal
D. To increase receiver sensitivity by reducing the noise floor
Notes: Answer: A Noise blanker = impulse noise (ignition, power lines). Random static = nothing helps much. Eliminating a carrier = notch filter. Receiver sensitivity = not what NB does — NB actually temporarily blanks the receiver, which can reduce sensitivity slightly.

## Slide 14
Checkpoint Quiz
What is the relationship between capacitive reactance and frequency?
A. Capacitive reactance decreases as frequency increases
B. Capacitive reactance increases as frequency increases
C. Capacitive reactance is constant regardless of frequency
D. Capacitive reactance equals inductive reactance at all frequencies
Notes: Answer: A Xc = 1/(2πfC). As f goes up, Xc goes down. This is the opposite of inductive reactance (XL = 2πfL, which increases with frequency). A capacitor passes high frequencies and blocks low frequencies.

## Slide 15
Checkpoint Quiz
What type of diode is commonly used for electronic tuning in receivers and transmitters?
A. Varactor diode
B. Zener diode
C. Schottky diode
D. Rectifier diode
Notes: Answer: A Varactor diode: its capacitance varies with applied reverse voltage. Voltage-variable capacitor. Used in VFOs and PLL circuits for electronic frequency tuning. The more reverse voltage, the less capacitance.

## Slide 16
Checkpoint Quiz
Two resistors of 10 ohms each are connected in parallel. What is the total resistance?
A. 5 ohms
B. 20 ohms
C. 10 ohms
D. 0.5 ohms
Notes: Answer: A Two equal resistors in parallel = half the value. 10/2 = 5 ohms. Or use the formula: 1/R_total = 1/10 + 1/10 = 2/10, so R_total = 10/2 = 5 ohms.

## Slide 17
Checkpoint Quiz
What is the function of a speech processor in an SSB transmitter?
A. To increase average power by reducing the peak-to-average ratio of the voice signal
B. To improve audio quality by filtering unwanted frequencies
C. To increase transmitter bandwidth for clearer audio
D. To reduce microphone sensitivity to prevent distortion
Notes: Answer: A Speech processing (compression) reduces the dynamic range of the audio — it makes quiet parts louder and limits peaks. The result is higher average power without exceeding the transmitter's peak power capability. The other station hears a louder signal. Trade-off: audio sounds more "processed" or dense.

## Slide 18
HamStudy Assignment
Drill these sections before next module:
G4A — Station Operation & Controls
G4B — Test Equipment
G4C — RF Interference
G4D — SSB & Dynamic Range
G4E — Mobile & Field Ops
G5A — Impedance & Reactance
G5B/C — Circuit Calculations
G6A — Diodes
G6B — Transistors & PLLs
hamstudy.org · scan to join our study group
Notes: G4 is the biggest G-subelement with 5 exam questions. Prioritize: transceiver controls (what each does), test equipment (what each measures), and RF interference remedies. G5 reactance direction (Xc down, XL up with frequency) is high-priority.