## Slide 1
TavaOne Education
General License Course · 2023–2027 Pool
Module 4
Signals, Emissions
& Practical Circuits
General License Course · G7 + G8 · 6 Exam Questions
Notes: Module 4 covers G7 (Practical Circuits, 3 Qs) and G8 (Signals and Emissions, 3 Qs) = 6 of 35 exam questions = 17%. Practical circuits includes power supplies, amplifiers, and receivers. Signals covers modulation, digital modes, and emission designators.

## Slide 2
Hour 1
Practical Circuits: Power, Amplifiers, Receivers
Notes: G7 covers power supply fundamentals, amplifier classes, and receiver architecture. Foundational knowledge for understanding how transceivers work.

## Slide 3
G7A — Power Supplies
Transformer: steps AC voltage up or down; provides isolation from the power line (safety)
Rectifier: converts AC to pulsating DC; common types: half-wave (wastes half), full-wave (center tap), full-wave bridge (most common)
Filter capacitor: smooths pulsating DC to ripple DC; larger capacitor = less ripple
Ripple frequency: for full-wave rectifier on 60 Hz AC → ripple = 120 Hz (twice the input frequency)
Voltage regulator: maintains constant output despite load or line changes; IC regulators (7805 = 5V, 7812 = 12V, etc.)
Switching power supply: chops DC at high frequency for efficiency; compact and efficient; can cause RFI
Linear supply: wasteful (drops excess voltage as heat) but very clean RF-wise
Battery types: lead-acid (flooded, AGM, gel), lithium iron phosphate (LiFePO4); charging requirements differ
Notes: G7A power supply questions focus on ripple frequency (120 Hz for full-wave), and the function of each stage (transform → rectify → filter → regulate). The ripple frequency = 2× line frequency for full-wave is a high-probability exam question.

## Slide 4
G7B — Amplifier Classes
Linear Classes (for SSB)
Class A: always conducting; output follows input; low distortion; ~25-30% efficient
Class AB: conducts slightly more than half cycle; good linearity; 50-70% efficient; most SSB finals use this
Both A and AB required for SSB — you need linear amplification to preserve the sideband's information
Non-Linear Classes (CW/FM)
Class B: conducts exactly half cycle; more efficient than A (~75%)
Class C: conducts less than half cycle; ~80% efficient; highly non-linear; only for CW or FM where distortion doesn't matter
Class D/E: switching amplifiers; very high efficiency; emerging in ham radio
Class C on SSB = terrible distortion = splatter = causing interference to adjacent channels
Notes: Amplifier class is tested in G7B. Key facts: Class A and AB = linear = OK for SSB; Class C = non-linear = only CW or FM. The efficiency vs. linearity trade-off is the concept. Why not Class C for SSB? Because the non-linearity creates sideband distortion.

## Slide 5
G7B — Negative Feedback in Amplifiers
Negative feedback: take a fraction of the output, invert it, add it back to the input
Effect: the amplifier "corrects" itself → less distortion → more linear response
Trade-off: gain is reduced by the feedback amount (if you feed back 10%, gain drops ~10×)
Benefits: more stable gain over temperature and frequency; lower output impedance; wider bandwidth
Op-amps run with massive negative feedback (open-loop gain = 100,000, closed-loop = whatever you set with resistors)
Oscillators: use POSITIVE feedback → signal grows until limited; the feedback must be in-phase
The difference: negative feedback stabilizes; positive feedback creates oscillation
Audio amplifiers in transceivers always use negative feedback for low distortion
Notes: Negative feedback is tested conceptually: reduces gain, reduces distortion, improves stability. This is a foundational electronics concept. The G8 exam questions sometimes touch on feedback in the context of oscillators vs. amplifiers.

## Slide 6
G7C — The Superheterodyne Receiver
Superheterodyne (superhet): the architecture used in virtually all HF receivers since the 1920s
Signal path: Antenna → RF stage → Mixer → IF amplifier → Detector → Audio amplifier → Speaker
Mixer: combines the incoming RF with a local oscillator (LO) signal; produces sum and difference frequencies
IF (Intermediate Frequency): a fixed frequency (455 kHz common for AM; 10.7 MHz for FM; 8.215 MHz for SSB); filtering happens here
Why convert to IF? A fixed-frequency filter is much easier to make sharp and stable than a tunable one
BFO (Beat Frequency Oscillator): injects a carrier to heterodyne against the IF; required for SSB and CW demodulation
AGC (Automatic Gain Control): maintains constant audio level as signal strength varies; samples IF level
SDR: Software Defined Radio — ADC digitizes the signal early in the chain; everything else done in software
Notes: The superhet architecture is tested. Students need to know the signal flow and what each stage does. Key testable facts: why do we need an IF? (easier to filter). What does the BFO do? (demodulate SSB/CW). What does AGC do? (level control).

## Slide 7
Hour 2
Signals and Emissions
Notes: G8 covers modulation modes (AM, SSB, FM), emission designators, and digital modes. 3 exam questions.

## Slide 8
G8A — Modulation Modes Compared
AM (Double-sideband AM): carrier + two sidebands; carrier wastes 2/3 of transmitter power
SSB (Single Sideband, suppressed carrier): one sideband, no carrier; most efficient; ~3 kHz bandwidth
FM (Frequency Modulation): frequency varies with audio; constant amplitude (no amplitude fading); ~15 kHz for VHF
Emission designators: J3E = SSB phone (the J means suppressed carrier, 3 = phone, E = telephony)
A3E = AM double sideband; F3E = FM phone; G3E = PM phone; F1B = RTTY; J2B = PSK
Bandwidth comparison: CW (~200 Hz) < PSK31 (~80 Hz, narrower!) < SSB (~3 kHz) < AM (~6 kHz) < FM (~15 kHz)
Why SSB for HF? Efficient power use, narrow bandwidth, punches through noise better than AM
Why FM for VHF/UHF? Noise immunity (capture effect), simple receivers, FM-only repeaters
Notes: Emission designators are tested in G8. J3E (SSB) is the one most students need to know. The bandwidth comparison is also testable — remember PSK31 is actually narrower than CW in many implementations. The overall order: CW < SSB < AM < FM.

## Slide 9
G8B — FM Deviation and Modulation
FM deviation: how far the carrier swings above and below center frequency in response to audio
Amateur VHF FM: ±5 kHz maximum deviation (so channel width = 2×5 = 10 kHz around center)
Modulation index (FM): ratio of frequency deviation to modulating frequency; index = Δf / fm
Deviation ratio: ratio of MAXIMUM deviation to MAXIMUM modulating frequency
Overdeviation: audio too loud → exceeds ±5 kHz → adjacent channel interference; "wideband" sounds of over-deviated stations
Capture effect: FM receiver "captures" the stronger of two co-channel signals; suppresses the weaker; why FM is good in mobile use
Intermodulation products: f_IM = n×f1 ± m×f2; third-order (2f1−f2) fall close in — receiver problem
Carson's rule: approximate FM bandwidth = 2 × (max deviation + max modulating freq)
Notes: FM deviation is testable. Know: ±5 kHz max deviation for VHF amateur FM. Capture effect is a G8 question — FM captures the strongest signal. Intermodulation in the context of G8 is more about receiver IMD than transmitter distortion.

## Slide 10
G8C — Digital Modes
RTTY (Radio Teletype): two frequencies (mark and space), 170 Hz shift standard, 45.45 baud; uses LSB with AFSK
PSK31: phase-shift keying; 31.25 baud; ~80 Hz bandwidth; keyboard-to-keyboard; uses LSB with AFSK
PSK31 note: dial frequency ≠ RF frequency; add audio tone (~1500 Hz) to dial to get actual RF
FT8: 15-second transmit/receive cycles; computer clock must be within ±1 second of UTC; 4-tone GFSK; ~50 Hz wide
FT8 uses: WSJT-X software; exchanges grid squares and signal reports; fully automated QSO
MFSK: multi-frequency shift keying; multiple tones for higher throughput; more robust than 2-tone FSK
Winlink: email over radio; HF gateways; uses PACTOR or Ardop; addressed as regular email
APRS: 1200 baud on VHF (144.39 MHz); position, messaging, weather; uses AX.25 protocol
Notes: G8C digital mode questions focus on operating characteristics. FT8's clock requirement (±1 second) is a testable fact. PSK31's dial-vs-actual-RF distinction is also tested. RTTY's 170 Hz shift is a specific fact that shows up in questions.

## Slide 11
Checkpoint Quiz
What is the ripple frequency output of a full-wave rectifier connected to a 60 Hz AC source?
A. 120 Hz
B. 60 Hz
C. 240 Hz
D. 30 Hz
Notes: Answer: A Full-wave rectifier processes both the positive and negative halves of the AC cycle. 60 Hz input × 2 = 120 Hz ripple. The filter capacitor must filter at 120 Hz. Half-wave rectifier would produce 60 Hz ripple (one half of each cycle).

## Slide 12
Checkpoint Quiz
Which amplifier class is most suitable for use in the final stage of a single-sideband transmitter?
A. Class AB
B. Class A
C. Class C
D. Class D
Notes: Answer: A Class AB is the preferred choice for SSB finals. It's linear enough to preserve the SSB signal's integrity (unlike Class C) while being more efficient than Class A. Class C is non-linear and suitable only for CW or FM. Class A is linear but too inefficient for high-power finals.

## Slide 13
Checkpoint Quiz
What term describes the ability of an FM receiver to suppress the weaker of two co-channel signals?
A. Capture effect
B. Quieting effect
C. Desensitization
D. Adjacent channel rejection
Notes: Answer: A Capture effect: FM receiver locks onto the stronger of two signals on the same frequency and suppresses the weaker one. This is both a feature (works well in mobile use, ignores weak interferers) and a limitation (you might not hear a weaker station at all).

## Slide 14
Checkpoint Quiz
What is the emission designator for a single-sideband phone signal with a suppressed carrier?
A. J3E
B. A3E
C. F3E
D. G3E
Notes: Answer: A J3E: J = single sideband with suppressed carrier; 3 = analog voice (telephony); E = telephony. A3E = AM double sideband (A = double sideband full carrier). F3E = FM phone. G3E = PM phone. The J designator for SSB is the most frequently tested emission designator.

## Slide 15
Checkpoint Quiz
What function does a Beat Frequency Oscillator (BFO) serve in a receiver?
A. It generates a carrier to heterodyne with the IF signal for SSB and CW demodulation
B. It stabilizes the local oscillator frequency
C. It provides automatic gain control for the IF stage
D. It converts the detected audio to a digital signal
Notes: Answer: A BFO injects a carrier into the detector stage to mix with the SSB or CW signal. The detected audio is the beat frequency between the BFO and the signal. Without the BFO, SSB sounds like Donald Duck and CW sounds like silence.

## Slide 16
HamStudy Assignment
Drill these sections before next module:
G7A — Power Supplies
G7B — Amplifiers & Oscillators
G7C — Receivers & Transmitters
G8A — Modulation Modes
G8B — FM & Modulation
G8C — Digital Modes
hamstudy.org · scan to join our study group
Notes: G7 and G8 together = 17% of the exam. High-priority: 120 Hz ripple (full-wave rectifier), amplifier classes (A/AB = linear for SSB; C = FM/CW only), J3E emission designator, capture effect in FM, FT8 clock requirement.